## Slide 1: Application of Sentinel-2A/B satellites to retrieve turbidity in the Guadalquivir estuary (Southern Spain)
Masuma Chowdhury
Cesar Vilas
Stef VanBergeijk
Gabriel Navarro
Irene Laiz
Isabel Caballero de Frutos
Sentinel-2
Date: 28th December, 2019
CC BY 4.0 License

## Slide 2
  A glance at the Guadalquivir River and Sentinel-2 satellites
  In-situ Data and Sampling stations
  ACOLITE atmospheric correction analysis
  Spectral feature analysis from low to high turbidity levels
  Turbidity models calibration & validation
  Conclusions
  Contact details
  Acknowledgement
Table
of content
vEGU General Assembly 2021: Gather Online, 19-30 April 2021

## Slide 3
  The major watercourse located in the Southwest Spain, crosses the whole region of Andalusia and ends into the Gulf of Cadiz, in the Atlantic Ocean.
  Main source of freshwater inputs and nutrients to the estuary & the adjacent Gulf of Cadiz shelf, thereby regulating the high biological productivity of the basin.
  Occasionally experiences high discharge episodes laden with high sediment concentrations, resulting in negative effects on water quality and clarity, productivity of the aquatic ecosystems, as well as human consumption, recreation and manufacturing.
  Several prolonged turbid episodes originated hypoxia and inhibition of phytoplankton growth in the adjacent coastal region are endeavoring the policy-managers & stakeholders.
  Therefore, examining the turbidity level is required to assist the challenging coastal management & water quality monitoring.
Source: Google
Source: Navarro et al., (2012); Losada et al., (2017); Caballero et al., (2018); & Denizli et al., (2018)
The Guadalquivir River at a glance.....

## Slide 4
Copernicus Sentinel-2A/B at a glance.....
  Two polar orbiting identical satellites
  High spatial resolution at 10m, 20m & 60m.
  High revist time (5 days at equator)
Source: Sentinel2_infographic
  Highly prominsing for coastal and inland water quality monitoring

## Slide 5
Study period: Nov 2017 to Present time
Satellite data: Sentinel-2A/B
In-situ data: Instituto de Investigacion y Formacion Agraria y
Pesquera (IFAPA)
Sampling area: → Tarfia
          → Bonanza
          → Transit between Tarfia and Bonanza
Data
vEGU General Assembly 2021: Gather Online, 19-30 April 2021
Model calibration: Nov 2017 to Oct 2020
Model validation: Nov 2020 to present time

## Slide 6
Tarfia
Bonanza
Field Survey & Sampling Stations

## Slide 7
ACOLITE atmospheric correction analysis
RGB composites from Sentinel-2 image covering Guadalquivir River estuary (Spain) (Fig. A-C). Surface reflectance at TOA level (Fig. A), atmospheric correction using standard DSF without glint (Fig B) and with glint (Fig. C) correction. Fig. D-H represent the reflectance band at the wavelength of 665, 704, 740, 783 and 865 nm respectively with DSF + glint correction.
Spectra extracted from the above Fig A-C. Fig I represents spectra before (TOA) and after (BOA with DSF + Glint) atmospheric correction. Fig. J & K represent a zoom in the atmospherically corrected spectra at the BOA level without glint and with glint correction respectively.
P1
P2
P4
P3
vEGU General Assembly 2021: Gather Online, 19-30 April 2021
I
J
K

## Slide 8
Spectral
features
√ Offshore clear water region √ Low levels of turbidity
√ Medium levels of turbidity √ High levels of turbidity
vEGU General Assembly 2021: Gather Online, 19-30 April 2021

## Slide 9
Turbidity
models
vEGU General Assembly 2021: Gather Online, 19-30 April 2021

## Slide 10
Turbidity algorithm_Rrs_740
vEGU General Assembly 2021: Gather Online, 19-30 April 2021
B

## Slide 11
Turbidity algorithm_Rrs_740
vEGU General Assembly 2021: Gather Online, 19-30 April 2021
B

## Slide 12
Validation processing is ongoing..
Next validation field campaign will be carried out on mid May, 2021
Validation
vEGU General Assembly 2021: Gather Online, 19-30 April 2021

## Slide 13
The atmospheric correction assessment of this study suggests that ACOLITE DSF along with ‘Glint’ correction is more reliable than without ‘Glint’ correction, especially for this study region where sun glint is a major problem during summertime, affecting most of the Sentinel-2 satellite scenes.
So far, among the four turbidity algorithms, the Rrs 740 nm algorithm is the best suited one, however, we need to wait until our next field campign in oder to validate this algorithm.
This algorithm will be a key to understand the turbidity level in the Guadalquivir river & therefore, will support the scientists, policy makers and the statkeholders for ensuring sustainable coastal management of the estuary, its adjacent coastal areas and its resources.
Conclusions
vEGU General Assembly 2021: Gather Online, 19-30 April 2021

## Slide 14
  Masuma Chowdhury - masuma.chowdhury@alum.uca.es
  César Vilas - cesar.vilas@juntadeandalucia.es
  Stef VanBergeijk - stefaniea@juntadeandalucia.es
  Gabriel Navarro - gabriel.navarro@icman.csic.es
  Irene Laiz - irene.laiz@uca.es
  Isabel Caballero - isabel.caballero@icman.csic.es
Contact
Details
vEGU General Assembly 2021: Gather Online, 19-30 April 2021

## Slide 15
Acknowledgements
vEGU General Assembly 2021: Gather Online, 19-30 April 2021
This study has been done as an internship work for the Erasmus Mundus Joint Masters Degree on Water and Coastal Managemet (WACOMA Project586596-EPP-1-2017-1-IT-EPPKA1-JMD-MOB), in association with ICMAN-CSIC (Sen2Coast Project: RTI2018-098784-J-100) and IFAPA (Research Project PP.FEM.PPA201700.5) under the umbrella of ‘Blue Growth Associate Unit CSIC-IFAPA.

## Slide 16
Thank You
vEGU General Assembly 2021: Gather Online, 19-30 April 2021