## Slide 1: Nowcasting for urban flash floods in Africa: a machine-learning and satellite-observation based model
Trained on 13-year radar data for the Netherlands:
TrajGRU better than Pysteps-SPROG (Optical Flow) for:
higher intensities
longer lead times
MSc thesis Eva van der Kooij (HKV, KNMI, TU Delft)
Dorien Lugt1, Mattijn van Hoek1, Jan Fokke Meirink2, Eva van der Kooij1,3
HKV 2. KNMI 3. TU Delft
Contact: lugt@hkv.nl
Many African cities face frequent flash floods due to
rapid urbanization with poor drainage, and
high intensity convective rainfall.
Early warning is effective for risk reduction,
but small latency, high spatial and temporal resolution are required.
Meteosat Second Generation (MSG) – SEVIRI
for Africa and Europa
at 45 min. latency
at 15 min. frequency
at 3x3km spatial resolution (at nadir)
Retrieval: Nighttime Precipitation Estimation (Brasjen, A.M., et al., 2014).
Nowcasting rainfall (0-3 hours):
Traditional: Optical Flow
ML: TrajGRU (Shi et al., 2017)
Trained on 1-year dataset for Ghana:
Next steps:
Train TrajGRU on larger MSG-SEVIRI dataset
Compare PySTEPS with TrajGRU in Ghana
Evaluate the use of nowcasts in Early Warning Systems
observation
TrajGRU
SPROG
Available for free on rainsat.net and appstore:
Notes: Rivers, coasts and deltas enable prosperity and development, but are often also vulnerable due to flooding. Management strategies like Room for the River, Building with Nature or construction of flood defences
like dykes and storm surge barriers help to reduce the flood risk. Our experts ensure that proposed plans meet desired objectives. To this end, we offer extensive knowledge of hydraulics and morphology.