## Slide 1
E.G. Mamagiannou et al.
Software: GeoGravGOCE
GeoGravGOCE: A GOCE SGG processing software for datum
transformations and filtering
Software
E.G. Mamagiannou, E.A. Pitenis, D.A. Natsiopoulos, G.S. Vergos, I.N. Tziavos
GravLab – Laboratory of Gravity Field Research and Applications, DGS, AUTH, Greece
European Geosciences Union GA 2021
Session G1.5
Vienna, Austria
April 29, 2021

## Slide 2
Outline
E.G. Mamagiannou et al.
Software: GeoGravGOCE
Software description
SGG Pre-processing tab
GGM Transformation tab
Filtering tab
Reference Systems Transformation tab
GUI efficiency
Conclusions
References
Acknowledgements

## Slide 3
Software description
Software: GeoGravGOCE
E.G. Mamagiannou et al.
The software consists of a GUI divided into the four following tabs:
GeoGravGOCE software is designed to pre-process the SGG data, reduce the gravity field's systematic trends of GGs, filter the reduced signals, and transform the final GOCE signals to the conventional reference frames.
GeoGravGOCE
1. SGG Pre-processing
2. GGM Transformation
3. Filtering
4. Reference Systems Transformations
goal & structure

## Slide 4
SGG Pre-processing
GOCE gradiometric data (EGG_NOM_2)
Precise science kinematic orbits (SST_PSO_2)
GOCE orbit delineation
Geodetic coordinates calculation
.MAT files with gravity gradients in GRF ()
Statistics
Figures
Inputs:
Outputs:
Processes:
E.G. Mamagiannou et al.
Software: GeoGravGOCE
This tab pre-processes the Level 2 GOCE products, provides visualization of the output files and offers additional output options.
Info

## Slide 5
Time series of the GOCE gravity gradients
GOCE altitude
Global maps with the GOCE orbit track
The maps are created via the m_map mapping toolbox (Pawlowicz, 2020).
Figures:
Software: GeoGravGOCE
SGG Pre-processing
outputs
E.G. Mamagiannou et al.

## Slide 6
TXT-files with the gravity gradient’s geodetic coordinates in the format: .
Computation of the gravitational tensor components via GrafLab software (Bucha & Janák, 2013).
Software: GeoGravGOCE
SGG Pre-processing
outputs
Additional outputs:
E.G. Mamagiannou et al.

## Slide 7
Software: GeoGravGOCE
GGM Transformation
Inputs:
GGM gravitational tensor components
Quaternios (PSO_2_QAT)
Processes:
Quaternion interpolation
Transformations: LNOF EFRF IRF GRF
This tab is used for the transformation of a Global Geopotential Model's gravity gradients from the LNOF to the GRF.
Outputs:
.MAT files with the transformed gravity gradients
Figures
Statistics
Info
E.G. Mamagiannou et al.

## Slide 8
Software: GeoGravGOCE
GGM Transformation
outputs
Figure:
The transformed gravity gradients in GRF.
E.G. Mamagiannou et al.

## Slide 9
Software: GeoGravGOCE
Filtering
options
3 input options for the upcoming filtering
3 filtering methods (FIR, IIR, Wavelet).
This tab provides optimal filtering methods for the observed gravity gradients, which remove low-frequency errors and undesired effects by preserving the signals in GOCE MBW (0.005-0.1 Hz).
The tab offers:
Note:
Each method performance evaluation is done in terms of the Power Spectral Densities (PSDs) of the original unfiltered and filtered signal.
Info
E.G. Mamagiannou et al.

## Slide 10
Software: GeoGravGOCE
Filtering
FIR
FIR filter is non-recursive. Its output is computed using only the current and previous inputs. So, there is no feedback in the filter structure.
Input:
Outputs:
Filter's order (user’s choice)
.MAT files with the filtered reduced GOCE signal ()
Statistics
Figures
Magnitude response of the filter
Info
E.G. Mamagiannou et al.

## Slide 11
Software: GeoGravGOCE
Filtering
FIR
outputs
Figures:
The reduced FIR filtered Vij in GRF.
PSDs of the reduced FIR filtered GOCE signals.
Magnitude and Phase response of the -order filter.
Unfiltered
E.G. Mamagiannou et al.

## Slide 12
Software: GeoGravGOCE
Filtering
IIR
IIR is a recursive filter. The filter's output is computed using the current and former inputs and former outputs.
Input:
Outputs:
Filter's order (user’s choice)
.MAT files with the filtered reduced GOCE signal
Statistics
Figures
Magnitude response of the filter
Info
E.G. Mamagiannou et al.

## Slide 13
Software: GeoGravGOCE
Filtering
IIR
outputs
Figures:
The reduced IIR filtered Vij in GRF.
PSDs of the reduced IIR filtered GOCE signals.
Magnitude response of the -order filter.
E.G. Mamagiannou et al.

## Slide 14
Software: GeoGravGOCE
E.G. Mamagiannou et al.
Filtering
Wavelet
Wavelet Multi-Resolution Analysis uses a 1d Daubechies family wavelet with 10 vanishing moments (db10) at 12 levels of decomposition.
Info
Decomposition in twelve levels.
Reconstruction of the selected detail coefficients (user’s choice).
Processes:
13 checkboxes: the twelve detail coefficients of the levels and the approximation coefficient of the last level.
Outputs:
.MAT files with the filtered reduced GOCE signal
Statistics
Figures

## Slide 15
The detail and approximation coefficients of the gradient of the first orbit.
Software: GeoGravGOCE
E.G. Mamagiannou et al.
Filtering
Wavelet
outputs
Figures:
d1
d2
d5
d6
d3
d4
d7
d8
d9
d10
d11
d12
a12
Spatial resolution
d1: 8-16 km
d2: 16-32 km
...
Info
decomposition

## Slide 16
Software: GeoGravGOCE
E.G. Mamagiannou et al.
d1
d2
d5
d6
d3
d4
d7
d8
d9
d10
d11
d12
a12
Figures:
PSDs of the detail and approximation coefficients of the gradient of the first orbit.
Filtering
Wavelet
outputs
decomposition

## Slide 17
Software: GeoGravGOCE
E.G. Mamagiannou et al.
Reconstructioned gravity gradients & their PSDs.
Figures:
Filtering
Wavelet
outputs
reconstruction
Filtered
Unfiltered

## Slide 18
Software: GeoGravGOCE
E.G. Mamagiannou et al.
Reference Systems Transformations
This tab is used for the transformation of the gravity gradients from the GRF to the LNOF and vice versa.
Info
Input:
.MAT file (in the required format)
Processes:
Transformations: LNOF EFRF IRF GRF
Transformations: GRF IRF EFRF LNOF
Outputs:
.MAT files with the transformed gravity gradients
Figures
Statistics

## Slide 19
Software: GeoGravGOCE
E.G. Mamagiannou et al.
Reference Systems Transformations
outputs
GRF
LNOF
Figures:
The transformed gravity gradients.

## Slide 20
Software: GeoGravGOCE
E.G. Mamagiannou et al.
GUI efficiency
SGG Pre-processing (1st tab)
GGM Transformation (2nd tab)
Multi-processing
The GeoGravGOCE software has been developed in such a way that when multiple files are requested as input, parallel processing capabilities are enabled.

## Slide 21
Software: GeoGravGOCE
E.G. Mamagiannou et al.
Conclusions
GeoGravGOCE:
Is an open-source software developed with MATLAB.
Consists of an easy-to-use Graphical User Interface divided into four tabs.
Allows the reliable pre-processing of the GOCE gravity gradients, precise transformation in their reference frames, and appropriate filtering with a FIR, an IIR, and a Wavelet MRA filter.
Is suitable for educational purposes, as it provides all the necessary pre-process of GOCE GGs, and can manage extensive experiments with multiple files.
Free download: http://olimpia.topo.auth.gr/GeoGravGOCE/

## Slide 22
Software: GeoGravGOCE
E.G. Mamagiannou et al.
References
Bucha, B., & Janák, J. (2013). A MATLAB-based graphical user interface program for computing functionals of the geopotential up to ultra-high degrees and orders. Computers and Geosciences. https://doi.org/10.1016/j.cageo.2013.03.012
Pawlowicz, R. (2020). M_Map: A Mapping package for Matlab (1.4m). https://www.eoas.ubc.ca/~rich/map.html

## Slide 23
Software: GeoGravGOCE
E.G. Mamagiannou et al.
Acknowledgements
The research project was supported by the Hellenic Foundation for Research and Innovation (H.F.R.I.) under the “1st Call for H.F.R.I. Research Projects to support Faculty members and Researchers and the procurement of high-cost research equipment grant” (Project Number: 3488.).
GeoGravGOCE is funded by (HFRI) within its Call for Research Projects for Research and Academic Staff (HFRI/Staff) following a successful application to the General Secretariat for Research & Technology (GSRT).