## Slide 1
(1)
introduction
(2)
study area
(3)
methods
(4)
results
AIM OF THE RESEARCH
(5)
outcomes
The role of inter-row grass cover in steep viticulture: understanding soil erosion combining in-field observation and remote sensing
Eugenio Straffelini (1), Stefan Otto (2), Anton Pijl (1), Enrico Marchesini (3), Simone Gottardi (3), Nicola Tormen (4), Andrea Pitacco (1), Luca Tezza (1), Paolo Tarolli(1)
(1) Department of Land, Environment, Agriculture and Forestry, University of Padova, 35020 Legnaro (PD), Italy, eugenio.straffelini@unipd.it
(2) National Research Council, Institute for Sustainable Plant Protection, Agripolis, 35020 Legnaro (PD), Italy, stefan.otto@cnr.it
(3) Agrea s.r.l, 37057 San Giovanni Lupatoto (VR), Italy, enrico.marchesini@agrea.it
(4) WBA Project s.r.l, 37137 Verona (VR), Italy, nicola.tormen@gmail.com
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 2
This work aims to evaluate the effectiveness of different types of grass cover in terms of erosion and runoff generation in steep slope viticulture.
We propose the combination of 2 different approach:
  Field-based measurement of water & sediment using special traps;
  Modelling based on high-resolution UAV-SfM data
AIM OF THE RESEARCH
home:
(1)
introduction
(2)
study area
(3)
methods
(4)
results
(5)
outcomes
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 3
(1)
introduction
Steep slope viticulture is a common practice in the Mediterranean basin offering landscapes of considerable environmental and socio-economic value. However, these complex agricultural systems are very fragile.
One of the main problems is soil erosion due to extreme rainfall, both in terms of drop splash and water accumulation. This may cause a progressive reduction in soil fertility and the occurrence of instabilities and land degradation phenomena.
Sustainable farming techniques may provide innovative solutions to reduce the risk of soil erosion. A virtuous approach involves the use of herbaceous coverings between the rows of vines, for many reasons. They provide active protection from the kinetic energy of water droplets; reduce the amount of water flowing on the surface positively affecting the infiltration capacity of the soil; improve ecosystem services in the vineyard.
home:
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 4
(2)
study area
Veneto region, IT
home:
www.soilutionsystem.com
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 5
(3)
methods
Continuous tillage
Reference
Nectariferous
(year 1 & 2)
Single tillage
Native
grass cover comparison
erosion/deposition analysis
home:
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 6
(3)
methods
grass cover comparison
methods:
home:
Continuous tillage
Row ploughed continuously throughout the year to ensure bare soil removing grass and vegetation cover
Reference
Row managed in the same way as the vineyard is traditionally managed. Constant herbaceous cover throughout the year and use of machinery
Nectariferous
Row managed by annual herbaceous cover designed to promote rapid growth and consisting of pollen and nectar seed mix. Use of machinery
Single tillage
Row ploughed and sown in autumn and not tilled again during the year. Use of machinery
Native
Row sown with native species of the place where the vineyard is located. Use of machinery
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 7
(3)
methods
erosion/deposition analysis
methods:
home:
Field-based approach
Modelling approach
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 8
(3)
methods
ero-dep analysis:
home:
Field-based approach
erosion/deposition analysis
runoff & sediment trap
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 9
Field-based approach:
home:
Setting up of a system (cost-effective and easy-to-install) that collect runoff/sediment transported to the bottom of the experimental rows;
The system consists of a box and aluminum channels that transport the runoff/sediment inside;
Rainfall is constantly monitored using weather station data and from field measurements of total precipitation;
Following the intense precipitation that generated the runoff, the amount of water in the box is measured and a sample is collected. By sediment concentration analysis, the amount of soil and water caused by the precipitation is estimated;
This provides an assessment of the runoff and sediment generating capacity of each type of management studied.
25 %
80 m2
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 10
(3)
methods
erosion/deposition analysis
home:
ero-dep analysis:
Data collection
DJI Matrice 210v2 & GNSS
Point cloud generation (SfM) & filtering
Digital Terrain Model (DTM)
1
2
3
SIMulation Water Erosion
4
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 11
(3)
methods
erosion/deposition analysis
home:
modelling approach:
SIMWE
r.sim.water
simulation of surface runoff
input
output
DTM
Soil infiltration rate
Rainfall value
Manning value
Runoff depth (mm)
Runoff discharge(m3/s)
r.sim.sediment
simulation of soil erosion/transportation/deposition
input
output
DTM
Runoff depth (mm)
Soil characteristics
Manning value
Transport capacity [kg/ms]
Sediment concentration [particle/m3]
Sediment flux [kg/ms]
Erosion/deposition [kg/m2s]
Model developed by Mitas and Mitasova (1998)
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 12
home:
(4)
results
erosion/deposition estimation
Field-based approach
Modelling approach
methods:
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 13
home:
(4)
results
Management | Runoff (m3) | Sed. (mg/L)
Reference | 0.021 | 132.5
Cont. tillage | 0.020 | 147.5
Nect. (yr 1) | 0.012 | 88.7
Nect. (yr 2) | Under study | Under study
Sing. tillage | Under study | Under study
In Reference, on average more runoff was observed than in Continuous Tillage and Nectariferous;
Less runoff was observed in Continuous Tillage than in Reference (mainly thanks to a higher infiltration rate of the soil), but a higher concentration of sediment;
In Nectariferous less runoff and less sediment was observed, which proved to be a good management for soil erosion mitigation promoting biodiversity.
Runoff was a quite common event. The runoff/rainfall ratio was low, showing good infiltration capacity of the soil. Soil loss was also low, showing the low erodibility of soil.
Soil loss variability agrees with the loss measured by Bagagiolo et al. (2008) using more complex runoff measuring systems, as well as the number of events were similar
↓2020↓ | 
Total rainfall (mm) | 1271
Rainfall/runoff events | 8
Runoff/rainfall ratio (%), average ¦ max | 0.2 ¦ 0.8
Sediment transported by runoff (kg/ha), average ¦ max | 11 ¦ 176
Rainfall analysis
results:
runoff & erosion/deposition estimation
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 14
home:
Rainfall Analysis
RE1 >> RE8 are the 8 rainfall that generated runoff
runoff & erosion/deposition estimation
(4)
results
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 15
home:
(4)
results
particle/m3 is a measure of sediment concentration in the runoff (log-scale);
In cont.till the highest sediment concentration is observed for each rainfall simulation. This is followed by ref. under lower intensity conditions. At higher intensities, the situation is similar also for net and sing.till.
Q measures the water discharge of the runoff (log-scale);
In cont.till the smallest discharge is observed under lower intensity rainfall thanks to soil infiltration rate. In ref., the higher Q values are observed. At higher intensities, the situation tends to become homogeneous.
results:
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society

## Slide 16
home:
(5)
outcomes
results:
Management | Runoff (m3) | Sed. (mg/L)
Reference | 0.021 | 132.5
Cont. tillage | 0.020 | 147.5
Nect. (yr 1) | 0.012 | 88.7
Nect. (yr 2) | Under study | Under study
Sing. tillage | Under study | Under study
↓2020↓ | 
Total rainfall (mm) | 1271
Rainfall/runoff events | 8
Runoff/rainfall ratio (%), average ¦ max | 0.2 ¦ 0.8
Sediment transported by runoff (kg/ha), average ¦ max | 11 ¦ 176
Both approaches show the importance of inter-row grass cover to protect the soil surface for mitigating soil loss;
A single tillage during autumn in combination with nectariferous grass cover may provide a balance between the effect of the tillage (> infiltration rate), soil protection and sustainability in the management
https://doi.org/10.5194/egusphere-egu21-2158
Earth Surface Processes
and Society