## Slide 1: A Constructive Heuristic approach for solving Mixed Integer Nonlinear cascade optimization
Considering an hydrological uncertainty model
Daniel Firmo Kazay, Carlos Roberto Mendonça da Rocha
Universidade Estadual do Oeste do Paraná – Unioeste, Brazil
Results
Case Study
Formulation
Overview
Resolution Method
The orange ‘Home’
Button takes you to
the section menu
The left/right arrows
take you to the
next page
PICO Navigation
Conclusions

## Slide 2: A Constructive Heuristic approach for solving Mixed Integer Nonlinear cascade optimization
Overview
Overview
Challenge: NL formulation + Consistent Scenarios
High-dimensional problems, Mixed Integer Nonlinear Programming solution.
Use of Constructive Heuristics
Considering an hydrological uncertainty model
Daniel Firmo Kazay, Carlos Roberto Mendonça da Rocha
Universidade Estadual do Oeste do Paraná – Unioeste, Brazil
Scenarios
Ensemble Forescast
Hydrological Simulations
Formulation
Detailed representation of
hydropower plant cascade
operation
NLP Solver + CH
Case study
Photo: Itaipu Binacional

## Slide 3
Case Study
General Information
Four hydropower plants: H1, H2, H3 and H4.
H1, H2 and H3 have three turbines; H4 has five turbines.
The time delay between the hydropower plants are one hour
Scuzziato (2011)
Photo: Itaipu Binacional
¹ There are two turbine groups in H4 with different technical characteristics

## Slide 4
Resolution
Formulation
Formulation
Mass balance
Hydraulic, mechanical and electrical losses equations.
Energy balance
Objetive function: Minimize the discharge
Max and min power generation
Turbine efficiency equation
Conception
Power generation equation
Complete formulation
Upstream and downstream level
Scenarios
Photo: Itaipu Binacional

## Slide 5
Conception
t is the set of hours considered for scheduling
s is the set of considered scenarios.
Choice of the best power scheduling for the hydropower plant cascade
Considering several precipitation scenarios
Forecast date
Photo: Itaipu Binacional
Daily Inflow (m³/s)

## Slide 6
Daily Inflow (m³/s)
Scenarios
Forecast date
ECMWF Ensemble (51 members)
Hydrological model
Photo: Itaipu Binacional

## Slide 7
Objectve Function
Z is the objective function.
a is a coefficient considered in the proposed Constructive Heuristic.
Q is the outflow of the turbine.
This objective function aims to supply a fixed demand using the minimum of water
Photo: Itaipu Binacional

## Slide 8
Mass Balance Equation
α is a conversion term.
τ is the time delay of the hydropower plants.
β is the set of hydropower plants located upstream of the hydropower plant.
I is the incremental flow.
V is the volume of the reservoir
Photo: Itaipu Binacional

## Slide 9
Energy balance
D is the power demand.
Pg is power generated per turbine
Each hydropower plant needs to supply a power demand
Power demand (MW)
Time (h)
Adapted from Scuzziato (2011)
Photo: Itaipu Binacional

## Slide 10
Turbine efficiency equation
Hydraulic net head (m)
Outflow of the turbine (m³/s)
Efficiency
Max and min outflow of the turbines
Power generated
Adapted from Scuzziato (2011)
ρ is the turbine efficiency.
HH is the hydraulic net head.
f6, f7 and f8 are polynomial functions.
Photo: Itaipu Binacional

## Slide 11
Power generation equation
Pst is the brut power generated per turbine
G is a constant
Q is the outflow of the turbine
HH is the hydraulic net head.
ρ is the turbine efficiency.
Classical approach to estimate the power generated per turbine
Photo: Itaipu Binacional

## Slide 12
Max and min power generation
Pg is power generated per turbine.
Pmin and Pmax are the thresholds of power of the turbine.
Pmax
Pmin
Photo: Itaipu Binacional
Pu of MW
Pu of MVar

## Slide 13
Losses equations
Pg is power generated per turbine.
Pst is the brut power generated by the turbine.
Pgg are the electrical losses of the generator.
Pmt are the mechanical losses of the generator.
f1 and f5 are polynomial equations.
f2 is an exponential equation.
HH is the hydraulic net head.
UP is the upstream level.
Down is the downstream level.
Lo are the hydraulic and mechanical losses.
Losses
Photo: Itaipu Binacional

## Slide 14
Upstream and downstream level
Up is the upstream level.
Down is the downstream level.
f3 and f4 are polynomial equations.
Downstream level
Upstream level
Turbine outflow
Reservoir volume
Adapted from Scuzziato (2011)
Photo: Itaipu Binacional

## Slide 15
Z is the objective function. a is a coefficient considered in the proposed Constructive Heuristic. Q is the outflow of the turbine. H is the set of hydropower plants. U is the set of turbines. t is the set of hours considered in the problem. s is the set of considered scenarios. α is a conversion term. τ is the time delay of the hydropower plants. β is the set of hydropower plants located upstream of the hydropower plant. I is the incremental flow. V is the volume of the reservoir. D is the power demand. Pg is power generated per turbine. Pmin and Pmax are the thresholds of power of the turbine. Pst is the net power generated by the turbine. Pgg are the electrical losses of the generator. Pmt are the mechanical losses of the generator. f1, f2, f3, f4, f5, f6, f7 and f8 are functions. HH is the hydraulic net head. UP is the upstream level. Down is the downstream level. Lo are the hydraulic and mechanical losses. ρ is the turbine efficiency curve.
Complete formulation
For each scenario s

## Slide 16
Resolution
The left/right arrows
take you to the
next page
Conception
Non linear equations with integrity restrictions
Constructive Heuristic approach
Sensivity factor is the variable “a” that represents the aperture of the turbine
Software GAMS
Solver CONOPT
Photo: Itaipu Binacional

## Slide 17: The proposed CH
Consider a continuum variable (a);
Values between 0 and 1 ;
For
  each turbine
  of each hydropower plant
  of each time step
Resolution
Photo: Itaipu Binacional

## Slide 18: The proposed CH
The proposed CH has two parts:
1ª part: Definition of integer part
  The NLP solver get a solution for a real value of “a”.
  The "a" values ​​of all turbines in each plant for each time step are added together.
  The truncated sum value is the number of turbines whose "a" is set to 1.
  The values ​​of the variables "a" of the last remaining turbines subtracted from 1 are fixed at 0.
  Only one turbine position per plant per time step remains free "a".
  In other words, only the fractional part of the sum value remains free for the optimization problem.
Resolution
Photo: Itaipu Binacional

## Slide 19: Example
1ª part: Definition of the integer part of the project
H4
t = 3
a(u1) = 0.8
a(u2) = 0.8
a(u3) = 0.8
a(u4) = 0
a(u5) = 0
Resolution
Photo: Itaipu Binacional

## Slide 20: Example
H4
t = 3
a(u1) = 0.8
a(u2) = 0.8
a(u3) = 0.8
a(u4) = 0
a(u5) = 0
Sum = 2.4
1ª part: Definition of the integer part of the project
Resolution
Photo: Itaipu Binacional

## Slide 21: Example
1ª part: Definition of the integer part of the project
H4
t = 3
a(u1) = 0.8
a(u2) = 0.8
a(u3) = 0.8
a(u4) = 0
a(u5) = 0
Sum = 2.4
a(u1) = 1
a(u2) = 1
a(u3) = ?
a(u4) = 0
a(u5) = 0
a(u1,u2,u4,u5) – fixed
a(u3) - variable
Resolution
Photo: Itaipu Binacional

## Slide 22: The proposed CH
The proposed CH has two parts:
1ª part: Definition of integer part
2ª part: Definition of the fraction part
  The problem is solved two times for the two possibilities of the free “a” values [0;1]
  The Objetive Function (OF) values are compared
Resolution
Photo: Itaipu Binacional

## Slide 23: Example
2ª part: Definition of the fraction part of the problem.
a(u1) = 1
a(u2) = 1
a(u3) = ?
a(u4) = 0
a(u5) = 0
a(u1) = 1
a(u2) = 1
a(u3) = 0
a(u4) = 0
a(u5) = 0
a(u1) = 1
a(u2) = 1
a(u3) = 1
a(u4) = 0
a(u5) = 0
1
2
Resolution
Photo: Itaipu Binacional

## Slide 24: Example
2ª part: Definition of the fraction part of the problem.
a(u1) = 1
a(u2) = 1
a(u3) = ?
a(u4) = 0
a(u5) = 0
a(u1) = 1
a(u2) = 1
a(u3) = 0
a(u4) = 0
a(u5) = 0
a(u1) = 1
a(u2) = 1
a(u3) = 1
a(u4) = 0
a(u5) = 0
Solution?
Solution?
1
2
No
2
No
1
Resolution
Photo: Itaipu Binacional

## Slide 25: Example
2ª part: Definition of the fraction part of the problem.
a(u1) = 1
a(u2) = 1
a(u3) = ?
a(u4) = 0
a(u5) = 0
a(u1) = 1
a(u2) = 1
a(u3) = 0
a(u4) = 0
a(u5) = 0
a(u1) = 1
a(u2) = 1
a(u3) = 1
a(u4) = 0
a(u5) = 0
Solution?
Solution?
1
2
No
2
No
1
Yes
OF(1)<OF(2)?
1
Yes
Yes
No
2
Resolution
Photo: Itaipu Binacional

## Slide 26
Results
Hystogram of Objective Function Value
52.590
52.595
52.600
Number of scenarios
Photo: Itaipu Binacional

## Slide 27: Results of reservoir volume
H1
Results
H2
Scenarios
Photo: Itaipu Binacional

## Slide 28
Conclusions
Conclusions
The results of the Constructive Heuristic were compared with other similar works with perfect correspondence.
The system was tested for 51 ECMWF precipitation forecast scenarios as input of the hydrologic model MGB (Large Basin Model) with coherent results.
The proposal is a feasible approach to reach unique optimal solutions for high-dimensional non-linear problems considering integer variables.
Further information
Scuzziato (2011)
Photo: Itaipu Binacional