## Slide 1
EGU General Assembly 2021 Vienna Austria 19-30 April 2021
Scarp of the landslide of 1999
Monte Cornito
1) RAINFALL DATASET: 1000 years synthetic hourly rainfall series has been generated with the Neyman-Scott Rectangular Pulse (NSRP) model (calibrated with available data from 1st January 2001 to 31st December 2017 )
Case study: Cervinara slope
2) PHYSICALLY-BASED MODEL OF INFILTRATION: Richards 1D equation (all the parameters have been assigned according to available laboratory and field monitoring observations)
3) SLOPE STABILITY ANALYSIS: geotechnical module for the evaluation of the factor of safety under the inﬁnite slope hypothesis
IDENTIFICATION OF HYDRO-METEOROLOGICAL THRESHOLDS FOR RAINFALL-INDUCED LANDSLIDE PREDICTION WITH CLUSTERING TECHNIQUES
Leakage
Naples

## Slide 2
EGU General Assembly 2021 Vienna Austria 19-30 April 2021
Landslide prediction with meteorological and hydro-meteorological thresholds
The red lines, obtained by maximising the true skill statistic (TSS) for 1000 years long synthetic data sets (rainfall and water content), represents the thresholds separating landslides (P) and no landslides event (N)
TSS
 | Cervinara slope (total rainfall events = 53061) |  |  |  |  | 
 | Threshold law | Plane | True skill statistic (TSS) | N. of landslides (Positives) | Missed Alarms (M) | False Alarms (F)
1) |  | log(D)–log(I) | 0.908 | 42 | 3 | 1107
2) | X + B | - H | 0.971 | 42 | 1 | 290
 | Cervinara slope (total rainfall events = 53061) |  |  |  |  | 
 | Threshold law | Plane | True skill statistic (TSS) | N. of landslides (Positives) | Missed Alarms (M) | False Alarms (F)
1) |  | log(D)–log(I) | 0.908 | 42 | 3 | 1107
2) |  |  | 0.971 | 42 | 1 | 290
IDENTIFICATION OF HYDRO-METEOROLOGICAL THRESHOLDS FOR RAINFALL-INDUCED LANDSLIDE PREDICTION WITH CLUSTERING TECHNIQUES
Rainfall events after which no landslide is triggered;
Rainfall events followed by the triggering of a landslide;
1)
2)
Meteorological threshold D-I
Hydro-meteorological threshold - H

## Slide 3
EGU General Assembly 2021 Vienna Austria 19-30 April 2021
Dynamic 3D clustering
IDENTIFICATION OF HYDRO-METEOROLOGICAL THRESHOLDS FOR RAINFALL-INDUCED LANDSLIDE PREDICTION WITH CLUSTERING TECHNIQUES
LANDSLIDE FREQUENCY
Landslide prediction with clustering techniques
No landslides events (Negatives = 53019)
Landslides events (Positives = 42)
Cervinara slope (rainfall events = 53061)

## Slide 4
EGU General Assembly 2021 Vienna Austria 19-30 April 2021
Identification of hydro-meteorological thresholds for rainfall-induced landslide prediction with clustering techniques
Pasquale Marino, Carlo Giudicianni, Giovanni Francesco Santonastaso, and Roberto Greco
Università della Campania ‘Luigi Vanvitelli’ – Dipartimento di Ingegneria - Aversa (CE), Italy
THANK YOU FOR YOUR ATTENTION!!!
FOR ANY QUESTION ASK IN CHAT