## Slide 1: An Assessment of CYGNSS Ocean Wind Speed Products
Matthew Hammond, Giuseppe Foti, Christine Gommenginger, Meric Srokosz, and Nicolas Floury
EGU 2021

## Slide 2: NASA CYGNSS
NASA’s GNSS-Reflectometry mission
Aimed at retrieval of wind speeds - particularly in hurricanes
Constellation of 8 satellites
  A first for GNSS-R
  Covering latitudes ±38°
  Providing rapid revisit times (mean = 7hrs)

## Slide 3: Background and Method
Ocean surface roughness is the first-order geophysical driver of Sigma0
  Also secondary dependencies (SWH, SST, SSS, etc)
Fixing ocean surface conditions -> reveal non-geophysical effects in L1 data
ECMWF ERA-5 reanalysis model output used as reference
  Wind & wave data, 1hr / ~30km resolution, global
CYGNSS reflected signals collocated with ECMWF ERA-5
  v3.0 L1 (Aug 2018 – Dec 2019)
  ~7 Tbytes CYGNSS catalogue

## Slide 4
CYGNSS L1 v3.0 NBRCS
Notes:     Instrument: (geometry / antenna / attitude)
    Surface: (wave conditions)

## Slide 5: NBRCS Geographical patterns
Setup
  Single FM
  Single SVN
  U10 ~7 m/s
Prominent geographical biases in NBRCS

## Slide 6: NBRCS Geographical patterns
Setup
  Single FM
  Single SVN
  U10 ~7 m/s
Prominent geographical biases in NBRCS
Geographical pattern strongly correlated with bistatic geometry

## Slide 7
Setup
  All SVN
  U10 ~7 m/s
Inter-calibration bias ~0.1dB
Sigma0 range up to ~2 dB (for fixed wind speed)
NBRCS vs Incidence Angle

## Slide 8
Setup
  Single FM
  Split by SVN (all)
  Coloured with GPS Block
  U10 ~7m/s
Strong dependence on SVN and geometry
  Range ~3dB
NBRCS vs SVN and Incidence Angle

## Slide 9
CYGNSS L1 v3.0 LES
Notes:     Instrument: (geometry / antenna / attitude)
    Surface: (wave conditions)

## Slide 10: LES Geographical patterns
Setup
  Single FM
  All SVN
  U10 ~7 m/s
Strong spatial pattern in LES
  Not wind/wave related
Instead related to geoid
  Geoid undulation values w.r.t. WGS84
LES calculation approach?

## Slide 11: LES Geographical patterns
Setup
  Single FM
  All SVN
  U10 ~7 m/s
Strong spatial pattern in LES
  Not wind/wave related
Instead related to geoid
  EGM2008 geoid height (relative to WGS84)
Impact of geoid on LES calculation in DDM?
EGM2008 geoid height

## Slide 12: Summary
We fixed ocean surface conditions (U10~7 m/s) to analyse non-geophysical effects in CYGNSS L1 v3.0
Prominent geographical patterns in NBRCS shown
  Not associated with geophysical phenomena, but with residual dependence on SVN and bistatic geometry
LES shows similar dependence on SVN and geometry as found for NBRCS
In addition, LES shows geographical patterns linked to the geoid
  Likely due to current estimation of LES from DDMs
Biases and variability in CYGNSS L1 data all linked to unresolved instrument and processing issues, or to inaccuracies in the process of signal calibration
Notes:     Instrument: (geometry / antenna / attitude)
    Surface: (wave conditions)

## Slide 14: Extra

## Slide 15
Setup
  U10 ~ 7m/s
  All SVN
  Split by FM
Azimuthal dependence ~1dB
NBRCS vs Azimuth Angle