## Slide 1
Scientific aspects about the project SWEETS
Within the project SWEETS (FFG funded) it is intended to develop a forecasting model, to predict the expected impact of solar events, like coronal mass ejections (CMEs), on satellites at different altitudes between 300-800 km. For the realization, scientific data, such as kinematic orbit information and accelerometer measurements, from a wide variety of satellites are incorporated. Based on the evaluation of the impact of several hundred solar events on the thermosphere the forecasting will be realized through a joint analysis and evaluation of solar wind plasma and magnetic field data observed at the Lagrange point L1.
In this contribution we show first preliminary results of thermospheric densities estimates based on kinematic orbit information for different satellite missions (e.g., TerraSAR-X, TanDEM-X, Swarm A-C, GRACE, GRACE-FO, CHAMP). To validate the outcome, we compare the results with state-of-the-art thermospheric models as well as with densities estimated from accelerometer measurements if available. Finally, for some specific CME events we will perform a comparison between the post-processed density estimates and results from our preliminary forecasting tool.
Kinematic orbit information / products
Event description
Results
Estimation of neutral mass densities
Evaluation of the approaches
Forecasting orbit decay
Click on the
section you
are interested in
Current status of project SWEETS:
Estimating thermospheric neutral mass densities from satellite data at various altitudes
S. Krauss1, B. Suesser-Rechberger1, S. Behzadpour1, T. Mayer-Guerr1, M. Temmer2, S. Kroisz2, L. Drescher2 1Institute of Geodesy, Graz University of Technology, 2Institute of Physics, University of Graz
This work is funded by the Austrian Research Promotion Agency (FFG): Proj. No.:878876

## Slide 2
Preparation of kinematic orbit information
All data are freely available at our website:
https://www.tugraz.at/institutes/ifg/downloads/satellite-orbits/
Methodology:
GRACE-FO-1
TerraSAR-X
TanDEM-X
GRACE-FO-2
GRACE-1
GRACE-2
CHAMP
Jason-1
Jason-2
Jason-3
MetOp-A
MetOp-B
Sentinel-1A
Sentinel-1B
Sentinel-3B
Sentinel-3A
Swarm-1
Swarm-3
Swarm-2
The list of currently processed satellites includes:
Available products for each satellite are as follows
Kinematic orbit
Attitude
Reduced Dynamic Orbit
Non-conservative forces
Covariance
Observing atmospheric variations by means of precise positions of low earth orbiting (LEO) satellites is an appropriate additional method besides to satellite missions with on board accelerometers.
The kinematic strategy for precise orbit determination of LEO satellites uses only geometric observations to estimate the satellite orbit and does not take any forces into account.
This strategy requires a large number of observations for one epoch to estimate the satellite position. The determination of the kinematic orbits is done via a raw observation approach using an iterative least square adjustment and systematic effects are corrected or will be estimated as parameters
Raw observation processing steps:
Determination of GNSS orbit, clock and bias solutions
  Solving GNSS antenna center variations and take them for the next determination iteration
GNSS orbit, clock and bias solutions are then input parameters for the kinematic orbit determination
  Solving LEO satellite antenna center variations and take them for the next determination iteration
https://github.com/groops-devs/groops
GROOPS
Preparation of kinematic orbit information

## Slide 3
Preparation of kinematic orbit information
GNSS processing is split into two parts:
            Ground station GNSS network processing (GNSS orbit, clocks and biases as well as NEQs for GNSS ACV)
            Kinematic orbit processing (LEO Orbit and NEQs for LEO and GNSS ACVs )
Illustration of the GNSS processing
Residuals
Normal equations
for LEO ACV
LEO ACV
Ground station-GNSS network
GNSS-LEO satellite
Normal equations
for GNSS ACV
GNSS ACV
Normal equations
for GNSS ACV
Accuracy
Kinematic orbit processing
GNSS orbits
clocks, biases
Ground station-GNSS network processing
output:
GNSS orbits, clocks, biases
Normal equations for GNSS antenna center variations (ACV)
output:
LEO Orbit
Normal equations for LEO and GNSS antenna center variations (ACV)
LEO ACV
determination
Measurement
determination
GNSS ACV
determination

## Slide 4
Within the project SWEETS we pursue two approaches for the estimation of thermospheric mass densities. The first is based on on-board accelerometer measurement - applicable for the satellite missions CHAMP, GRACE, GRACE-FO. The second approach relies on kinematic orbit information and is applied for the other satellites which are not equipped with on-board accelerometers.
SWARM A-C
Estimation of neutral mass densities
Accelerometer
observation
Acceleration
calibration
Reduction of undesired accelerations
Earth radiation pressure
Solar radiation pressure
Spacecraft
re-radiation
Density estimation
Along-track accelerations and resulting neutral mass densities
GRACE-A
GNSS processing
CHAMP, GRACE, GRACE-FO
GNSS tracked satellites like Swarm, TerraSAR-X, TanDEM-X, Sentinel(s), Icesat , …
Two-step approach by
Klinger et al. (2015)
Vielberg and Kusche (2020)
Fahnenstock et al. (2012)
Montenbruck et al. (2015)
Wetterer et al. (2014)
Robertson (2015)
Eclipse modelling
orbit, clock,
bias solution
station (ACV)
Kinematic orbit determination
LEO (ACV)
Sutton (2009), Doornbos (2011)
Zehentner and Mayer-Gürr (2015)
Süsser-Rechberger et al. (2020)
Orbit fit
RDO | KIN
Background models

## Slide 5
In the case of GRACE the opportunity exists to estimate neutral mass densities based on on-board accelerometer data as well as kinematic orbit information. Thus, it is predestinated to evaluate the current approach to deviate accelerations from kinematic orbits. Preliminary results look very promising (see picture) and indicate that the kinematic approach is feasible way to estimate neutral mass densities. Thus, the approach can be applied for satellite missions which do not have accelerometer instruments on-board but are equipped with GNSS receivers.
SWARM A-C
Estimation of neutral mass densities based on accelerometer (white) and kinematic orbit information (red) during the geomagnetic storm in March 2015.
Evaluation applying both approaches
Accelerometer based approach:
Temporal resolution: 5 s
Drag estimation applying direct approach using
Kinematic orbit based approach:
Reduced dynamic orbit fitted to kinematic orbit
Spline degree 3
Sampling: 15 min
Estimate accelerometer bias in cross and radial direction
Models in use:
Satellite macro-model
SRP: SOLRAAS
ERP: monthly averaged CERES model (TOA-SYN1deg)
Horizontal winds via HWM-14 model
Gravity field (static+trend+annual): GOCO06s
Atmosphere+Ocean & atmos. tides: AOD1B RL06
Earth tides, pole tides (red. sec. pole): IERS 2014
Ocean tides: FES2014c
Ocean pole tides: Desai 2004
Gradient field: GOCO06s static up to d/o 5
Kvas et al. (2021)
Doornbos (2011)
Bettadpur (2012)

## Slide 6
The March 15, 2015 event caused the largest geomagnetic storm at Earth of solar cycle 24, and it registered a Dst peak of -223 nT. The movie covers the time range March 14-15, 2015, revealing multiple events using running difference images of SoHO/LASCO C2 and C3 white light data (in addition a potential field source surface model is used showing the global coronal magnetic field structure). The first eruption looks like a streamer blowout, maybe even backsided (not much is seen on the disk at that time) and there might be no interaction between these events which is also confirmed by other studies (e.g., Wang Y., 2016, JGR).
However, magnetic field reconstructions from in-situ data show two „intact“ flux ropes. The eruption site itself covered a large filament and showed very broad post-eruptive arcade. A filament eruption in two phases is a very common scenario and could be the cause of two flux ropes. Moreover, there was a coronal hole visible close to the CME eruption location (see image).
An interaction between the CME and the emanating high-speed stream from the coronal hole might be possible, pushing the CME in the rear part leading to a low expansion of the CME magnetic structure and with that it could keep a strong magnetic field that caused the high geoeffectiveness.“
Test case: ICME event on March 15, 2015.

## Slide 7
The approach of estimating neutral mass densities from kinematic orbits allows the evaluation of further satellite missions which differ in their actual orbital altitude, satellite size, mass or orientation of the orbital plane with respect to the sun-earth line (beta prime angle).
SWARM A-C
Results
Mean orbital altitudes:
Beta prime angles:
Estimated neutral mass densities based kinematic orbit information (grey). For a better visibility, the mean density per revolution is introduced (solid white line) and compared to modelled densities applying the JB2008 thermosphere model (red).
(Not shown are density estimates from GRACE-2, Swarm-3 and TanDEM-X due to their comparable orbit design to GRACE-1, Swarm-1 and TerraSAR-X, respectively) .

## Slide 8
The forecast of a possible storm induced orbit decay relies on the observations of the interplanetary magnetic field component Bz.
Observations are taken in near-real time from either of the spacecraft ACE, WIND or DSCOVR in the Lagrange point L1.
Background statistic is deviated from correlation analysis of ~ 200 ICME events between 2003 – 2015 and will be continuously extended.
Currently, the prediction is valid for a predefined altitude of 490km, but will be extended to further heights in the near future.
SWARM A-C
ST3.1 - 'Open Session on Ionosphere and Thermosphere’:
Wednesday, 28 April 2021, 15:48 CEST
EGU21-4773: “Statistical relations between in-situ measured Bz component and thermospheric density variations by Sofia Kroisz et al.”
For details of the corresponding presentation please see: https://meetingorganizer.copernicus.org/EGU21/session/40142
Forecasting storm induced orbit decay
Krauss et al. (2018, 2020)
Pilot study (“SODA”) for ESA – SSA service (ESC Ionospheric Weather)
Demonstrator of the prediction tool is available at
https://swe.uni-graz.at/index.php/services/nd-forecast
graphical update will be soon available
Further information:

## Slide 9
References

## Slide 10
References
Bettadpur S. (2012) Gravity Recovery and Climate Experiment. Product Specification Document GRACE 327-720 (CSR-GR-03-02), Rev 4.6 – May 29, 2012
Doornbos, E. (2011). Thermospheric density and wind determination from satellite dynamics (Doctoral dissertation), Delft University of Technology. https://doi.org/10.1007/978-3-642-25129-0
Fahnestock, E., Park, R., Yuan, D.-N., & Konopliv, A. (2012). Spacecraft thermal and optical modeling impacts on estimation Of the GRAIL Lunar Gravity Field. American Institute of Aeronautics and Astronautics (pp. 1–17). Minneapolis, Minnesota. https://doi.org/10.2514/6.2012-4428.
Klinger, B., & Mayer-Gürr, T. (2016). The role of accelerometer data calibration within GRACE gravity field recovery: Results from ITSG-Grace2016. Advances in Space Research, 58(9), 1597–1609. https://doi.org/10.1016/j.asr.2016.08.007
Krauss, S., Temmer, M., & Vennerstrom, S. (2018). Multiple satellite analysis of the Earth's thermosphere and interplanetary magnetic field variations due to ICME/CIR events during 2003–2015. Journal of Geophysical Research: Space Physics, 123, 1–11. https://doi.org/10.1029/2018JA025778
Krauss S., Behzadpour S., Temmer M., Lhotka C. (2020): Exploring thermospheric variations triggered by severe geomagnetic storm on 26 August 2018 using GRACE-FO data. Journal of Geophysical Research: Space Physics, 125, 1-14, 10.1029/2019JA027731
Kvas, A., Brockmann, J.M., Krauss, S., Schubert, T., Gruber, T., Meyer, U., Mayer-Guerr T., Schuh, W.D., Jaeggi, A., Pail, R. (2021): GOCO06s -- a satellite-only global gravity field model, Earth System Science Data}, 13, 1, 10.5194/essd-13-99-2021.
Montenbruck, O., Steigenberger, P., & Hugentobler, U. (2015). Enhanced solar radiation pressure modeling for Galileo satellites. Journal of Geodesy, 89(3), 283–297. https://doi.org/10.1007/s00190-014-0774-0
Robertson, R. V. (2015). Highly physical solar radiation pressure modeling during penumbra transitions (Unpublished doctoral dissertation), State University.
Suesser-Rechberger B.;Mayer-Guerr T.; Krauss S.; 2020, Kinematic Orbit Positioning Applying the Raw Observation Approach, Talk presented at AGU Fall Meeting, 1-17 December 2020 (online).
Vielberg, K., & Kusche, J. (2020). Extended forward and inverse modeling of radiation pressure accelerations for LEO satellites. Journal of Geodesy, 94, 43. https://doi.org/10.1007/s00190-020-01368-6
Wang Y, Zhang Q, Liu J, Shen C, Shen F, Yang Z, Zic T, Vrsnak B, Webb DF, Liu R, Wang S, Zhang J, Hu Q, Zhuang B (2016) On the propagation of geoeffective coronal mass ejection during March 15–17, 2015. J Geophys Res 121:7423–7434. doi:10.1002/2016JA022924
Wetterer, C. J., Linares, R., Crassidis, J., Kelecy, T., Ziebart, M., Jah, M., & Cefola, P. (2014). Refining space object radiation pressure modeling with bidirectional reflectance distribution functions. Advances in the Astronautical Sciences, 37(1), 185–196. https://doi.org/10.2514/1.60577
Zehentner N., T. Mayer-Gürr (2015): Precise orbit determination based on raw GPS measurements. In: Journal of Geodesy. doi: 10.1007/s00190-015-0872-7.