## Slide 1
Live presentation slide – 26.04.2021 13:53

## Slide 2
Combining recordings of earthquake ground-motion and ambient vibration analysis to estimate site response variability in the city of Lucerne, Switzerland
Paulina Janusz1, Vincent Perron1, Christoph Knellwolf3, Walter Imperatori1, Luis Fabian Bonilla2, Donat Fäh1
1 SED - ETH Zürich, 2 Université Gustave Eiffel, 3 Verkehr und Infrastruktur, Abteilung Naturgefahren, Kanton Luzern
Contact: paulina.janusz@sed.ethz.ch

## Slide 3: Introduction

## Slide 4
Seismic site effects
theguardian.com
Urban vulnerability
Elevated seismic risk
Recent urbanization
Exposed elements
High population
Ciaccio and Cultrera (2014)
Site effects
Increase of amplitude and/or duration of the ground motion
Importance of site effects
Mexico 1985
+
=

## Slide 5
The goal of the study
Evaluation of complex soil response and its variability in the urban environment
Linear site response analysis
Empirical methods
Reference site methods (earthquakes-,
noise-based)
using

## Slide 6
Case study – Lucerne area
Lucerne area
map.geo.admin.ch
map.geo.admin.ch
Central Switzerland

## Slide 7
Case study – Lucerne area
Lucerne area
Possibility of strong site effects and amplification of seismic waves
Narrow sedimentary basin
map.geo.admin.ch
map.geo.admin.ch

## Slide 8
Lucerne area - seismicity
Known earthquakes with damage
Seismic hazard SA 5Hz 10% in 50 years
All recorded earthquakes
Year 1601, Mw 5.9
seismo.ethz.ch
seismo.ethz.ch
Lucerne
Low-to-moderate seismicity area with some strong historical earthquakes

## Slide 9
Methods and results
Reference-site methods

## Slide 10
Evaluation of variability of soil response
Estimation of relative amplification factors with reference-site methods:
using earthquakes recordings
Standard Spectral Ratios (Borcherdt, 1970)
Perron et. al. (2018)

## Slide 11
Temporary local seismic monitoring network
Installation: November 2019
9 new station installed
permanent SSMNet stations
Recording time: about 6 months
map.geo.admin.ch
Removal: May/June 2020

## Slide 12
Standard spectral ratios (SSR)
Reference: rock station LUZ01
(the plots on the map are scaled version of the above plot)
map.geo.admin.ch
Zoom in
Amplification factors up to 10

## Slide 13
Evaluation of variability of soil response
Estimation of relative amplification factors with reference-site methods:
Perron et. al. (2018)
High background noise level in the city
Low seismicity in Lucerne area
Low number of high-quality earthquake recordings
Problems
using earthquakes recordings | using ambient noise
Standard Spectral Ratios (Borcherdt, 1970) | Standard Spectral Ratios using ambient noise (Kagami, 1982)

## Slide 14
Evaluation of variability of soil response
Estimation of relative amplification factors with reference-site methods:
Perron et. al. (2018)
using earthquakes recordings | using ambient noise
Standard Spectral Ratios (Borcherdt, 1970) | Standard Spectral Ratios using ambient noise (Kagami, 1982)

## Slide 15
Standard spectral ratios using ambient noise (SSRn)
Above f0 - SSRn >> SSR

## Slide 16
Evaluation of variability of soil response
Estimation of relative amplification factors with reference-site methods:
Perron et. al. (2018)
Overestimation of amplification factors
Influence of local sources
Possible variability due to human activities
Etc.
Some problems
using earthquakes recordings | using ambient noise
Standard Spectral Ratios (Borcherdt, 1970) | Standard Spectral Ratios using ambient noise (Kagami, 1982)
Standard spectral ratios – hybrid method by Perron et al. (2018) | 

## Slide 17
Evaluation of variability of soil response
Estimation of relative amplification factors with reference-site methods:
Perron et. al. (2018)
using earthquakes recordings | using ambient noise
Standard Spectral Ratios (Borcherdt, 1970) | Standard Spectral Ratios using ambient noise (Kagami, 1982)
Standard spectral ratios – hybrid method by Perron et al. (2018) | 
Hybrid method:
earthquakes + ambient vibration

## Slide 18
Hybrid standard spectral ratios (SSRh) by Perron et al. (2018)
SSRh SSR

## Slide 19
Ambient noise measurement campaign
map.geo.admin.ch
9 new station installed
SSMNet stations
60 single-station measurements
Performed: 23-25.06.2020

## Slide 20
Relative amplification map (using SSRh)
Relative amplification factors (1.2 Hz)
Relative amplification factors (2.0 Hz)
Reference: rock station HOR01
Ambient noise measurements
Points with earthquake recordings

## Slide 21
Relative amplification map (using SSRh)
Movie

## Slide 22
SSRh – importance of intermediate stations deployment
SSRh function may depend on intermediate station

## Slide 23
SSRh – importance of intermediate stations deployment
Weighted mean
My solution: weighted mean of all intermediate stations

## Slide 24
SSRh – influence of human activities
Differences due to the time when recorded
SSRn:
significant differences
SSRh:
moderate differences
Day recordings and 24h recording – similar SSRh
Assumption:
We can use day recordings
SSR:
earthquakes recordings ->
no differences

## Slide 25
SSRh – influence of human activities
However, differences due to human activities usually within error bars

## Slide 26
SSRh – influence of human activities and deployment
Solutions:
Preliminary analysis using stations for which SSR function is known:
Check the fit between SSR and SSRh amplification functions
Check the influence of the time when you record
Check if there is a difference due to the choice of intermediate station
(not always applicable based on another case study)
+
The more and the more evenly distributed intermediate stations, the better
The longer ambient noise recording (to some extent), the better
Removal of transient part from ambient noise recordings (not checked)

## Slide 27
Conclusions

## Slide 28
Conclusions
Preliminary estimation of relative amplification factors in Lucerne area:
Strong spatial variability of the soil response
High amplification factors in broad frequency range
SSR SSRhybrid
SSRhybrid similar to SSR
Simple and cheap (min. 2 permanent stations + short ambient noise recordings) High spatial resolution
SSRhybrid similar to SSR
Simple and cheap (min. 2 permanent stations + short ambient noise recordings) High spatial resolution
What to remember before using:
Deployment of intermediate stations
Influence of human activities

## Slide 29
References
Bard, P.-Y., 1999. Microtremor measurements: A tool for site effect estimation? Eff. Surf. Geol. Seism. Motion 3, 1251–1279.
Bonnefoy-Claudet, S., Cotton, F., Bard, P.-Y., 2006. The nature of noise wavefield and its applications for site effects studies: A literature review. Earth-Sci. Rev. 79, 205–227. https://doi.org/10.1016/j.earscirev.2006.07.004
Borcherdt, R.D., 1970. Effects of local geology on ground motion near San Francisco Bay. Bull. Seismol. Soc. Am. 60, 29–61.
Ciaccio, M. G. and Cultrera, G.: Terremoto e rischio sismico, Ediesse, Italy, 2014.
Clinton, J., Cauzzi, C., Fäh, D., Michel, C., Zweifel, P., Olivieri, M., Cua, G., Haslinger, F., Giardini, D., 2011. The Current State of Strong Motion Monitoring in Switzerland, in: Earthquake Data in Engineering Seismology. Predictive Models, Data Management and Networks. Springer, pp. 219–233. https://doi.org/10.1007/978-94-007-0152-6_15
Fäh, D., Giardini, D., Kästli, P., Deichmann, N., Gisler, M., Schwarz-Zanetti, G., Álvarez Rubio, S., Sellami, S., Edwards, B., Goertz-Allmann, B., Bethmann, F., Woessner, J., Gassner-Stamm, G., Fritsche, S., Eberhard, D., 2011. ECOS-09 Earthquake Catalogue of Switzerland Release 2011. Swiss Seismol. Serv. ETH Zür.
Field, E.H., Hough, S., Jacob, K.H., 1990. Using microtremors to assess potential earthquake site response: a case study in Flushing Meadows, New York City. Bull. - Seismol. Soc. Am. 80, 1456–1480.
Kagami, H., Duke, C. M., Liang, G. C., Ohta, Y., 1982. Observation of 1- to 5-second microtremors and their application to earthquake engineering. Part II. Evaluation of site effect upon seismic wave amplification due to extremely deep soil deposits. Bull. Seismol. Soc. Am. 72(3), 987–998.
Perron, V., Gélis, C., Froment, B., Hollender, F., Bard, P.-Y., Cultrera, G., Cushing, E.M., 2018a. Can broad-band earthquake site responses be predicted by the ambient noise spectral ratio? Insight from observations at two sedimentary basins. Geophys. J. Int. 215, 1442–1454. https://doi.org/10.1093/gji/ggy355
Poggi, V., Fäh, D., 2016. Guidelines and strategies for seismic microzonation in Switzerland (Report). SED/ ETH Zurich. https://doi.org/10.3929/ethz-a-010735479
Poggi, V., Fäh, D., Burjanek, J., Giardini, D., 2012b. The use of Rayleigh-wave ellipticity for site-specific hazard assessment and microzonation: application to the city of Lucerne, Switzerland. Geophys. J. Int. 188, 1154–1172. https://doi.org/10.1111/j.1365-246X.2011.05305.x