## Slide 1: Suppression of air-sea CO2 transfer by surfactants - direct evidence from the Southern Ocean
Mingxi Yang*1, Timothy J. Smyth1 Vassilis Kitidis1, Ian J. Brown1, Charel Wohl1
Margaret J. Yelland2 Thomas G. Bell1
1. Plymouth Marine Laboratory, UK 2. National Oceanography Centre, UK
*miya@pml.ac.uk

## Slide 2: How is air-sea CO2 flux computed in models? Flux = K ΔC
K : Gas transfer velocity, typically simple function of U10n (10-m neutral wind speed)
∆C : Air-sea concentration difference
Southern Ocean:
large CO2 sink
Climatological Mean CO2 flux , Takahashi et al 2009

## Slide 3: K & wind speed : mean relationship - factor of ~2 discrepancy in high winds - ca. 20% difference in moderate winds
Large discrepancy in low winds too
~U2
~U3

## Slide 4: K & wind speed : variability - wind speed often explains 50-80% of variance in K - what else might control K.. Waves? Bubbles? Surfactants?
Notes: Include mean k vs u here, +Edson

## Slide 5: Impact of surface active organics (surfactants) on gas exchange?
Engel et al. 2017
Organic surfactants present in water column & concentrated near air/water interface
Comprised of carbohydrates, proteins, fatty acids…

## Slide 6: Different types of surfactants probably affect air-sea gas transfer differently
Hydrophobic (‘insoluble’) surfactants form slicks at very low winds
→ act as additional barrier to gas transfer
Hydrophilic (‘soluble’) surfactants
→ suppress small waves/turbulence across a wide range of wind conditions
Engel et al. 2017

## Slide 7: Previous studies of natural surfactant effects on gas transfer
Tank/floating chamber measurements suggest natural surfactants can reduce gas transfer
Gas transfer suppression correlates with surfactant concentration, which can vary by factor of ~10 in surface ocean
Gas transfer measured in tank or chamber might not be representative of real ocean (different turbulence)
Pereira et al. 2018
Atlantic transect

## Slide 8: Direct observation of CO2 flux (by eddy covariance) and K (=flux/ΔC) Novel measurement of Gas Transfer Efficiency (GTE), function of seawater composition ANDREXII cruise Feb-Apr 2019, 11000 km long transect in Southern Ocean (along 60°S)

## Slide 9
Measuring Air-Sea CO2 Flux by Eddy Covariance (EC) Basis: away from Interface, gas transported by turbulent eddies
C: atmospheric CO2 mixing ratio, w: vertical wind velocity
If C’ + when W ’+ (updraft), then F + (net sea-to-air flux)
If C’ + when W ’- (downdraft), then F – (net air-to-sea flux)
Flux averaged to 20-min to account for randomness in turbulence
~ 1 km
Modified from Licor
Further details on motion correction
Further description of Eddy Covariance flux system

## Slide 10: Novel measurement of Gas Transfer Efficiency (GTE) based on partial CO2 equilibration in Segmented Flow Coil Equilibrators – Quantifies impact of varying seawater composition on gas exchange
CO2
analyser
Long coil
Short coil
CO2-free air
Underway seawater
Underway seawater
Fully equilibrated CO2→xCO2w
Partially equilibrated CO2
Gas Transfer Efficiency = xCO2short/xCO2w
More details about the Segmented Flow Coil Equilibrator here
Long & short coils alternately measured every 5 min

## Slide 11: CO2 flux (ANDREXII)
Upwelling
Flux (EC)
ΔfCO2
Southern Ocean mostly a CO2 sink (as expected), but not always

## Slide 12: Gas Transfer Efficiency (GTE) - Range of ~20% during ANDREXII - Bimodal distribution
Gas Transfer Efficiency (GTE) shows large variability and depends on seawater composition
Examples of GTE variability and TS diagram here

## Slide 13: Obs. K (= flux/ΔC): mean relationship and variability - closer to quadratic than to cubic in the mean - wind explains ~60% of variance in K, what about the other 40%?

## Slide 14: GTE explains some of the variability in K K in waters of low GTE tends to cluster below K of high GTE (most obvious at low-to-moderate wind speeds)
Paper submitted to Nature Sci. Rep.

## Slide 15: Clear evidence of lower gas transfer velocity (K) in low gas transfer efficiency (GTE) waters, implying surfactant effect Relative change in K explainable by GTE ~30% at wind speed of 7 m s-1 (~global mean); more pronounced at lower wind speed Similar wind speed dependence to previous lab studies of artificial soluble surfactant (Triton-X 100); similar magnitude to previous field studies of artificial insoluble surfactant (olyel alcohol) Probably because surfactants accumulate more near the interface at low wind speeds

## Slide 16: Very rough estimation of impact of neglecting surfactants in CO2 flux calculation
Wind speed dependence in
surfactant effect
Assume K parametrizations based on dual tracer from many regions (e.g. Nightingale et al 2000) or global radiocarbon (e.g. Wanninkhof 2014) already reflect surfactant effect in the mean (i.e. 30% suppression)
Assume equal presence of both high surfactant and low surfactant waters
Then at wind speed <7 m/s (global mean), using wind-only based K could underestimate surfactant effect & overestimate flux magnitude, and vice versa for high winds
NCEP climatology

## Slide 17: Possible bias in CO2 flux (with minus without wind speed dependence in surfactant effect)
Considering surfactants could lead to a greater CO2 uptake (e.g. in Southern Ocean)
Clearly studies of GTE and surfactant composition in many regions are needed to improve estimates of air-sea CO2 flux
More CO2 uptake
Less CO2 uptake
Less CO2 emission
Based on NOAA CO2 flux (Park et al. 2010)

## Slide 18: Concluding remarks
Mean K vs. wind speed relationship closer to quadratic than cubic during ANDREXII cruise
First Southern Ocean evidence of gas transfer suppression due to natural surfactants
Gas transfer suppression most important relatively at low-to-moderate wind speeds (implications on spatial/seasonal variability in CO2 flux?)

## Slide 19
Flux equipment on the foremast of
James Clark Ross (JCR)
3D Motion sensor (Sysdon Donner MP II)
Heated 3D sonic anemometer (Metek)
CO2 inlet
Picarro CO2 instrument
PCs
See Dong et al 2021 for details on flux processing, QA/QC, and uncertainty estimates

## Slide 20: Use of Segmented Flow Coil Equilibrator to measure Gas Transfer Efficiency
Segmented flow coil equilibrator Wohl et al. Ocean Science 2019
Equilibrated air to gas analyzer
Gas exchanges between air/water segments, kept at ambient water temperature
Gas analyzer: Licor7000 with Nafion dryer
Zero air (no CO2)
25 cm3 min-1
Long coil: 20 m
Short coil: 0.4 m

## Slide 21: Gas transfer efficiency shows substantial variability, but does not obviously correlate with common seawater parameters

## Slide 22: Motion correction Example…

## Slide 23: Measured 3-D wind velocities
Large variations in wind velocities at the time scales of waves (7-10 seconds)
Need to remove ship’s motion from measured wind velocities to obtain true wind velocities

## Slide 24: Ship Motion (Linear Acceleration & Angular Rotation)

## Slide 25: True Wind Velocity = Measured Wind Velocity − Ship Velocity
Ship Velocity = Integrated Ship Acceleration

## Slide 26
Ship motion signal no longer apparent in corrected vertical wind velocity (W)

## Slide 27: Verification of Motion Correction
Variance (power) spectra of W (vertical wind velocity) and U (horizontal wind velocity)
Cospectrum of UW
Spurious peak at ~0.2 Hz due to ship’s motion removed
Covariance of UW negative (as expected for air-sea momentum transfer)
Frequency (Hz)
F x Co(U,W)
Log(F x PUU) & Log(F x Pww)