## Slide 1: Simulation study on gravity field determination with small satellites in NGGM
April 30, 2021
Nikolas Pfaffenzeller, Roland Pail (Technical University of Munich)
EGU 2021

## Slide 2: Motivation
Aspects in NGGMs consideration:
  increase of spatio-temporal resolution
  reduction of temporal aliasing
  Acceptable cost effort for dedicated mission
Possible concept: multi-constellations of small satellites (DFG Project „CubeGrav“)
 Miniaturization of satellites and of (gravity-relevant) instrument components necessary
 What is the impact of instrument errors on gravity field solutions?
 What is the impact of different satellite formations and constellations on gravity field solutions?

## Slide 3: Simulation environment
Inter-satellite ranging: Laser Ranging Interferometer
State-of-the art in NGGM concepts like MAGIC Project (Haagmans et al. 2020)
Used in all investigated scenarios
Gravity Field processing:
Full scale numerical closed loop simulations
Simulated instrument errors

## Slide 4: Accelerometer Performance
Electrostatic Accelerometer with state-of-the art NGGM performance (Haagmans et al. 2020)
MEMS accelerometer (Wu et al. 2020)
Optomechanical accelerometer (Hines et al. 2020)

## Slide 5: Simulations
Investigation period: 1 month
Variation of the
Number of satellites
Number of inter-satellite links (single, multi ISL)
Instrument performance (noise level)
Orbit parameters
Solution approach (Co-Parametrization of short periodic temporal gravity fields = “Wiese”) Wiese et al. 2011
Single inter-satellite links = links between adjacent satellites (1-2, 2-3, …) Multi inter-satellite links = links from each respective satellite to all other satellites
Temporal aliasing models
HIS signal + errors of AO and difference of two ocean tide models (FES2004 – EOT08a) used as errors

## Slide 6: Configurations
case | Altitude [km] | Inclination [°] | Inital condition
 | 439 | 89 | 
 | 334 344 | 89 70 | 
 | 439 410 | 89 70 | 
 | 439 410 | 89 70 | 
 | 370 407 445 | 89 80 70 | 
X… number of satellite pairs / satellites forming a chain per orbit forming a chain Y… number of orbits
Z… number of chains per orbit
Repeat cycle: 17 days
Inter-satellite distance: ~ 200 km
Single and mutli inter-satellite links
Notes: Bei Bender: Drift vorhanden -> optimalere Abdeckung

## Slide 7: Configurations
Impact analysis of 18 polar satellite pairs distribiuted on
One orbit plane
Various orbit planes
case | Altitude [km] | Inclination [°] | Inital condition
 | 439 | 89 | 
 | 439 | 89 | 

## Slide 8: simulation results – impact of different instrument noise level
MEMS noise dominates the gravity solution whereas the temporal signal can be detected when using the electrostatic or optomechanical accelerometer

## Slide 9: simulation results – impact of different instrument noise level
Detail view without MEMS sensor : overall performance of optomechanical accelerometer comparable to electrostatic accelerometer, in particular for Bender constellation
Degradation in scenarios

## Slide 10: Comparison SH coefficients electrostatic and optomechanical accelerometer
Lower performance of optomechanical accelerometer
 Impact on sectorial coefficients and striping pattern
 Impact on higher degree and order

## Slide 11: Simulation result
Observations from inclined orbits essential for improved performance
Benefit of multiple satellite pairs on either one or several orbit planes lower than observation from inclined orbits
Multiple satellites links increase only redundancy

## Slide 12: Simulation Results – Co-Estimation of 2 d gravity field solutions
All scenarios are able to resovle two-daily gravity fields
Observations from inclined orbits and simultaneously a higher amount of satellites (pairs) perform the best

## Slide 13: Simulation Results – Co-Estimation of 1 d gravity field solutions
Performance degradation of all scenarions except for when estimating daily gravity field estimates (same d/o than for two daily solutions)

## Slide 14: Simulation Results – Co-Estimation of 0.5 d gravity field solutions
Co-parametrization of half-daily estimates improves overall solutions when having sufficient observations, meaning scenarios

## Slide 15: Simulation Results – Co-Estimation of 0.25 d gravity field solutions
Only scenario is able to resolve quarter daily gravity fields and keep the overall solution stable
Low performance of remaining configurations in low d/o but stable behaviour in d/o above co-parametrization limit

## Slide 16: Conclusions
Co-estimation of short periodic gravity fields down to 0.25 d possible for multi-satellite constellations
Miniaturized optomechanical accelerometer suitable for a potential CubeSat gravity mission whereas performance of presented MEMS sensor too low
Importance level of different criteria for NGGMs:
  Observations from different inclined orbits
  Spatial distribution of the satellites
  Amount of satellite pairs
  Amount of inter-satellite links
Further investigations:
  Shorter-term gravity field parametrization (6 hours, …)
  Co-parameterization of ocean tides  high potential due to multiple satellites and increased temporal resolution
  Orbit Constellation regarding optimal ground track coverage

## Slide 17: References
DFG Project “CubeSat-Netzwerke für geodätische Erdbeobachtung am Beispiel der Schwerefeldbestimmung” (CubeGrav)
Haagman, R & Tsaoussi, L & Massotti, L & March, G & Dara, I, Next Generation Gravity Mission as a Mass-change And Geosciences International Constellation (MAGIC) Mission Requirements Document
Wiese, D. & Visser, Pieter & Nerem, Robert. (2011). Estimating low resolution gravity fields at short time intervals to reduce temporal aliasing errors. Advances in Space Research - ADV SPACE RES. 48. 1094-1107. 10.1016/j.asr.2011.05.027.
A. Hines, L. Richardson, H. Wisniewski, and F. Guzman, "Optomechanical inertial sensors," Appl. Opt. 59, G167-G174 (2020).
W. Wu et al., "Measurement of Tidal Tilt by a Micromechanical Inertial Sensor Employing Quasi-Zero- Stiffness Mechanism," in Journal of Microelectromechanical Systems, vol. 29, no. 5, pp. 1322-1331, Oct. 2020, doi: 10.1109/JMEMS.2020.3001928