## Slide 1: Japan’s L-SAR missions
Shin-ichi Sobue
Sobue.shinichi@jaxa.jp
ALOS-2 Project manager
Japan Aerospace Exploration Agency (JAXA)
April 29, 2021

## Slide 2: Japanese L-band SAR Satellites – 25-year Legacy
ALOS
(2006-2011)
ALOS-2
(2014- )
JERS-1
(1992-1998)
Improvement of Data Acquisition Abilities

## Slide 3
Application | Disaster, Land, Agriculture, Natural Resources, Sea Ice & Maritime Safety
L-band SAR (PALSAR-2) | Stripmap: 3 to 10m res., 50 to 70 km swath ScanSAR: 100m res., 350km/490km swath Spotlight: 1×3m res., 25km swath
Orbit | Sun-synchronous orbit Altitude: 628km Local sun time : 12:00 +/- 15min Revisit: 14days Orbit control: ≦+/-500m
Life time | 5 years (target: 7 years)
Launch | May 24, 2014; H-IIA launch vehicle
Downlink | X-band: 800Mbps(16QAM) 400/200Mbps(QPSK) Ka-band: 278Mbps (Data Relay)
Experimental Instrument | Compact InfraRed Camera (CIRC) Space-based Automatic Identification System Experiment 2 (SPAISE2)
Advanced Land Observing Satellite-2
Notes: ALOS-2 carries L-band Synthetic Aperture Radar called PALSAR-2.
The local sun time is at noon in order to complement other SAR satellites which are in dawn-dusk orbits. The revisit time is shortened from that of ALOS and the orbit is controlled within 500m tube for interferometry.
The observation data is transmitted either directly to a ground station via X-band at 800Mbps or through inter-satellite communication via Ka-band at 278Mbps.
ALOS-2 will contribute to Disaster monitoring, Land monitoring, Agricultural monitoring, Natural Resource Exploration and Global Forest monitoring as ALOS did.
And potential use such as maritime safety will be expected.

## Slide 4: ALOS-2 Observation Modes
70°
8°
350 km
or 490 km
25 km x 25km
70°
50 or 70km
Observable area
Approx. 1160km
ScanSAR
Spotlight
Strip map
8°
Newly added observation mode
for ALOS-2
Flight Direction
Non-observable area
Approx. 80km
Nadir Track
Right & Left Looking
Wide Incidence Angle: 8～70°

## Slide 5
5
Earthquake
Ice
Disaster monitoring
Environment and land management
Volcano
Forest and wetland
Agriculture & natural resources
Ocean
Flooding
ALOS-2 Mission Objectives
Oil Spill

## Slide 6: Monitoring Deforestation
JJ-FAST website （http://www.eorc.jaxa.jp/jjfast//jj_index.html）
Monitoring forests in 77 countries
Data source | ALOS-2/PALSAR-2 (ScanSAR mode)
Target area | 77 countries
Update | Every 1.5 months
JICA-JAXA Forest Early Warning System in the Tropics (JJ-FAST)
Red indicates the latest Deforest Point
Yellow indicates all Deforest Point

## Slide 7: CEOS 2019 VNSC chair initiative
Cross comparison among rice crop growth map of Mekong region by VNSC, JAXA and GEORICE by ALOS-2 and S1 in cooperation with respecting countries (space agencies and ministries of agriculture) under APRSAF SAFE and other regional framework
-> Continue to support CEOS 2020 chair activities
ALOS-2/INAHOR
Rice crop maps (crop season product) of the Mekong area (Cambodia, Laos, Thailand, Vietnam) linked with ESA GEORice, JAXA and GEO GEOGLAM Asia Rice team
Rice Phenology / Growth Stage (monthly product) of the Mekong Delta and Red River Delta, Vietnam.
Rice Crop Production / Yield Estimation (crop season product) of provinces in the Mekong Delta and Red River Delta, Vietnam.
Continued development of GEOGLAM National Crop Monitor with NASA Harvest.
GEORICE
VNSC/S1
ALOS-2/ INAHOR
GEORICE /S1

## Slide 8: Continuous Observations by ALOS Series
JFY 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
ALOS-2 (L-SAR)
ALOS-3 Follow-on
(Under Consideration)
ALOS-4 Follow-on
(Under Consideration)
Mission Operation (7 years)
Mission Operation (7 years)
Post-mission Operation
Launch
Assurance of safety and security of citizens, i.e. disasters monitoring and management, land deformation monitoring, national developing management, foods and natural resources, environmental issues in global etc.
Enhancement of commercial use of Earth observation data, i.e. National Spatial Data infrastructure (NSDI) and new applications.
Mission Operation
(5 years)
ALOS-3 (Optical)
ALOS-4 (L-SAR)
Development
Development

## Slide 9: ALOS-4 Overview
Launch | JFY2022~ by H3 launch vehicle
Orbit | Same orbit as ALOS-2 Sun-synchronous sub-recurrent orbit Altitude: 628 km Inclination angle: 97.9 degree Local sun time at descending: 12:00 ± 15 min. Revisit time: 14 day (15-3/14 rev/day)
Lifetime | 7 years
Size | X 10.0 m x Y 20.0 m x Z 6.4 m
Satellite Mass | ~2,990 kg
Downlink | 1.8/3.6 Gbps (Ka-band)
Mission Instruments | PALSAR-3 (Phased Array type L-band Synthetic Aperture Radar-3) SPAISE3 (SPace based AIS Experiment 3)
Prime contractor | Mitsubishi Electric Corporation
PALSAR-3 antenna
Ka-band DT antenna
SPAISE3
antenna
Solar array paddle
Y
X
Z

## Slide 10: ALOS-4 Mission Objectives
Precise monitoring of land deformation and subsidence using InSAR
Continuation and enhancement of ALOS-2 mission (all-weather disaster monitoring and forest monitoring, etc.)
Exploring new applications such as large infrastructure monitoring using InSAR time series analysis
Marine monitoring by SAR and Automatic Identification System for ships (AIS)
10

## Slide 11: PALSAR-3 Observation mode
Swath width of PALSAR-3/2
Modes | PALSAR-3 | PALSAR-2
Stripmap (res. 3/6/10 m) | 100-200 km | 30-70 km
ScanSAR (res. 25m*) | 700 km | 350-490 km
Spotlight (res. 1 x 3 m) | 35km×35km | 25km×25km
*single look
Right observation
Maximum :1160km
Left observation
Maximum : 1160km
Azimuth direction
8 deg
70 deg
30 – 56 deg
Spotlight
ScanSAR
Stripmap

## Slide 12: ALOS-4 Mission Objectives
Precise monitoring of land deformation and subsidence using InSAR
More frequent observation
  High resolution + wide swath width
Mutual interference with PALSAR-2
  The same orbit and observation geometry as ALOS-2
Orbit control is performed autonomously and its accuracy is within +/- 500 meters.
Improved orbit determination accuracy
  ~3 m (RMS) for onboard orbit
  ~0.1 m (RMS) for offline orbit
Coverage over Hawaii island
200 km swath
ALOS-4/PALSAR-3
50 km swath
ALOS-2/PALSAR-2

## Slide 13
 |  | CY 2020 |  |  |  | CY 2021 |  |  | 
 |  | 1Q Jan Mar | 2Q Apr Jun | 3Q Jul Sept | 4Q Oct Dec | 1Q Jan Mar | 2Q Apr Jun | 3Q Jul Sept | 4Q Oct Dec
ALOS | AVNIR-2 (10 m) |  |  |  |  |  |  |  | 
 | PALSAR FBS, FBD (10 m) |  |  |  |  |  |  |  | 
ALOS-2 | PALSAR-2 ScanSAR (25m) |  |  |  |  |  |  |  | 
Data Processing
Data Processing (L1.1 + L2.1 (L2.2))
Data Processing
Global
Global (L1.1+
L2.2)
Preparation
Data Distribution (O&F)
Data Distribution (Open and Free)
ALOS/ALOS-2 mass processing for O&F