## Slide 1
Hydrogeological controls on stream discharge dynamics in bedrock catchments: exploring the combined effects of seepage development and heterogeneity
Nicolas Cornette (Géosciences Rennes)
Jean-Raynald de Dreuzy (Géosciences Rennes)
Alexandre Boisson (BRGM)
Clément Roques (Géosciences Rennes)
Guillaume Pajot (OSUR)
Josette Launay (CRESEB)
Léguer Amont : Eco-bretons.info

## Slide 2
Characterization of the water resource on a regional scale
Quantitative aspect: Flows (streamflow, piezometry, …).
Introduction
Methods
Conclusion
Results

## Slide 3
Characterization of the water resource on a regional scale
Quantitative aspect: Flows (streamflow, piezometry, …).
Streamflow series :
  Watershed scale.
  Wide spatial and temporal range.
  Readily available.
  Integrates information about surface as well as underground environment.
Nancon watershed (1990-2009)
Introduction
Methods
Conclusion
Results

## Slide 4
Within a region, there is a significant variability in river dynamics
Arguenon watershed
Horn watershed
Introduction
Methods
Conclusion
Results
Jan.
Mar.
May
Jul.
Sep.
Nov.
Jan.
Jan.
Mar.
May
Jul.
Sep.
Nov.
Jan.

## Slide 5
What are the processes and factors that will control this variability of hydrological response ?
Arguenon watershed
Horn watershed
Introduction
Methods
Conclusion
Results
Jan.
Mar.
May
Jul.
Sep.
Nov.
Jan.
Jan.
Mar.
May
Jul.
Sep.
Nov.
Jan.

## Slide 6
Water cycle in a crystalline aquifer context
Introduction
Methods
Conclusion
Results
Infiltration
Runoff
Evapotranspiration
Seepage
Deep flow
Precipitation

## Slide 7
Water cycle in a crystalline aquifer context
Introduction
Methods
Conclusion
Results
Infiltration
Runoff
Evapotranspiration
Seepage
Deep flow
Precipitation
Surface flow
Subsurface flow

## Slide 8
Water cycle in a crystalline aquifer context
Limited aquifer capacities
Low permeability
Introduction
Methods
Conclusion
Results
Infiltration
Runoff
Evapotranspiration
Seepage
Deep flow
Precipitation
Surface flow
Subsurface flow

## Slide 9
Water cycle in a crystalline aquifer context
Limited aquifer capacities
Low permeability
Promote surface/subsurface interactions
Introduction
Methods
Conclusion
Results
Ogden and Watts., 2000; Tromp-van Meerveld and McDonnell., 2006; Wenninger et al., 2004, …
Infiltration
Runoff
Evapotranspiration
Seepage
Deep flow
Precipitation

## Slide 10
Water cycle in a crystalline aquifer context
Limited aquifer capacities
Low permeability
Aim : Investigating the combined effects of surface/subsurface interactions and geological heterogeneity in a crystalline basement region under temperate climate
Promote surface/subsurface interactions
Ogden and Watts., 2000; Tromp-van Meerveld and McDonnell., 2006; Wenninger et al., 2004, …
Introduction
Methods
Conclusion
Results

## Slide 11
Application on Brittany
Arguenon watershed
Nancon watershed
Introduction
Methods
Conclusion
Results

## Slide 12
Application on Brittany
Global dynamic on a regional scale based on flow data
Introduction
Methods
Conclusion
Results

## Slide 13
Application on Brittany
Global dynamic on a regional scale based on flow data
Subsurface flow simulation at the hillslope scale
hs1D model (Quentin Courtois)
Introduction
Methods
Conclusion
Results

## Slide 14
w
x
Winter et al., 1998
A topographic profile is associated with each hillslope
Equivalent hillslope: Average topographic profile of all hillslopes.
Introduction
Methods
Conclusion
Results

## Slide 15
w
x
Winter et al., 1998
A topographic profile is associated with each hillslope
Simulation of groundwater flow and seepage processes at the hillslope scale in 1D using Boussinesq equations (1877)
Marçais et al., 2017
Equivalent hillslope: Average topographic profile of all hillslopes.
Introduction
Methods
Conclusion
Results

## Slide 16
Calibration by a systematic parameter space exploration
Infiltration (SURFEX)
River
1. Boussinesq flow
Saturated zone
Unsaturated zone
K, θ.D
Homogeneous geology
2. Seepage
Runoff (SURFEX)
Parameter space exploration :
Hydraulic conductivity (K)
  10-4 à 10 m/h; n = 50
Porosity x Aquifer depth (θ.D)
  0 à 15 m; n = 50
Objective function :
Introduction
Methods
Conclusion
Results

## Slide 17
Incorporating hydraulic heterogeneity
Equivalent hillslope 1
Contribution : 50%
Equivalent hillslope 2
Contribution : 50%
K1, θD1
K2, θD2
Q1
Q2
QT = Q1 + Q2
Heterogeneous geology
Introduction
Methods
Conclusion
Results

## Slide 18
Nancon watershed
Best model distribution :
Selection criteria:
The ratio of hydraulic conductivities shows a heterogeneity of 2 orders of magnitude within the Nançon watershed.
The homogeneous model ( allows to describe the streamflow series.
Introduction
Methods
Conclusion
Results

## Slide 19
Arguenon watershed
Best model distribution :
Selection criteria :
The ratio of hydraulic conductivities shows a heterogeneity of 4 orders of magnitude within the Arguenon watershed.
The homogeneous model( does not allows for the description of streamflow series.
Introduction
Methods
Conclusion
Results

## Slide 20
Best model distribution :
Selection criteria :
The simulation of subsurface flows with 2 hydraulic parameters (1 equivalent hillslope) and 4 hydraulic parameters (2 equivalent hillslopes) allows describing the streamflow series with values of 0.72 et 0.80 respectively.
Incorporating hydraulic heterogeneity induces a 11% increase in the value of the .
Flood peaks and seasonal recessions are well described by the model even if extreme low flows, as in 2003, are underestimated.
Nancon watershed
Introduction
Methods
Conclusion
Results

## Slide 21
Best model distribution :
Selection criteria :
The simulation of subsurface flows with 2 hydraulic parameters (1 equivalent hillslope) and 4 hydraulic parameters (2 equivalent hillslopes) allows describing the streamflow series with values of 0.54 et 0.78 respectively.
Incorporating hydraulic heterogeneity induces a 44% increase in the value of the .
Flood peaks and seasonal recessions are well described by the heterogeneous model whereas homogeneous model only describes the flood peaks.
Arguenon watershed
Introduction
Methods
Conclusion
Results

## Slide 22
hs1D model with only 4 parameters allows describing the streamflow series on Nançon and Arguenon watersheds with NSElog values of 0.80 and 0.78 respectively.
Incorporating hydraulic heterogeneity induces a 44% increase of NSElog value in the Arguenon watershed. This improvement is not systematic at the regional scale (Nancon watershed).
This improvement is reflected by a distributional change of the flow during the year.
Differences between catchments hints on the potential identification of hydrogeological properties at the regional scale by the combined use of geological map and hydrographs.
Introduction
Methods
Conclusion
Results