## Slide 1
Snow Falling on Alpine Lakes
Hamish Pritchard*, Daniel Farinotti° and Steven Colwell*
*British Antarctic Survey °WSL, Switzerland
Measuring snowfall SWE on the landscape scale using lake water pressure
1. We’re getting snowfall wrong
2. We need better measurements
3. Here’s a new way
4. It works!
5. Summary
EGU21-7507

## Slide 2
1) The problem: we’re getting mountain snowfall wrong
Mountain snowfall biases are a global problem
WorldClim v2
Winter
Bias-correction factor for precipitation
WorldClim v2
Summer
(June-July-August mean)
Slide summary:
Mountain snowfall is not observed well enough…
…even where there are lots of weather stations (like in the western US).
Bias-correction factor: PBCOR for WorldClim v2, Beck et al. (2020) Bias correction of global high-resolution precipitation climatologies using streamflow observations. Weather stations: selected Global Historical Climatology Network stations located in mountains where January or July mean temperature is below freezing. Mountains: as defined by Karagulle et al. (2017) Modeling global Hammond landform regions from 250‐m elevation data.
Summer precipitation amounts are biased by this much
WorldClim v2
Winter
(December-January-February mean)
x Weather station in the
mountain cryosphere
The greatest biases are in the mountains in winter
CHELSA v1.2
Winter
CHPclim v1
Winter
…and other climatologies have the same problem
EGU21-7507
Notes: Full Beck ref: Beck HE, Wood EF, McVicar TR, Zambrano-Bigiarini M, Alvarez-Garreton C, Baez-Villanueva OM, et al. Bias Correction of Global High-Resolution Precipitation Climatologies Using Streamflow Observations from 9372 Catchments. J Clim. 2020;33(4):1299-315.
Shows GloH2O’s PBCOR for WorldClim v2 climatologies in June-July-August (left) and December-January-February (right), with the GHCN Daily stations located in the mountain cryosphere as black crosses. Shows widespread precip low bias in mountains, worse in winter than summer. Note also that gridded products CHELSA v12 and CHPClim v1 have similar biases.
Shows that mountain precip, and particularly snowfall, are not adequately represented in leading gridded products even in Western States where observations are relatively dense.

## Slide 3
Manual observations of SWE (Snow Water Equivalent) - infrequent
too few (difficult, expensive to install and maintain)
too biased (undercatch, sensor saturation etc.)
Other SWE gauges – rare, expensive, range or bias problems
pillow
$17,000
scales
$28,000
gamma
impedance
$34,000
cosmic ray
$21,000
$27,000
Most importantly: too small! (point measurements)
>$7000
Pluviometers – often biased
Fences and bushes reduce wind bias but are rarely used.
WMO reference station
2) What’s wrong with existing snowfall observations?
Lots of options:
EGU21-7507

## Slide 4
3) There is another way - use lakes to measure snowfall SWE
Accuracy advantages
b) no bias from wind ‘undercatch’ (submerged sensor)
c) no bias from ‘bridging’ (larger than pillows)
d) no bias from sensor ‘saturation’ (large range, e.g. 10 m WE)
e) no need to guess density etc. (direct measurement of mass = SWE)
Practicality advantages
a) low cost, low power, lightweight, easy to deploy, simple, robust
Pritchard HD et al. (2021) Measuring Changes in Snowpack SWE Continuously on a Landscape Scale Using Lake Water Pressure. J. Hydrometeorology. 22(4):795-811.
Find a lake
water pressure
summer
winter
Add a water-pressure sensor
Wait for winter (runoff stops)
P+
Falling snow increases pressure
And repeat
EGU21-7507

## Slide 5
EGU21-7507
Lake Tomasee, Switzerland (alt. 7700 ft), source of the River Rhine.
NB/ Tomasee is 1.25 million times larger than the AWS pluviometer.
Winter 2018/19 water-pressure from Tomasee, and precipitation from nearby AWS
Correcting for lake drainage to get snowfall SWE:
..to get snowfall SWE and its uncertainty e.g.:
= 7.3 ± 0.3 mm W.E.
(± 4%)
4) Using lakes to measure snowfall SWE: Swiss Alps
Precision advantages
f) uncertainty quantified from the observations
Pritchard HD et al. (2021) Measuring Changes in Snowpack SWE Continuously on a Landscape Scale Using Lake Water Pressure. J. Hydrometeorology. 22(4):795-811.
…and correct for drainage…
Measure the pressure rise…

## Slide 6
Lake Orajärvi: 10.95 km2
(274 million times larger than the nearest pluviometer)
AA
AA = AROME-Arctic 2.5 km weather model
It works on big lakes too: Finnish Arctic
5. Summary
Existing snow measurements are too sparse, too poorly distributed, too infrequent, too biased and too small to represent snowfall SWE in mountain landscapes.
Snowfall SWE can instead be measured using lake water pressure.
This has important advantages in accuracy, practicality, precision and sampling over existing instruments.
Sampling advantages of a lake sensor
g) no need to scale-up from point measurements (lakes can be as big as grid cells)
h) very large potential sample (e.g., 25,000 mountain lakes just in the contiguous USA)
Pritchard HD et al. (2021) Measuring Changes in Snowpack SWE Continuously on a Landscape Scale Using Lake Water Pressure. J. Hydrometeorology. 22(4):795-811.
Patent pending: PCT/GB2021/050398
big lake vs
tiny AWS
EGU21-7507