## Slide 1: Impact of NTSL on LLR observatories and on the estimation of EOPs
V.V. Singh1,2, L. Biskupek1, J. Müller1, M. Zhang1,3,4
1 Institute of Geodesy (IfE), Leibniz University Hannover, Germany
2 Institute for Satellite Geodesy and Inertial Sensing, German Aerospace Center (DLR) , Germany
3 State Key Laboratory of Geodesy and Earth's Dynamics, Institute of Geodesy and Geophysics, APM, Chinese Academy of Sciences, China
4 College of Earth and Planetary Sciences, University of Chinese Academy of Sciences , China
NTSL: Non-tidal station loading
LLR: Lunar Laser Ranging
EOP: Earth Orientation Parameters

## Slide 2: Principle of LLR
Laser pulse from telescope on Earth to reflector on Moon
Measurement of round-trip travel time
Space segment
Five retroreflectors
Ground segment
Laser
Detector
Clock
[Murphy, 2013]
LLR helps in (but isn’t limited to):
defining coordinate systems & estimating tidal parameters for the Moon
testing relativistic parameters
estimating Earth Orientation Parameters
Murphy, T. W.: Lunar laser ranging: the millimeter challenge, 2013, Reports on Progress in Physics 76

## Slide 3: LUNAR Software Package
Standard model follows IERS 2010 conventions:
  Tidal atmospheric loading (TAL)
  Tidal ocean loading
  Solid Earth tides
  Deformation due to polar motion
  Ocean pole tides
  Tropospheric delay
Non-tidal loading (NTL) not recommended by IERS
LLR observations possible only on clear sky conditions = high atmospheric pressure = TAL + NTAL (non-tidal atmospheric loading)
Blue sky effect due to NTAL
NTL effect also due to redistribution of masses in oceans (NTOL) and groundwater (HYDL)
Within the data modelling in parameter estimation:

## Slide 4: Results: Station Coordinates and Annual Signal
% change in WRMS for GFZ and IMLS NTSL solutions compared to the standard solution for all LLR stations
Post fit residuals, OCA station, 08.08.2012 05.10.2018, 5375 NPs
NPs: Normal points
Std: Standard
For details, refer Singh et. al (2021)
NTSL effect:
Improvement (smaller values) in LLR residuals with IMLS NTSL
Reduced annual signal at OCA station

## Slide 5: Results: EOP determination*
values obtained from the standard solution
Absolute changes to values of the standard solution upon addition of the IMLS NTSL solution and the uncertainty of values of the standard solution
NTSL effect:
Depends on number of NPs, nights, stations
Not significant compared to uncertainty
*For OCA IR data, 232 nights (> 10 NPs per night)

## Slide 6: Conclusions
NTSL (all loadings) added to LLR analysis from IMLS and GFZ from 1980 – present
EOP determination (this study, UT only) from LLR as corrections to IERS C04 series
  Corrections for 232 nights (nights with > 10 NPs per night)
  Range of corrections ±150 𝜇s (standard solution)
  Uncertainty of corrections up to 60 𝜇s
    Mean (uncertainty of corrections) = 17.79 𝜇s, Std. dev. = 10.17 𝜇s
Effect of NTSL on corrections (compared to standard solution) ±60 𝜇s
  NTSL effect less than uncertainty (of standard solution) for 71.55% nights (IMLS) and 78.02% nights (GFZ)
    IMLS: Mean* = 12.18 𝜇s, Std. dev.* = 11.44 𝜇s
    GFZ: Mean* = 9.94 𝜇s, Std. dev.* = 8.52 𝜇s
  Not recommended to be added for EOP determination
UT determination: LLR to verify VLBI results
*of absolute change when adding NTSL in UT calculation, compared to standard solution
Std. Dev.: Standard Deviation

## Slide 7: References and Acknowledgement
Biskupek, L. (2015).Bestimmung der Erdorientierung mit Lunar Laser Ranging. Ph.D. thesis Leibniz University Hannover. https://doi.org/10.15488/4721
Singh, V.V., Biskupek, L., Müller, J., & Zhang, M. (2021).Impcat of non-tidal station loading in LLR. Advances in Space Research. https://doi.org/10.1016/j.asr.2021.03.018
Current LLR data are collected, archived, and distributed under the auspices of the International Laser Ranging Service (ILRS) (Pearlman et al., 2019).
This research was funded by the German Aerospace Center's (DLR) Institute for Satellite Geodesy and Inertial Sensing, and Deutsche Forschungsgemeinschaft (DFG, German Research Foundation) under Germany’s Excellence Strategy EXC 2123 QuantumFrontiers, Project-ID 390837967. Further financial supports were from the Strategic Priority Research Program of the Chinese Academy of Sciences (grant nos. XDB23030100 and XDA15017700) and the National Natural Science Foundation of China (project no. 41704013).
Pearlman, M. R., Noll, C. E., Pavlis, E. C., Lemoine, F. G., Combrink, L.,Degnan, J. J., Kirchner, G., & Schreiber, U. (2019). The ILRS: approaching20 years and planning for the future. Journal of Geodesy,93(11), 2161–2180. doi:10.1007/s00190-019-01241-1.

## Slide 8
Thank you!