## Slide 1: Characterizing temporary stream dynamics: the Stream Length Duration Curve Nicola Durighettoa, Alfonso Senatoreb, and Gianluca Bottera a Dept. of Civil, Architectural and Environmental Engineering, University of Padua (ITALY) b Dept. of Environmental Engineering, University of Calabria (ITALY)
www.erc-dynet.it

## Slide 2
River networks are highly dynamical
in response to rainfall events
More than 50% of the global river network is temporary
Temporary Streams: streams that temporarily cease to flow
Durighetto and Botter, HPEye 2021

## Slide 3
Biological dispersion
Nutrient spiraling
CO2 outgassing
Water and sediment transport
River networks act as ecological corridors & biological hotspots by promoting:
Rinaldo et al. PNAS (2018)
Kiel & Cardenas, Nature (2014)
Minshall et al., The American Naturalist (1985)
Therefore, river shape and length are key factors that regulate ecosystem function
Notes: functioning.

## Slide 4
1
Creation of new observational datasets to overcome the limited availability of empirical data about network dynamics
2
Development new theoretical tools to enable a quantitative characterization of network dynamicity and an objective comparison of temporary streams
Research objectives

## Slide 5
Chart: Precipitation [mm]
| JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC
mm/month | 54.7455 | 74.1273 | 80.6182 | 95.2727 | 137.5818 | 129.5273 | 146.9818 | 155.6727 | 110.4545 | 146.8182 | 161.3818 | 84.4
°C | -2.9 | -1.3 | 2.4091 | 6.8818 | 10.4545 | 15.0273 | 16.8818 | 16.4 | 12.2455 | 7.2364 | 2.2727 | -1.7818
Alpine climate: short rainy summers, cold winters with snow
Catchment area: 5.3 km2
The Valfredda catchment
Land cover: debris deposits and pastures in the upper part, forest in the lower part
Elevation: from 1500 to 3000 m asl
Spring
Summer
Autumn
Winter
Durighetto et al., WRR 2020

## Slide 6
28 surveys since summer 2018
By walking along the river network and collecting gps coordinates of the points where surface flow starts/stops
Active
Dry
a
b
Active length ranges from 5.8 km (a) to 13.3 km (b)
72% of the network length is temporary
Water presence sensors were employed in 2019
Zanetti et al., HESSd 2021
Zanetti et al. Friday, 14:05

## Slide 7
Chart: Precipitation [mm]
| JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC
mm/month | 54.7455 | 74.1273 | 80.6182 | 95.2727 | 137.5818 | 129.5273 | 146.9818 | 155.6727 | 110.4545 | 146.8182 | 161.3818 | 84.4
°C | -2.9 | -1.3 | 2.4091 | 6.8818 | 10.4545 | 15.0273 | 16.8818 | 16.4 | 12.2455 | 7.2364 | 2.2727 | -1.7818
Mediterranean climate: hot dry summers, mild wet winters
Catchment area: 7.0 km2
The Turbolo catchment
Land cover: forest and pasture, with agriculture areas
Elevation: from 180 to 1000 m asl
Senatore et al., ESSOAr 2020

## Slide 8
77 surveys since April 2019
In two subcatchments (east and west), for a total of 100 ha
Active length ranges from 0 km to 5.14 km
All the network is temporary: complete dry-down of the streams during summer
Temporary network
Dry network

## Slide 9
How to quantitatively summarize active length dynamics and compare different catchments?
The Stream Length Duration Curve

## Slide 10
Concept: The stream length duration curve (SLDC)
Is the analogous to the flow duration curve
Shows the relative fraction of time for which each possible length of the active network is equaled or exceeded
Summarizes the temporal dynamics of the active length of the whole river network
Duration [%] = PL(L)
Botter and Durighetto, WRR 2020

## Slide 11
Definition: the stream length duration curve (SLDC) as the inverse function of the exceedance probability of the active length
Probability density function (PDF)
Exceedance cumulative distribution function (CDF)
STREAM LENGTH DURATION CURVE
The exceedance probability can be interpreted as duration

## Slide 12
Steepness of the curve is proportional to network dynamicity
Dry periods
Dry periods
Wet periods
Dry periods
Temporary length
Perennial length
Small slope: limited dynamics
High slope: enhanced dynamics
Intercept: stream dries out completely
High slope: very dynamic when active
Sudden drop: expanded-contracted network transition
Wet periods
Intersection with X-axis if the network dries down completely
Presence of plateaus if a specific length lasts for extended periods
Description: the stream length duration curve (SLDC) effectively summarizes many properties of stream network dynamics

## Slide 13
1
Results

## Slide 14
5.8 km permanent length
Enhanced dynamics (higher slope) for the wettest and driest periods
1
3
Limited dynamics for network lengths between 9 and 10 km
2
1
2
3
14.6 km max length
1
3
The SLDC of the Valfredda

## Slide 15
Pronounced seasonality: dry for > 50% of the time
Plateaus at about 1km of active length
2
3
1
2
3
Enhanced dynamics in the wet period (high slopes of the SLDCs)
1
The SLDC of the Turbolo

## Slide 16
The dynamics of the Valfredda network are limited when compared to the Turbolo (lower slope)
1
3
2
The plateaus in the Turbolo SLDCs have the same drainage density of the central part of the Valfredda SLDC
2
3
Comparing the drainage density duration of the catchments
Despite being perennial, the Valfredda has the lowest maximum drainage density
1

## Slide 17
5
4
3
2
1
The SLDC integrates the dynamics of the whole upstream catchment
Downstream
The SLDC is more stable than other point-wise properties, such as zero-flow duration, with respect to the spatial scale it refers to
A further note about the SLDC
Similar slope
But increasing perennial length

## Slide 18: CONCLUSIONS 1) The SLDC efficiently summarizes the dynamics of the active network 2) The SLDC enables a quantitative characterization of temporary streams 3) The SLDC was successfully used to compare the dynamics in the Valfredda and Turbolo catchments
THANKS FOR THE ATTENTION

## Slide 19
References
N. Durighetto, F. Vingiani, L. E. Bertassello, M. Camporese, G. Botter (2020).
Intraseasonal Drainage Network Dynamics in a Headwater Catchment of the Italian Alps.
Water Resources Research 56(4). https://doi.org/10.1029/2019WR025563
1
G. Botter, N. Durighetto (2020).
The Stream Length Duration Curve: A Tool for Characterizing the Time Variability of the Flowing Stream Length.
Water Resources Research 56(8). https://doi.org/10.1029/2020WR027282
2
A. Senatore, M. Micieli, A. Liotti, N. Durighetto, G. Mendicino, G. Botter. (2020)
Monitoring and Modeling Drainage Network Contraction and Dry Down in Mediterranean Headwater Catchments. Earth and Space Science Open Archive. https://doi.org/10.1002/essoar.10504177.1
3
N. Durighetto, G. Botter. (2021)
Time-lapse visualization of seasonal stream network dynamics from a limited number of field surveys.
Hydrological Processes HPEye. https://doi.org/10.1002/hyp.14053
4
F. Zanetti, N. Durighetto, F. Vingiani, G. Botter. (2021)
Analysing river network dynamics and active length-discharge relationship using water presence sensors.
Hydrology and Earth System Sciences Discussions. https://doi.org/10.5194/hess-2021-103
5
F. Zanetti, N. Durighetto, F. Vingiani, G. Botter. (EGU2021)
Analysis of the active length dynamics on intermittent streams using water presence sensors.
EGU General Assembly 2021, , EGU-8526. https://doi.org/10.5194/egusphere-egu21-8526
6

## Slide 20
Characterizing temporary stream dynamics: the Stream Length Duration Curve Nicola Durighetto, Alfonso Senatore, and Gianluca Botter
Temporary streams
Streams that temporarily cease to flow
Empirical dataset
Valfredda creek 28 field surveys
Turbolo creek 77 field surveys
Shows the relative fraction of time for which each possible length of the active network is equaled or exceeded
The Stream Length Duration Curve (SLDC)
Duration [%]
Length [km]
Can the SLDC be used to characterize stream network dynamics and compare catchments?
RESEARCH QUESTION