## Slide 1: Hydrological modelling of Sahelian hydrological paradox: accounting for explicit land use/land cover change in the simulation of hydrological processes
Roland Yonaba1, A. C. Biaou1, M. Koita1, T. Fowé1, A. L. Mounirou1, C. O. Zouré1, P. Queloz2, K. Karambiri1 ,H. Yacouba1
1International Institute for Water and Environmental Engineering (2iE),
Laboratory for Water, Hydro-Systems and Agriculture (LEHSA), Burkina Faso (roland.yonaba@gmail.com)
2Institute of Territorial Engineering (INSIT)
School of Management and Engineering Vaud (HEIG-VD), Yverdon-les-Bains, Switzerland.
https://doi.org/10.5194/egusphere-egu21-7974

## Slide 2: Hydrological modelling of Sahelian hydrological paradox: accounting for explicit land use/land cover change in the simulation of hydrological processes
OVERVIEW
1. Problem statement / Context
2. Study area
3. Modelling work and key findings
4. Key conclusions
The orange ‘Home’
Button takes you to
this section menu
The left/right arrows
take you to the
previous/next page
PICO Navigation
5. Published papers for more

## Slide 3: The problem: Modelling Hydrology in the West African Sahel
The West African Sahel context
High variability in the rainfall
(Buontempo et al., 2012)
High anthropic pressure (Potts et al., 2013)
Chart: Population (millions)
| 1950 | 2000 | 2050 | 2100
 | 31 | 103 | 340 | 606

## Slide 4: The problem: Modelling Hydrology in the West African Sahel
The Sahelian hydrological paradox
Severe droughts occured in the period 1970-1990 over the entire Western Sahel…
1
It resulted in loss of vegetation, soil surface crusting and sealing, land degradation…
1983
1995
2
3
Despite the rainfall decrease, a significant increase in surface runoff coefficients has been observed on most Sahelian hydrosystems, termed as the Sahelian hydrological paradox (SHP)
(Descroix et al., 2013)

## Slide 5: The problem: Modelling Hydrology in the West African Sahel
Sahelian context is a challenge for hydrological modelling
The SHP is an key indicator of the tight coupling between LULC changes and hydrological processes (HP) in the Sahelian context
The SHP cannot be reproduced within hydrological models : a decrease in rainfall translates to a decrease in runoff….
The issue arises because the LULC layer is kept static during the simulation, hence inducing stationarity in the runoff response to rainfall
Is the SHP effectively simulated in an hydrological model when integrating spatial and temporal LULC changes dynamically ?

## Slide 6: The study area : Tougou watershed
Yatenga province
Tougou watershed
37 km²
Located in northern Burkina Faso (West Africa)
Strong interrelations between climate, populations and environment, representative of the sahelian strip (Diello, 2007; Barbier et al., 2009)
Semi-arid climate (rainfall ~ 604 mm/yr - Avg. T°: 16-40°C – PET : 2095 mm/yr)
Daily Rainfall/runoff data monitoring during the period 2004-2018

## Slide 7: The study area : Tougou watershed
Land use/Land cover types found within the watershed (Yonaba et al., 2021b)
Bare / Degraded
Cultivated
Vegetation
Develops surface crusting and sealing
Low infilt. rates (6.2 ± 2.3 mm/hr)
High runoff potential
Limited crusting because of labour
High infilt. rates (44.7 ± 10.8 mm/hr)
Low/Moderate runoff potential
Develops surface crusting and sealing
Moderate infilt. rates (32.9 ± 8.2 mm/hr)
Low runoff potential

## Slide 8: The study area : Tougou watershed
1952
1973
1986
1999
2009
2017
Landscape evolution in the Tougou watershed (Yonaba et al., 2021b)
1952-1973: conversion of vegetation to cultivated
1973-1986: increase in bare/degraded (droughts)
1986-2017: recovery of bare/degraded to cultivated
Wet
Dry
Wet (period)

## Slide 9: Modelling work and key findings
Modelling the water balance with the SWAT model (Arnold et al., 1998)
SWAT: physically-based, continuous, semi-distributed hydrological model simulating the water balance at the scale of Hydrologic Response Units (HRU)
HRUs: set of unique and homogeneous combination of LULC, soil type, slope
Model Used
SWAT features a Land use UPdate module (LUP) which integrates dynamical LULC during the simulation by updating the fractional area occupied by a given HRU (HRU_FR) at discrete and user-predefined time-points (Pai et Saraswat, 2011; Yonaba et al., 2021a)

## Slide 10: Modelling work and key findings
Modelling scenarios and results
Warm-up
LULC 1999
Calibration
LULC 1999
Validation
LULC 1999
Daily rainfall/Runoff/climate data : 2004-2018
Two modelling scenarios are compared:
  SLU : static land use scenario
  DLU : dynamic land use scenario (where LULC is dynamically updated*)
* For intermediate dates in a period, fractional HRU_FR values are interpolated
SLU
Warm-up
LULC 1999
Calibration
LULC 2009
Validation
LULC 2017
DLU
2004-2005
2006-2012
2015-2018
Criterion | Calibration |  | Validation | 
 | SLU | DLU | SLU | DLU
KGE | 0,84 | 0,95 | 0,86 | 0,94
PBIAS (%) | -14,30 | -2,30 | -7,30 | 2,90
Simulation is quite satisfactory in both cases, however with an overestimation bias is SLU

## Slide 11: Modelling work and key findings
*Values in blue are annual average from observed runoff values (for surface runoff)
and from Koita et al. (2017) for deep aquifer recharge.
The depiction of the water balance is more accurate for deep aquifer recharge and for surface runoff using a dynamic LULC input
This increased accuracy might be explained by the runoff potential (CN values) for LULC conditions within the watershed
… which are updated in DLU mode!

## Slide 12: Modelling work and key findings
Surface runoff was therefore simulated over past periods (P1: 1952-1968, wet; P2: 1969-1985, dry and P3: 1986-2005, wet) using each of the LULC maps of the watershed in static mode (1952, 1973, 1986, 1999), which was compared with a dynamic scenario integrating all these LULC maps (DLU_HIST)

## Slide 13: Modelling work and key findings
The Sahelian Hydrological Paradox is only reproduced in DLU_HIST scenario, i.e. when explicitely accounting for LULC spatial and temporal changes within the watershed
In static LULC scenarios (SLU1952, SLU1973 and SLU1986), when rainfall decrease, surface runoff decreases as well.
The Sahelian Hydrological Paradox cannot be simulated.
Surface runoff increase between P1 and P3 despite the decrease in rainfall

## Slide 14: Modelling work and key findings
Disentangling annual rainfall variability and LULC changes impact on surface runoff
Scenario | Rainfall | LULC | Response
Period P1 condition | P1 | P1 | 
Effect of rainfall change | P3 | P1 | 
Effect of LULC change | P1 | P3 | 
Period P3 condition | P3 | P3 | 
Scenario | Rainfall | LULC | Response
Period P1 condition | P1 | P1 | 
Effect of rainfall change | P3 | P1 | 
Effect of LULC change | P1 | P3 | 
Period P3 condition | P3 | P3 | 
Crossing multiple scenarios (Yonaba et al., 2021a)
From P1 to P2 and P2 to P3, surface runoff is more sensitive to rainfall, but the effect is contrasted : rainfall tends to reduce runoff (P1 to P2), then to increase runoff (P2 to P3)
Overall, from P1 to P3, surface runoff is more sensitive to LULC changes, which tends to increase runoff.

## Slide 15: Key conclusions
Sahelian hydrology remains a challenge to hydrologists, especially for hydrological processes modelling
In this context, there is a tight coupling and interactions between land, climate, surface runoff and other hydrologicals. Such interactions are not yet fully understood and pose serious challenges to modelling
There is a need to account for spatial and temporal changes in LULC during hydrological simulation in order to simulate accurately specific processes in such environnments
There is a need to develop integrated modelling platforms or environnement coupling hydrological modelling and evolution of LULC conditions

## Slide 16: Published papers for more….
Yonaba, R., Biaou, A.C., Koïta, M., Tazen, F., Mounirou, L.A., Zouré, C.O., Queloz, P., Karambiri, H., Yacouba, H., 2021. A dynamic land use/land cover input helps in picturing the Sahelian paradox: assessing variability and attribution of changes in surface runoff in a Sahelian watershed.
https://doi.org/10.1016/j.scitotenv.2020.143792
Yonaba, R., Koïta, M., Mounirou, L.A., Tazen, F., Queloz P., Biaou A. C., Niang D., Zouré, C.O., Karambiri, H., Yacouba, H.. Spatial and transient modelling of land use/land cover (LULC) dynamics in a Sahelian landscape under semi-arid climate in northern Burkina Faso.
https://doi.org/10.1016/j.landusepol.2021.105305