## Slide 1
Andrey Afanasyev, Elena Vedeneeva
afanasyev@imec.msu.ru
Compositional modelling of impure gas injection into saline aquifers
with the MUFITS simulator
www.mufits.imec.msu.ru

## Slide 2: Contents
1. Why impure gas injection?
2. Compositional module of MUFITS
3. Governing equations
5. Validation of the software
7. Modelling cushion gas substitution with CO2
6. Modelling flue gas injection into a saline aquifer
8. Summary & Supplementary material
Overview of MUFITS
New modelling option; Mathematical formulation; Implementation in the software
Click on the panel to go to the corresponding slides
Application examples
4. Library of EoS coefficients

## Slide 3: Implications of impure gas injection
How to increase competitiveness of CCS?
Flue gas injection into subsurface
(reduce the cost of CO2 separation)
Cushion gas substitution with CO2
(explore the benefits of CO2 injection into UGS facilities)
More exhaust gas can be accommodated if CO2 purification reached only ~90%
A flue gas injection
(CO2, N2, O2, CH4)
Can UGS performance be improved by subsurface storage of CO2?
We aim at developing a software to predict such processes
Back to Contents

## Slide 4: Overview of MUFITS
Hydrodynamic simulator
Numerical modelling of the non-isothermal flows in porous media and wellbores
Includes several EoS modules for predicting the fluid properties
BLACKOIL
GASSTORE
COMPS
Other modules
Contains several EoS-modules for fluid properties prediction
The compositional module is based on a cubic EoS. We intend to improve this module for modelling phase equilibria in aqueous solutions
Can be freely downloaded from its webpage:
www.mufits.imec.msu.ru
A. Afanasyev, “Compositional Modelling of Petroleum Reservoirs and Subsurface CO2 Storage with the MUFITS Simulator,” in ECMOR XVII, Sep. 2020, vol. 2020, no. 1, pp. 1–13.
Back to Contents

## Slide 5: Compositional module
Hydrocarbon mixture
(CO2, N2, CH4, C2H6, C3H8, …)
Oil
Gas
Water
Water
Phases
Components
Petroleum reservoirs
does not mix with other components
each component is present in oil and gas
Aqueous solution
(brine, CO2, N2, CH4, …)
Oil
(brine phase)
Gas
Water
Water
Phases
Components
Gas injection into saline aquifers
not used
oil is treated as
the aqueous phase
i=l
i=g
non-aqueous phase
Originally designed for modelling three-phase flows in petroleum reservoirs
Only two-phase equilibria of aqueous solutions can be simulated by introducing the brine pseudo-component for the H2O-NaCl fluid
Oil is regarded as the brine phase
Back to Contents

## Slide 6: Transport equations
- mass conservation equation for each fluid component
- Darcy’s law
We account for the mechanical dispersion, i.e. hydrodynamic mixing in porous media
λL and λT characterize the longitudinal and transverse dispersion on the pore scale
A. Afanasyev, “Numerical modelling of solute flow dispersion in porous media using simulator MUFITS,” J. Phys. Conf. Ser., vol. 1129, p. 012002, Nov. 2018.
Back to Contents

## Slide 7: Equation of state (EoS)
We employ the conventional Peng-Robinson EoS in the modification for aqueous solutions proposed by Soreide & Whitson (1992).
The modification concerns to different sets of the binary interaction parameters τjk for the aqueous and non-aqueous phase parametrized as the functions of temperature (T) and NaCl molality (m) to account for the brine effect.
The most recent (e.g. Chabab et al. (2020)) correlation for τjk are implemented in the software to ensure an accurate prediction of mutual solubilities.
To improve density predictions, additional correlations for the volume shift parameters have been developed.
I. Søreide and C. H. Whitson, “Peng-Robinson predictions for hydrocarbons, CO2, N2, and H2S with pure water and NaCI brine,” Fluid Phase Equilib., vol. 77, no. C, pp. 217–240, 1992.
Back to Contents

## Slide 8: Library of EoS coefficients
COMPS
(compositional module)
Built-in library of EoS coefficients
CH4
CO2
N2
H2S
H2
O2
C2H6
C3H8
C4H10
Brine
Other components can be characterized by users
The development is supplemented with the built-in library of the EoS coefficients. The library makes it simpler the usage of the compositional module by the scientific community. Since only the most basic data are entered and all other coefficients and correlations are built into the reservoir simulator, no knowledge of phase equilibria modelling is required to use MUFITS.
The library contains the coefficients for these components; so, the multicomponent fluid can contain any of these.
Brine is a mandatory component for aqueous solutions.
Back to Contents

## Slide 9: Validation of the software
5540 m
440 m
Gas saturation
2670 m
To validate applicability of the developed module for modelling CO2 injection into saline aquifers, we consider the two-component flow of the H2O–CO2 fluid by modelling a benchmark problem developed by Class et al. (2009). We consider a sector model of an aquifer with one injector. The injection over 25 yr is simulated, then it is stopped and further 25 yr of the gas flow are simulated. In this scenario pure CO2 is injected.
The video on the left shows the CO2 saturation near the caprock over time.
CO2
Class et al., “A benchmark study on problems related to CO2 storage in geologic formations,” Comput. Geosci., vol. 13, no. 4, pp. 409–434, 2009.
Back to Contents

## Slide 10: Validation of the software
Distribution of the gas saturation at t=50 yr
CO2-in-place against time
CO2 is injected over first 25 yrs. Then, the injection is stopped and further 25 yr of CO2 migration are simulated
A good correspondence between the prediction of the COMPS and GASSTORE modules (solid and dashed lines, respectively) validates a good accuracy of the COMPS module.
The distribution of the gas saturation can hardly be distinguished from that obtained with other modules of MUFITS or reported in Class et al. (2009).
Afanasyev, et al., “Validation of the MUFITS Reservoir Simulator Against Standard CO2 Storage Benchmarks and History-matched Models of the Ketzin Pilot Site,” Energy Procedia, vol. 97, pp. 395–402, Nov. 2016.

## Slide 11: Modelling flue gas injection
CO2 (90%)+N2 (10%)
Now we change the composition of injected gas. It consists of 90% of CO2 and 10% N2.
Gas
saturation
Gas
density
N2 molar
fraction
in gas
Brine
density
Gas density at the leading front of the plume decreases. As a result, the plume propagates significantly farther in the structural dip direction.
The gas phase becomes richer in N2 at the leading edge of the plume due to a much higher, as compared to N2, solubility of CO2 in brine.
Back to Contents

## Slide 12: Flue gas against pure CO2
Flue gas
injection
Pure CO2
injection
Total mass of CO2 and N2 in the domain (M(2) and N2) and the mass of CO2 in gas and liquid phases (Mg(2) and Ml(2)). The dashed line shows the average mass fraction of N2 in the gas phase.
The plume of the flue gas propagates farther than that of pure CO2.
at t=46 yr
at t=50 yr
Back to Contents

## Slide 13: Cushion gas substitution with CO2?
We consider a synthetic model of a storage reservoir and simulate an initial period of CO2 and CH4 (is used as proxy for NG) injection followed by three cycles (seasons) of NG injection and production. We account for the mechanical dispersion to accurately simulate the mixing of gases.
Summer Winter Summer Winter
NG injection
Back-production
NG injection
Back-production
t
Molar fraction of CO2 in gas at the end of the initial period

## Slide 14: Cushion gas substitution with CO2?
CO2 molar
fraction in gas
Pressure
Gas
saturation
Back to Contents

## Slide 15: Parameters at the end the 1st and 3rd cycles
CO2 molar
concentration in gas
Gas
saturation
Gas
density
Brine
density
End of
the 1st cycle
End of
the 3rd cycle
At reservoir conditions, the density of CO2 is much larger than that of CH4. This, to some degree reduces the intensity of the mixing
Back to Contents

## Slide 16: Fluid-in-place quantities
Fluid-in-place quantities
Injection/production rates
Tubing head pressure
of an NG wells
Changes in the flow direction and the mechanical dispersion result in that more than a half of injected CO2 is trapped by solubility after 3 cycles.
The total mass of injected CO2 is several times larger than that of NG
The dashed line shows the molar fraction of CO2 in the produced gas. Thus, due to intensive mixing, CO2 spreads to the NG wells after 3 years when its concentration reaches 4%.
Back to Contents

## Slide 17: Summary
We present an improved Søreide and Whitson EoS for modeling aqueous solutions. We supplement the SW EoS with correlations for volume shifts
We implement the SW EoS in the compositional module of the MUFITS simulator. It contains a built-in library of EoS coefficients to ease the usage of the software.
The gas plume is significantly wider for an impure CO2 injection.
A simulation example of cushion gas substitution with supercritical CO2 is presented. The mechanical dispersion can cause a rapid CO2 spread into the wells used for natural gas production.
Acknowledgements: The authors acknowledge funding from Russian Science Foundation under grant # 19-71-10051.
Back to Contents

## Slide 18: Supplementary material
Click on the links to download the supplementary material
MUFITS site
Input file to the benchmark study of CO2 injection
Input files to the study of flue gas injection
Input files to the study of cushion gas substitution
Reference manual
Back to Contents