## Slide 1: Assessment of deep learning based landslide detection and mapping performances with backscatter SAR data
EGU General Assembly 2022 - Session NH3.8 - Thursday, 26 May, 13:42–13:49
Lorenzo Nava¹, Kushanav Bhuyan¹, Sansar Raj Meena¹, Oriol Monserrat², Filippo Catani¹
¹ Machine Intelligence and Slope Stability Laboratory (MISSlab), Department of Geosciences, University of Padova, Italy
² Department of Remote Sensing, Geomatic Research Unit, Centre Tecnològic Telecomunicacions Catalunya, Spain

## Slide 2
Introduction:
EGU General Assembly 2022
Source: http://meteoweb.eu
Cause severe damages to communities as well as to human infrastructures.
Earthquake- and rainfall-triggered multiple landslides events damage wide areas in a short time span.
We must be able to intervene promptly right after the event.

## Slide 3
Research problem:
EGU General Assembly 2022
Optical data has limitations in presence of thick cloud cover.
Lack of research on SAR data in combination with Deep Learning to map landslides.
Source: https://blogs.agu.org/

## Slide 4
Purpose of the study:
EGU General Assembly 2022
Overcome whether-related limitations of optical data for rapid landslide mapping.
Evaluating performances of DL models on composites of different polarizations and orbits of Sentinel-1 SAR amplitude data.

## Slide 5
EGU General Assembly 2022
Iburi sub-prefecture, Hokkaido, Japan.
Fig. 1: Localization of the study area.
Event considered:
A 6.6 Mw earthquake triggered about 7837 coseismic landslides on September 6, 2018.
Fig. 2: Coseismic landslides in the study area. (Source: Wang et al. 2019).
Study area:

## Slide 6
EGU General Assembly 2021
Sentinel-1 SAR GRD products (VV and VH polarizations).
Sentinel-2 VHR RGB image (10 m x 10 m).
Digital Elevation Model (DEM) (30 m x 30 m) and Slope obtained from the same.
Materials:

## Slide 7
EGU General Assembly 2022
Sentinel-1 SAR Layers
Topographic Layers
Input
Input
+
Conv2D, 3x3
MaxPool2D, 2x2
MaxPool2D, 2x2
Conv2D, 3X3
ReLU
ReLU
Rete Neurale
CNN
Object detection:
Sliding Window

## Slide 8
Object detection:
Nava et al., 2021
EGU General Assembly 2022

## Slide 9
EGU General Assembly 2022
Image segmentation:
Sentinel-1 SAR Layers
Topographic Layers

## Slide 10
Image segmentation:
Nava et al., 2022
EGU General Assembly 2022

## Slide 11
Conclusions:
EGU General Assembly 2022
It is possible to detect and map landslides also in presence of cloud cover (DL and SAR data).
Limitations due to geometric distortions.
Relevant benefits in terms of emergency management and civil protection operations, such as significantly decreasing the time delay in the emergency response in various scenarios.

## Slide 12
References:
EGU General Assembly 2022
Nava, L., Monserrat, O., & Catani, F. (2021). Improving landslide detection on SAR data through deep learning. IEEE Geoscience and Remote Sensing Letters, 19, 1-5.
Nava, L., Bhuyan, K., Meena, S. R., Monserrat, O., & Catani, F. (2022). Rapid Mapping of Landslides on SAR Data by Attention U-Net. Remote Sensing, 14(6), 1449.

## Slide 13: THANK YOU FOR YOUR ATTENTION
lorenzo.nava@phd.unipd.it