## Slide 1
What control hydrothermal dolomitization?
Experimental replacement with time-step monitoring by X-ray microtomography
B. Lefeuvre, N.E. Beaudoin, S. Centrella
E2S project supported by « Disturb » chair
Co-funded by CCLO & INSU projects
benjamin.lefeuvre@univ-pau.fr
25/05/2022

## Slide 2
m to km
µm
2CaCO3 + Mg2+ = (Ca,Mg)(CO3)2 + Ca2+
calcite
dolomite
fluid
fluid
Density = 2,71
Density = 2,84
 Apparition of 16% of porosity
Introduction
Gomez-Rivas et al., 2021
Mc Cormick et al., 2021
Centrella et al., 2020
Dol
Dol
Cc
Cc
Dolomites mountains, Italy
Replacement of calcite by dolomite
1

## Slide 3
2CaCO3 + Mg2+ = (Ca,Mg)(CO3)2 + Ca2+
calcite
dolomite
fluid
fluid
Density = 2,71
Density = 2,84
 Apparition of 16% of porosity
Introduction
Mc Cormick et al., 2021
Replacement of calcite by dolomite
Very good reservoir properties (high porosity)
  - Hydrocarbons, CO2 storage, geothermy, groundwater
Often associated with MVT deposits (Zn, Pb, Ag, Sulfides)
Results of the transformation of two carbonate phases…
- Impact on CO2 cycle?
DOLOSTONE
MVT
Haldar, 2020
1

## Slide 4
2CaCO3 + Mg2+ = (Ca,Mg)(CO3)2 + Ca2+
calcite
dolomite
fluid
fluid
Density = 2,71
Density = 2,84
 Apparition of 16% of porosity
Introduction
Mc Cormick et al., 2021
Replacement of calcite by dolomite
How can we reconciliate scales of observations?
What can we learn from the replacement front morphology?
Does the creation of porosity help propagating the replacement front?
 Need of experimental petrology to recreate dolomitization
1

## Slide 5
HYDROTHERMAL
REACTOR
Confinement
pressure
(16 bars)
Reactive fluid
Reactive Mg-enriched
fluid
(H2O , CaCl2 , MgCl2 , ZnCl)
Vandeginste et al., 2019
Fluid-rock interactions
 CLOSED SYSTEM !!!
Hydrothermal reactors
Sealed and hermetic
Teflon holds up to ≈ 287°C
Suited to hydrothermal conditions !
Experimental setup
Carrara Marble
De Bresser et al., 2005
1 cm
SAMPLE
De Bresser et al., 2005
Homogeneous
No porosity
2

## Slide 6
HYDROTHERMAL
REACTOR
Confinement
pressure
(16 bars)
Reactive fluid
Vandeginste et al., 2019
STEAMROOM (200°C)
Experimental setup
Incubation
(1, 2, 3 weeks)
Reactive Mg-enriched
fluid
(H2O , CaCl2 , MgCl2 , ZnCl)
2

## Slide 7
HYDROTHERMAL
REACTOR
Confinement
pressure
(16 bars)
Reactive fluid
Vandeginste et al., 2019
Incubation
(1, 2, 3 weeks)
X-RAY
MICROTOMOGRAPHY
3D
(x,y,z)
STEAMROOM (200°C)
Experimental setup
Reactive Mg-enriched
fluid
(H2O , CaCl2 , MgCl2 , ZnCl)
2

## Slide 8
HYDROTHERMAL
REACTOR
Confinement
pressure
(16 bars)
Reactive fluid
Vandeginste et al., 2019
STEAMROOM (200°C)
X-RAY
MICROTOMOGRAPHY
3D
(x,y,z)
4D
(x,y,z,t)
Experimental setup
Incubation
(1, 2, 3 weeks)
Reactive Mg-enriched
fluid
(H2O , CaCl2 , MgCl2 , ZnCl)
2

## Slide 9
Experimental setup
Unreacted
calcite core
Dolomite
t2wks
4mm
Experimental setup
3
ᴓ

## Slide 10
x, y
t1wk
(voxel = 4,25µm)
1mm
Heterogeneous replacement front:
Propagating along grain boundaries
Developping macro pores or not…
Results
4

## Slide 11
Results
5

## Slide 12
Dol
Cc
ProtoDol
Results
Two-steps reaction
5
Cc to Protodol
Protodol to Dol
Different porosities between the three minerals at stake in this reaction
How do they connect?
What are the impacts of pores sizes??

## Slide 13
Results
Same sample, same (x,y) slice, different time!
x, y
t1wk
x, y
t2wks
x, y
t3wks
6
ᴓ
≈ 3,43mm
ᴓ
≈ 3,36mm
ᴓ
≈ 3,26mm
Reduction of diameter with time implies dolomite dissolution in the reactive fluid
- Need of ICP-MS concentrations of the different fluids collected after the experiments to constrain fluid/rock equilibrium

## Slide 14
Results
Same sample, same (x,y) slice, different time!
x, y
t1wk
x, y
t2wks
x, y
t3wks
% | t1 | t2 | t3
Dol | 10,27 | 15,27 | 17,63
Cc | 87,04 | 81,09 | 78,61
Pores | 2,69 | 3,64 | 3,76
6
Usefull to constrain kinetics
Cc
Dol & Pores

## Slide 15
Conclusions and perspectives
7
Experimental setup
Fluid chemistry (Vandeginste et al., 2019 recipee)
Selected samples (Carrare marble)
Suitable experimental conditions (hydrothermal reactors)
Imaging the dolomitization front
3D morphology
Pores repartition
Quantification
Protodolomite
Evolution of the porosity
Coupled dissolution-precipitation between Cc and Protodolomite
Coupled dissolution-precipitation between Protodolomite and dolomite??
Diffusion of Mg?

## Slide 16
Thanks for your attention!
benjamin.lefeuvre@univ-pau.fr