## Slide 1: GNSS-Reflectometry for Ocean Remote Sensing
Matthew Hammond, Giuseppe Foti, Christine Gommenginger, Meric Srokosz, and Nicolas Floury
EGU 2022

## Slide 2: Introduction
GNSS-R uses reflected signals from Global Navigation Satellites
GNSS-R ocean missions have typically targeted retrieval of wind speed
  E.g. NASA’s CyGNSS mission (a constellation of 8 satellites)
We assessed GNSS-R ocean geophysical dependencies
Reference datasets:
  ECMWF ERA-5 reanalysis model - Wind / SWH / SST / Precipitation
  SMOS - SSS
  Global Precipitation Climatology Product (GPCP)
Notes: GNSS-R what is
Constellation = large volumes of data
Wind speed primary target

## Slide 3: Impact of Geophysical Dependencies
Investigate impact on CyGNSS observable (NBRCS) over ocean
  Across a range of wind speeds
Strong sensitivity to:
  Significant wave height
  Precipitation
  At low wind speeds
Low sensitivity to SST
  At all wind speeds
  After SWH effect removed
No apparent sensitivity to SSS

## Slide 4: GNSS-R Precipitation Retrieval
Strong relationship seen between GNSS-R retrieval and GPCP dataset across range of rainfall values

## Slide 5: Global Retrieval Comparison
Global comparison of GNSS-R retrieved rainfall patterns with GPCP product
Large similarity in patterns of precipitation
  GNSS-R retrievals currently more noisy
Some increased discrepancy around islands (e.g. South East Asia)
  Likely from assumed swell-wind wave relationship
GPCP
GNSS-R
Notes: ITCZ,

## Slide 6: Summary
A number of geophysical dependencies affect GNSS-R signals over ocean (especially at low wind speeds)
  SWH (up to 4dB)
  SST (~0.5 dB, all wind speeds)
  Precipitation (up to 4dB)
Precipitation can be retrieved using GNSS-Reflectometry
  At low wind speed
  With knowledge of impact of other geophysical parameters
GNSS-R can provide new source of precipitation information
  Different scattering mechanism
  Constellations can provide frequent revisits
  Supplement established approaches
Notes:     Note different scattering form
Precipitation highly spatially / temporally variable