## Slide 1
Validation of a 1-D lake model for modeling evaporation from an elongated and deep boreal reservoir
Habiba Kallel (1,2), François Anctil(1,2) , Daniel F.Nadeau (1,2), Antoine Thiboult (1,2), and Murray D.Mackay (3)
(1) Department of Civil and Water Engineering, Université Laval, Quebec, Canada.
(2) CentrEau, Water research center, Quebec QC, Canada
(3) Meteorological Research Division, Environment and Climate Change Canada, Toronto, Ontario,Canada
Habiba.kallel.1@ulaval.ca

## Slide 2
Lake size | Number | Total area of Canada
0.001- 1 km2 | 19.5 x106 | 161000 (24 %)
1-10 km2 | 27800 | 73000 (11%)
10-100 km2 | 3300 | 86000 (13%)
100- 100000 km2 | 400 | 356000 (52%)
La Romaine 2 hydroelectric reservoir (50.7°N, 63.2°W)
Observations
Twos fluxes towers using an eddy-covariance system with a sampling rate of 10 Hz.
A1. Year –round on shore
A2. Ice-free on a raft
B. Water temperature measurements available from the surface to 70 m deep.
Introduction And Study Site
Lake-atmosphere interactions are crucial for climate and weather assessment.
Inland and water bodies are diverse in size and shape
Canada

## Slide 3
Parameter | Value
Mean Depth (m) | 60
Vertical resolution | 0.5
Time step | 30 min
Fetch | 9200 m
Simulation period | 2018-06-25 to 2021-06-08 (3 years)
Initial temperature profile | Observations on 2018-06-25
Climate observations
Canadian Small Lake Model
Model Assessment
Meteorological forcing
Model setup

## Slide 4
Model Performance: Turbulent Heat Fluxes

## Slide 5
Model Performance: Turbulent Heat Fluxes
Comparison shows a good agreement for H.
Deviations mostly occur before freeze-up (October-December) and around ice-off (April-May).
Tendency of overestimating LE when its observed magnitude is small (ice cover period).

## Slide 6
Thermal Regime
Near-surface water temperature confirming the ability of the CSLM to simulate the near-surface seasonal cycle.
Early depletion of the energy storage leading to an early modeled freeze-up.
During fall: overestimation of the water temperature induces an overestimation of the heat fluxes.
Observed
Observed
Simulated
Simulated

## Slide 7
Thermal Regime
Observed
Observed
Simulated
Simulated
CSLM overestimates number of freezing days
 | Observed (day) | Simulated (day) | Error (day)
Year 1 | 148 | 170 | 22
Year 2 | 133 | 148 | 15
Year 3 | 86 | 110 | 24

## Slide 8
Take home message
Objective
Accurate modeling water-atmosphere interactions to better understand the role of lakes on weather and climate
Strengths
Turbulent fluxes were successfully predicted during the open-water period.
Thermal mixing and mixed layer deepening well estimated.
Difference between number of simulated and observed freezing days always below 25 days.
Limitations
Overreaction to high wind speed episode.
Underestimation of water temperature in the late fall causing an early lake freeze-up.
Lower performance following the seasonal overturns.
Challenge
Surface heat fluxes are particularly challenging to model because of the scarcity of direct observations

## Slide 9
Thank you for attention
Habiba.kallel.1@ulaval.ca