## Slide 1: Numerical analysis for dispersion characteristic from time domain induced polarization based on laboratory measurement data of complex resistivity
Juyeon Jeong1 · Bitnarae Kim1 · Desy Caesary1 · YoungSam Mun2 · Doukhee Won3· Myung Jin Nam1, 4*
1Department of Energy and Mineral Resources Engineering, Sejong University, South Korea
2DevBox Inc.
3C&H Inc.
4Department of Energy Resources and Geosystems Engineering, Sejong University, South Korea

## Slide 2: Introduction
TDIP
easier &
measuring time ↓
Field scale
SIP data acquisition
 analysis on
dispersion characteristics
Laboratory scale
core sample
(Mewafy et al., 2013)
1) site TDIP data dispersion characteristics
2) comparison TDIP/SIP estimation parameter
Full time decay estimation ↑
TDIP instrument advance
 sampling rate ↑
Time window: 6 ch
1970-80s
2010s
2000s
Time window: 10 ch
Sampling rate: 70-250 Hz
Sampling rate ~ kHz
Time window: 20 ch
M-4

## Slide 3: Theory
Induced polarization (IP) methods classification
(Pelton et al,. 1978)
Time domain CC model
Frequency domain CC model
(Cole & Cole, 1941; Pelton et al,. 1978)
Cole-Cole (CC) model

## Slide 4: schematic of research process
(Shefer et al,. 2013)
1) Digitizing SIP data & parameter fitting
inversion result
CC
parameter
2) SIP parameters are used for
constructing the numerical simulation
1 ohm-m, 200 mv/v,
s, 0.4
100 ohm-m, 1 mv/v,
s, 0.8
modified
4) TD CC parameter fitting from inversion results
Research process sequence
3) Time-channel inversion

## Slide 5: Verification of a single anomaly
SIP fitting parameter by chargeability
TDIP fitting parameter by chargeability
CC |  |  | 
SIP | 66 |  | 0.17
TDIP | 24 | 11 | 0.66
relative error (%) | 64 | 94 | 74
CC |  |  | 
SIP | 66 |  | 0.17
TDIP | 24 | 11 | 0.66
relative error (%) | 64 | 94 | 74
CC |  |  | 
SIP | 172 |  | 0.35
TDIP | 106 | 18 | 0.57
relative error (%) | 38 | 33 | 38
CC |  |  | 
SIP | 172 |  | 0.35
TDIP | 106 | 18 | 0.57
relative error (%) | 38 | 33 | 38
CC |  |  | 
SIP | 243 |  | 0.38
TDIP | 160 | 27 | 0.55
relative error (%) | 33 | 55 | 30
CC |  |  | 
SIP | 243 |  | 0.38
TDIP | 160 | 27 | 0.55
relative error (%) | 33 | 55 | 30
chargeability ↑  relative error of the chargeability ↓
doesn't fit well regardless of the value
= 50 mV/V
= 200 mV/V
= 300 mV/V
ohm-m, ,
sec, 0.4
= 200 mV/V inversion results
Chargeability[mV/V]

## Slide 6: Mode1: NAPL contamination site
amplitude
phase
SIP Response by Biodegraded Oil Saturation
(Abdel Aal et al., 2014)
LNAPL; BTEX, Aromatic Hydrocarbon mixture
(Cozzarelli et al. 2010)
30 Years of Active Biodegradable Oil
Oil saturation (So)  0/0.4/0.8
Difficult to describe with CC
 use only range 0.1 - 100 Hz
SIP CC parameter fitting
oil saturation ↑
 m ↑
0.1 ~ 1000 Hz measurements
13 equal logarithmic intervals
Sample

## Slide 7: Mode1-model description
, 115 mV/V,
sec, 0.21
:
, 18 mV/V,
sec, 0.31
▪vadose zone
: saturation zone
+ 500 ohm-m
m: 0 mV/V
tau, c: equal saturation zone
time-window: 9
modeling cell: 1 m 1 m 1 m
No. line: 5
dipole spacing: 4 m
n-spacing: 4
maximum receiver dipole: 12
time range: 1.59E-03 ~ 7.39E-01
noise: Gaussian random 2%
Model setting
Saturated zone
Model description

## Slide 8: Mode1-TDIP inversion results & TDIP fitting
oil saturation 0.4
oil saturation 0.8
TD-CC fitting & comparison
Chargeability[mV/V]
9
12
0
3
6
Chargeability[mV/V]
52
70
0
18
35
Ⅰ . oil saturation 0.4
Ⅱ. oil saturation 0.8
CC |  |  | 
SIP | 18 |  | 0.31
TDIP | 11 | 1.6 | 0.15
relative error (%) | 39 | 99 | 52
CC |  |  | 
SIP | 18 |  | 0.31
TDIP | 11 | 1.6 | 0.15
relative error (%) | 39 | 99 | 52
SIP vs. TDIP CC
relative error: 52 %
CC |  |  | 
SIP | 115 |  | 0.21
TDIP | 88 | 12 | 0.1
relative error (%) | 23 | 100 | 52
CC |  |  | 
SIP | 115 |  | 0.21
TDIP | 88 | 12 | 0.1
relative error (%) | 23 | 100 | 52
t (s)
1.59E-03
3.43E-03
7.39E-03
1.59E-02
3.43E-02
7.39E-02
1.59E-01
3.43E-01
7.39E-01
TDIP inversion results

## Slide 9: Mode2: mine site
6.0 % vol. chalcopyrite
mixed with Quartz sand
Porosity: 42.46 %
Radii of conducting particles: 500 ~ 425
(Mahan et al., 1986)
mineral  chalcopyrite
clay
(Ghorbani et al., 2009)
amplitude
phase
background
Silica sand sample
grain size: 125-250 μm
Radii of conducting particles: 500 ~ 425
Silica sand sample
(Chen et al., 2008)
SIP Response by several samples
Sample
Difficult to describe with CC
 use only range 0.1 - 100 Hz
SIP CC parameter fitting

## Slide 10: Mode2-model description
halo, overburden
 Kang & Oldenburg et al., 2019
Layer |  | m | tau | c
mineral | 414 | 347 | 0.012 | 0.9
Clay | 30.6 | 105 |  | 0.26
background | 773 | 0.01 | 0.1 | 0.36
halo | 500 | 0.1 | 0.5 | 0.5
Overburden | 900 | 0.01 | 0.1 | 1
Layer |  | m | tau | c
mineral | 414 | 347 | 0.012 | 0.9
Clay | 30.6 | 105 |  | 0.26
background | 773 | 0.01 | 0.1 | 0.36
halo | 500 | 0.1 | 0.5 | 0.5
Overburden | 900 | 0.01 | 0.1 | 1
time-window: 14
modeling cell: 4 m 4 m 4 m
No. line: 1
dipole spacing: 5 m
maximum receiver dipole: 19
time range: 0.16 ~ 1.6
(use Syscal Pro semi log time range)
noise: Gaussian random 2%
fitting
parameter
literature reference
(Kang & Oldenburg et al., 2019)
mineral
background
clay
overburden
halo
460
parameter substitution
Model setting
Model description

## Slide 11: Mode2-TDIP inversion results & TDIP fitting
Ⅰ . clay
Ⅱ. mineral
SIP vs. TDIP CC
relative error: 28 %
CC |  |  | 
SIP | 105 |  | 0.31
TDIP | 102 | 2.4 | 0.26
relative error (%) | 2.9 | 64 | 16
CC |  |  | 
SIP | 105 |  | 0.31
TDIP | 102 | 2.4 | 0.26
relative error (%) | 2.9 | 64 | 16
CC |  |  | 
SIP | 115 |  | 0.46
TDIP | 112 | 1.7 | 0.28
relative error (%) | 2.6 | 99 | 39
CC |  |  | 
SIP | 115 |  | 0.46
TDIP | 112 | 1.7 | 0.28
relative error (%) | 2.6 | 99 | 39
TD-CC fitting & comparison
anomaly
appeared well
t (s)
0.16
0.24
0.32
0.4
0.48
0.56
0.64
0.72
0.8
TDIP inversion results

## Slide 12: Conclusions & further research
Conclusions
Further research
Comparisons 3D SIP parameters model from TD and FD
Using Fourier transform rather than time-domain CC model
Chargeability (): TDIP inversion results & TDIP fitting well matched with the constructed model by SIP parameters
Time constant (): – well fitted as TDIP fitting within 1 period – incorrectly fitting
Most of experimental IP data
TDIP Cole-Cole model  limited range for