## Slide 1: Differential Learning: A method for polar motion time series prediction
Mostafa Kiani Shahvandi, Matthias Schartner, and Benedikt Soja
EGU General Assembly, May 27, 2022
Space Geodesy Group
Institute of Geodesy and Photogrammetry

## Slide 2: Table of Contents
Polar motion time series prediction problem
Differential Learning method
Comparative analyses with other methods
Conclusions

## Slide 3: Polar motion time series prediction problem
Polar motion: changes in the earth's rotation axis with respect to the earth's surface, referred to a reference called Conventional Intermediate Pole (CIP)
Determined by different space-geodetic techniques, including Global Navigation Satellite Systems (GNSS)
Not constant!
Earth image from https://giphy.com/gifs/art-earth-speed-3ohhwgrL4KKPIZoTQY

## Slide 4: Polar motion time series prediction problem
Polar motion: needed for space application, particularly those requiring transformation between geodetic and celestial coordinate systems
Navigation of spacecrafts
Orientation of deep-space telescopes
One major issue: final, most accurate data come with a latency of up to several days (or weeks)
However : the mentioned applications require instantaneous polar motion information
Solution: using predictions of polar motion
Requirement: predictions be as close as possible to the final polar motion data

## Slide 5: Polar motion time series prediction problem
Polar motion time series characteristics
  Major deterministic, periodic signals (and trend)
    Chandler (433) and yearly (365)
    Basis for harmonic + autoregression models
    Achieving best performance in the first Earth Orientation Parameters Prediction Campaign (EOPPCC)

## Slide 6: Polar motion time series prediction problem
Polar motion time series characteristics
  2. Relation to the Effective Angular Momentum (EAM) functions
    Directly related to EAM via Liouville differential equation in complex domain(basis for the method conversion from EAM to polar motion)
    Generally not separable in this differential equation  are related
    The main driving factor: Oceanic Angular Momentum (OAM)
Earth's pole region
Particle redistributed
CIP
Instantaneous pole position
Earth image from https://www.amnh.org/explore/ology/earth/what-is-earth

## Slide 7: Polar motion time series prediction problem
Polar motion time series characteristics
  3. Linearity in short time intervals
    Measured through differentiation and fitting of a line
    Suitability of linear models
Linear models for the prediction of polar motion work well

## Slide 8: Differential Learning method
An appropriate method for polar motion prediction:
  Learns the deterministic and stochastic parts (simultaneously)
  Takes advantage of different sources of physical information
  Selects the suitable model type (linear vs. nonlinear)
Differential Learning
Based on ordinary differential equations (ODE)
No preprocessing required
Using different sources of physical information
Different forms; linear and nonlinear
Dealing with unevenly-spaced time series: combination with Latent ODEs

## Slide 9: Differential Learning method
ODE of order
A parametric, neural network
Physical information (EAM, other EOPs)

## Slide 10: Differential Learning method
General solution
Linear weights
indefinite integration of
Based on successive integrals, approximation, and numerical integration
Input sequence length

## Slide 11: Differential Learning method
Linear Differential Learning
Combination with Latent ODEs possible
Based on linear form for the neural networks (Dense layers with linear activation functions)
Feature importance analysis
Uncertainty propagation analysis

## Slide 12: Comparative analyses with other methods
Analysis under the conditions of first EOPPCC
  prediction horizon of 10 days (short-term)
  time interval for training the model between September 1, 1996 and September 30, 2005
  time interval for submitting the predictions from October 1, 2005 to December 31, 2008, every Thursday
  possibility of using various data sources, such as EOPs, EAM, etc.
  evaluation based on the IERS final EOP data
The best performing method in the first EOPPCC: harmonic analysis + autoregression
We use
  Jet Propulsion Laboratory (JPL) polar motion series (containing rates)
  EAM data from GFZ German Research Centre for Geosciences
  Linear Differential Learning (DL) combined with Latent ODEs

## Slide 13: Comparative analyses with other methods
Investigation of the best input sequence length
  Based on a validation set (last 20% of the training set)
  Empirically determine  which value for results in the best prediction performance on the validation set
  Start from 1, increase incrementally
  L

## Slide 14: Comparative analyses with other methods
Prediction accuracy assessment based on Mean Absolute Error (MAE, in the milliarcseconds unit)
Prediction day | Improvement in percentage | Improvement in percentage
1 | 85 | 81
2 | 74 | 62
3 | 65 | 50
4 | 64 | 48
5 | 63 | 46
6 | 61 | 42
7 | 61 | 39
8 | 56 | 31
9 | 49 | 28
10 | 42 | 25
Prediction day |  | 
1 | 85 | 81
2 | 74 | 62
3 | 65 | 50
4 | 64 | 48
5 | 63 | 46
6 | 61 | 42
7 | 61 | 39
8 | 56 | 31
9 | 49 | 28
10 | 42 | 25
Average improvement across both components | 53%

## Slide 15: Comparative analyses with other methods
Distribution of residuals (observation minus prediction)
  Gaussian distribution with increasing means
  Higher standard deviations in later prediction days

## Slide 16: Comparative analyses with other methods
Analysis of the importance of the features
  The most important features: themselves, their rates, and EAM
  The rates of polar motion: closely related to Geodetic Angular Momentum (GAM) functions

## Slide 17: Comparative analyses with other methods
Analysis of the importance of the time steps in the input sequence
  The last time step is the most important one
  The penultimate time step is also important
  Importance of last time step of for and vice versa

## Slide 18: Conclusions
Polar motion time series has major deterministic signals; in addition, it displays stochastic parts
For polar motion phenomenon different physical information exist, the most important of which are the EAM functions
In short-term intervals, polar motion changes linearly, thus making linear models suitable for modelling and prediction of this time series
Differential Learning is a method for learning deterministic and stochastic parts simultaneously, taking advantage of different sources of physical information, including EAM functions
Linear Differential Learning combined with Latent ODEs achieves state-of-the-art accuracy compared to the best performing method in first EOPPCC, improving the results on average by approximately 53%

## Slide 19
Mostafa Kiani Shahvandi, Matthias Schartner, Benedikt Soja
{mkiani,mschartner,soja}@ethz.ch
ETH Zürich
Space Geodesy Group,
HPV G51, G56, G54
Robert Gnehm Weg 15
8093 Zürich, Switzerland
www.space.igp.ethz.ch