## Slide 1
Towards fully automated root phenotyping in the field: from Minirhizotron image acquisition to data analysis
Kaining Zhou1, Adam Soffer2, Jhonathan E. Ephrath1, Ofer Hadar2, Naftali Lazarovitch1
1. French Associates Institute for Agriculture and Biotechnology of Drylands, Jacob Blaustein Institutes for Desert Research, Ben-Gurion University of the Negev, Sede Boqer Campus, 8499000, Israel
2. School of Electrical and Computer Engineering, Ben-Gurion University of the Negev, 8410501 Beer Sheva, Israel
Scan me
to read
the abstract

## Slide 2: Effective root monitoring in the soil is important for making sound decisions.
water
Fertilizer
Minirhizotron system (MR)

## Slide 3
Minirhizotron image annotation is tedious and time-consuming
1.5mins per image
Annotation time for
a long-term experiment:
Time & cost
Observation replicate & frequency
7,500-15,000 minutes

## Slide 4
Snapshot vs. Monitor on a continuous basis
Day 1
Day 11
Example:

## Slide 5
Root growth from Day 1 to Day 11

## Slide 6: Towards fully automated root phenotyping in the field
Estimated root length:
46 mm
Field
Automatic Minirhizotron camera
Download image remotely
Image analysis with Convolutional Neural Networks
Decision making

## Slide 7
 | Conventional Minirhizotron system (BTC-ICAP) | RootCam
Image dimensions | 640 × 480 pixels | 2952 × 1944 pixels
Image size | 18 × 13.5 mm2 | 25 × 19 mm2
Operation | Manual | Automated
Data acquisition | Copy manually | Download remotely
Automated Minirhizotron system: RootCam© by
1 mm

## Slide 8
A root length estimation model is developed based on
Convolutional neural networks (CNN)
FE: Feature Extraction Module
CM: Classification Module
RM: Regression Module

## Slide 9
Result comparison: manual annotation vs. CNN model
Chart: Manual annotated TRL per image (mm)
 | Training dataset | Test dataset
Images taken from | Tomato roots | Pepper roots
Image amount | 18,000 | 832
Image acquisition system | Conventional Minirhizotron | Automated Minirhizotron: RootCam

## Slide 10
Time used for data analysis: manual annotation vs. CNN model
VS.
Total root length:
46 mm
90s per image
3s per image

## Slide 11
Time used for data analysis: manual annotation vs. CNN model
Chart: Time used for analysis (min)
| Maual annotation | Model estimation
 | 1248 | 37.8182
Chart: Days after transplanting
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130
Ground truth | 0 | 111.9883 | 170.3294 | 178.8173 | 174.0419 | 176.5721 | 246.6135 | 609.196 | 756.5352 | 989.4645 | 1092.2746 | 1080.0191 | 1103.9239 | 1110.1347 | 1098.1315 | 1107.4367 | 1107.9872 | 1099.3353 | 1115.8886 | 1162.9255 | 1172.5489 | 1189.4371 | 1190.6592 | 1203.7682 | 1206.7145 | 1245.6869
Estimated by model | 137.3695 | 202.5228 | 239.1283 | 229.727 | 243.8686 | 249.3707 | 304.0802 | 737.3714 | 768.1181 | 1115.388 | 1116.7878 | 1222.0342 | 1226.4511 | 1150.4525 | 1073.4546 | 1133.3725 | 1052.1095 | 1169.3961 | 1132.0926 | 1164.8 | 1136.3018 | 1224.701 | 1168.2749 | 1235.5624 | 1182.7253 | 1258.7995

## Slide 12: Applications
Monitor rooting depth
Study root hairs
Detect root-knot nematode infection
Monitor root
Dynamics in real time
Evaluate plant stress
with fluorescent roots
Provide timely data
to build models

## Slide 13: Take home message
The automated Minirhizotron system greatly facilitates image acquisition.
The CNN model is accurate to estimate root length on Minirhizotron images.
This platform will accelerate high-throughput root phenotyping in the field.

## Slide 14: Thank you for your attention! Welcome to contact us if you have any questions.
Kaining Zhou
zhoy@post.bgu.ac.il
French Associates Institute for Agriculture and Biotechnology of Drylands, Jacob Blaustein Institutes for Desert Research, Ben-Gurion University of the Negev, Israel