## Slide 1: Triggering mechanisms of the induced seismicity at the Underground Gas Storage of Castor, Spain
victor.vilarrasa@idaea.csic.es
EGU, 23-27 May, 2022
Víctor Vilarrasa
Silvia De Simone, Jesús Carrera, Antonio Villaseñor

## Slide 2
4.1
17
4-10
M
days
km

## Slide 3
Amposta Fault
Known and active, 1-km offset
Gas storage
Castor platform
Deep fault
Not mapped, critically stressed
2 km
4 km
6 km
8 km
10 km
The induced earthquakes are aligned along a deep fault
How could gas injection at 1.7-km depth cause earthquakes several kilometers below with no hydraulic connection?
Earthquakes
Injection wells
Mediterranean Sea
ΔPmax=0.8 MPa

## Slide 4
During the 15 days of injection, the increase in pore pressure was the main cause of the Amposta fault movement
The gas continued to destabilize the Amposta fault after the stop of injection because its low density exerts a vertical buoyancy force
Amposta fault
Gas injection accelerated the movement of the critically stressed Amposta fault, producing progressive aseismic slip
Vertical loading
Horizontal unloading

## Slide 5
The slow, aseismic slip of the Amposta fault caused the movement of another, deeper fault that produced the earthquakes felt by the population
Amposta fault
Deep fault
Stiff rocks, generate earthquakes when they break
Soft rocks, progressively deformed
Injected gas
The deep fault was destabilized by shear-slip stress transfer and transient slip-driven pore pressure changes
Vilarrasa et al. (2021) GRL

## Slide 6
This project has received funding from the European Research Council (ERC) under the European Union’s Horizon 2020 research and innovation programme (grant agreement No 801809)
Questions?
This presentation reflects only the author's view and the Agency and the Commission are not responsible for any use that may be made of the information it contains.