## Slide 1: GIS-based Aquifer Thermal Energy Storage (ATES) systems potential assessment in Spain
Adela Ramos Escudero
Martin Bloemendal
May 23th 2022

## Slide 2: ATES potential areas identification.
1.1 - Hydrogeological conditions
Aquifers with potential for thermal use:
High permeability aquifers (fissured and fractured)
Acceptable depth
Geothermal energy potential evaluation report. PER 2011-202. Institute for the Diversification and save of energy. Spain.
1
VALENCIA
1.2 - Climatic conditions
Balance heating and cooling needs based on climatic zones.
Residential & Tertiary sector
38%
Total Surface

## Slide 3: ATES market potential.
2
  Towns with pot. aquifers
26%
  Total population living in pot. areas
53%
  Towns with excellent conditions
13%
  Residential sector
  Total population in Spain
28%
  Aquifers with thermal use
  Potential aquifers vs population
  in towns (>1,500 inhabitants per km2)

## Slide 4: Feasibility study.
Two case studies selected:
For Residential and Tertiary
Hydrogeological parameters:
  Water quality (<50 meters)
  Water freshness, avoid salinization
  Groundwater flow. Low velocities.
Bloemendal, M., & Hartog, N. (2018). Combining climatic and geo-hydrological preconditions as a method to determine world potential for aquifer thermal energy storage
3
Parameter | Unit | Tertiary | Residential
Surface | m2 | 10,000 | 2,000
Heating capacity | kW | 54 | 6
Heating energy demand | MWh | 140 | 19.4
Cooling capacity | kW | 400 | 50
Cooling energy demand | MWh | 420 | 20

## Slide 5: Economic and GHG reduction potential.
4
63%
68%
10 years
6,503 €
18 years
1,483 €
Payback Period
Greenhouse Gas Emissions savings

## Slide 6: Thank you very much! adela.ramos@upct.es