## Slide 1: New cosmogenic nuclide dating laboratory in CENIEH, Spain Toshiyuki Fujioka (toshiyuki.Fujioka@cenieh.es), L. Miguens, J. Iglesias, F. Jiménez, M.I. Sarró, J.M. Parés CENIEH, Burgos, Spain
Take home:
First, routine, full chemistry lab for cosmogenic nuclides in Spain
Focus on 26Al/10Be burial dating and meteoric 10Be
Competitive access every year
Budget friendly
Consultation on lab development & application, e.g., 10Be, 26Al, 53Mn, 21Ne, 36Cl
GM2.5 What’s new with cosmogenic nuclides? EGU 2022, 26/5/22

## Slide 2
ARCHAEOLOGY
PALEOBIOLOGY
GEOCHRONOLOGY & GEOLOGY
  ESR
  OSL
  Paleomagnetism
  U-series
  Cosmogenic nuclides
CENIEH = National Research Center on Human Evolution
EARTH SCIENCES
Landscape
Environment
Paleoclimate
Tectonics
Natural disaster (Geohazard)
…
HUMAN EVOLUTION

## Slide 3
Quartz extraction & Be-Al separation at CENIEH
Quartz extraction from rock, sediment, artefacts
• Crushing & sieving
• Magnetic separation
• Density separation
• Acid leaching (e.g., aqua-regia, H2SiF6, HF)
• Magnetite powder
Methods are selected & modified, depending on material types, approaches (exposure, burial, erosion) and age-range, to optimise process time.
Be-Al extraction
• Dissolution in HF
• HF fuming (boron elimination)
• Anion & cation exchange chromatography modified from Stone/Ditchburn’s H2SO4-HCl method (Fe, Ti elimination & Be-Al separation)
• pH control with suprapur NH3(aq.)
• Intrinsic Al measured by in-house ICP-OES
Currently, Be- and Al-hydroxides are sent to AMS facilities for calcination & press into AMS holder. This last step is under development in CENIEH.
Ancillary analysis
Supporting facilities are available in CENIEH, including:
• Laser diffraction grain size analyser
• ICP-MS, -OES
• XRD, XRF, Raman spectroscopy
• SEM
• Thin section
Heavy-liquid density separation
Magnetic separator
2 x 180 cm-wide scrubber fume hoods
Savillex vessels & Teflon-coated graphite hotplate
for HF evaporation
ICP-MS (Neptune & Element) & ICP-OES lab
XRF, XRD, Raman spectrometry lab
SEM, micro CT lab

## Slide 4
Procedure tests
9Be carriers & chemistry procedural background
• Several commercial Be standards & non-commercial mineral spikes (beryl, phenakite) were tested
• Mineral spikes are excellent (10Be/9Be ~4 e-16)
• Some commercial spikes acceptable (~ 5 e-15)
• CENIEH milli-q & suprapur NH3 do not raise background
• Procedural blanks are also good (10Be/9Be ~2-4 e-15) with likely 10Be source prior to cation column (i.e., quartz dissolution, HF fuming and/or anion column)
Column chemistry (adopted from J. Stone (2001), Ditchburn & Whitehead (1994))
Anion exchange (using Biorad 1-x8 200-400# resin):
• >99% Fe is isolated from Be and Al
Cation exchange (using Biorad 50W-x8 200-400# resin):
• >99% Ti is isolated from Be and Al
• Beryllium & aluminium yields are ~90-95%
• ~5% Al is leaked into Be fraction?
Standard batch & process time:
• 9 sample + 1 blank per batch
• 20 g quartz (w/ Al <200 ppm) & 300 ug 9Be spike
• Quartz extraction time, ~1 week to 2 months
• Be-Al extraction time, < 3 weeks
Performance:
• Final BeO contains Mg (~35%) & Al (~20-25%)
• Final Al2O3 contains Ca (15-25%)
• Initial results proved BeO oxide purity, where BeO– ion source output is generally ~40-80% of standard materials in the same AMS run
Direct ppt at CENIEH
Cation exchange onward
Full procedural blanks
Direct ppt (solutions were sent to established AMS labs for oxidation)
Commercial spikes
Mineral
spikes
Final oxide inventory
Cation exchange test
Be blank tests

## Slide 5
PROJECTS
Archaeological/Paleoanthropology
• Oldowan-Acheulean transition, long-term human evolution (H. habilis & H. erectus) & paleoclimate reconstruction in East Africa (e.g., Olduvai Gorge, Lake Tanganyika) [collab. w/ CENIEH, Spanish Research Council Madrid, ICDP]
• Pan-Mediterranean human migration & settlement (e.g., Armenia, Israel, Argeria, Morocco) [collab. w/ CENIEH, IPHES Tarragona, Nat. Acad. Sci. Armenia, Uni Haifa Israel]
• Arrival & distribution of Acheulean culture in Iberian Peninsula in mid Pleistocene [collab. w/ CENIEH]
Gran Dolina, Atapuerca
Late Miocene terrace, upper Duero River
Glacial boulder, Aneto, central Pyrenees
Paleoclimate history in Pyrenees [collaboration w/ IPE Zaragoza]
• Glacial history in central Pyrenees since 60 ka through Holocene & Little Ice Age
• Approach with cosmogenic exposure dating
• Combined with 14C, OSL in glacial lake deposits
• Implication to paleoclimate conditions in the context of Atlantic & Mediterranean influence
Landscape evolution in northern Iberian Peninsula [collaboration w/ CENIEH, National Museum Madrid]
• Duero & Ebro basin, endorheic-exorheic transition, incision & fluvial terraces during Plio-Pleistocene
• Approach with cosmogenic (simple & isochron) burial dating
• Combined with other dating methods, e.g., OSL, ESR, p-mag
ATAPUERCA [collaboration w/ CENIEH, IPHES Tarragona, Uni Complutense de Madrid]
• Multi-level cave complex
• 1.2 m.y. human evolution (including oldest Euro human fossil & H. antecessor)
• Approach with cosmogenic (simple & isochron) burial dating
• Combined with other dating methods, e.g., OSL, ESR, p-mag
• Correlation with fluvial terraces

## Slide 6
1.48 ± 0.25 Ma
Advantage:
- Overcome uncertainties of ‘simple’ cosmogenic burial dating
- Direct dating = Improved reliability (cf. ESR on teeth)
Disadvantage:
- Destructive
- Labor intensive

## Slide 7: Contact: Email: (toshiyuki.Fujioka@cenieh.es) Twitter: @ToshiFujioka Instagram: toshifujioka_cosmogenic Facebook: Toshiyuki Fujioka
Take home:
First, routine, full chemistry lab for cosmogenic nuclides in Spain
Focus on 26Al/10Be burial dating and meteoric 10Be
Competitive access every year
Budget friendly
Consultation on lab development & application, e.g., 10Be, 26Al, 53Mn, 21Ne, 36Cl
Acknowledgement:
• CEREGE: Régis Braucher, ASTER Team
• DREAMS: Anton Wallner, Silke Merchel, Konstanze Stuebner, Georg Rugel, Johannes Lachner
• SUERC: Derek Fabel, Ángel Rodés
• CologneAMS: Steven Binnie
• CNA Sevilla: Jóse María López Gutiérrez, Elena Chamizo