## Slide 1: Quantifying the spatial and temporal non-CO2 effect of aviation by using algorithmic climate change functions
Simone Dietmüller, Sigrun Matthes, Volker Grewe, Katrin Dahlmann, Patrick Peter, Hiroshi Yamashita
DLR, Institute of Atmospheric Physics, Oberpfaffenhofen, Germany
TU Delft, The Netherlands
EGU 2022, 25/05/2022

## Slide 2
Climate impact of aviation emissions
Warming
Cooling
Radiation forcing (RF) from individual aviation emissions
Lee et al. 2021
Non-CO2 emissions responsible for 2/3 of aviation’s total RF
Emission of aviation
Aviation emission impact climate by CO2 and non-CO2 effects (e.g. ozone, contrail-cirrus, aerosol)

## Slide 3: Algorithmic Climate Change functions (aCCFs)
aCCFs characterize sensitivity of atmosphere to aviation emissions at specific location (position, altitude) and time.  MET product for climate-optimized trajectory planning
METEO
Prototype algorithmic climate change functions (aCCFs) of non-CO2 effects give climate impact of aviation emissions at a specific location and time
aCCFs can be calculated for contrail-cirrus, water vapour, NOx-induced changes of ozone and methane
aCCFs enable calculating climate impact based on meteorological parameters from numerical weather prediction data
Climate change from meteorological input data by using aCCFs
aCCFs
Contrail aCCF
NOx-induced aCCF
Water vapour aCCF
[K/kg(fuel)]
[K/kg(NO2)]
[K/km(contrail)]
Calculated by mathematical formulas -> computational efficient
Water vapour and NOx induced aCCF is positive (warming)
Contrail (daytime) aCCF warming/cooling impact in areas where contrails can form
geopotential
FLYATM4E WP1 - Advisory Board 19/05/22

## Slide 4: Analysis of NOx-induced aCCFs
June 2018, 12 UTC, ERA5 0.28°
December 2018,12 UTC, ERA5 0.28°
250 hPa
Vertical cross section at 0°
NOx induced aCCF positive (warming)
Variation in NOx aCCF with
  different synoptical conditions
  different season (Higher values in summer. Day to day variability higher in winter)
  with cruise altitude (vertical gradients higher in winter)

## Slide 5: Analysis of contrail aCCFs
June 2018, 12 UTC, ERA5 0.28°
December 2018, 12 UTC, ERA5 0.28°
250 hPa
Vertical cross section at 0°
Contrail (daytime) aCCFs warming or cooling effect, in areas of contrail formation
Strong day-to-day variation in contrail aCCFs
Seasonal variation in contrail aCCFs:
  contrail formation higher in winter
  more areas with cooling contrails in winter
Variation with cruise altitude

## Slide 6
Summary
Generation of merged non-CO2 aCCFs
aCCFs enable climate-optimized trajectory planning
Individual water vapour, NOx induced and contrail-cirrus aCCFs show large variations with different meteorological situations, seasons and altitudes
Merged non-CO2 aCCFs are generated. Large influence of contrails aCCFs.
With merged aCCFs specific weather situations with large mitigation potential can be identified.
Merged non–CO2 aCCFs combine contrail-cirrus, total NOx and water vapour aCCFs (taking assumptions on technical specifications of emission indices and physical climate metric)