## Slide 1
Turbulent transfer and concentration statistics in a street canyon with tree planting
Sofia Fellini
Annika Vittoria Del Ponte, Marilina Barulli, Luca Ridolfi, Lionel Soulhac, Massimo Marro, and Pietro Salizzoni
sofia.fellini@ec-lyon.fr
https://www.researchgate.net/profile/Sofia-Fellini

## Slide 2
Temperature regulation
Filters for pollutant particles
Regulate water flow
Physical and mental health
Urban biodiversity
What about the aerodynamic effect?
Boulevard in Paris © K.G.Hawes
Tree planting in urban areas
Sofia Fellini (DIATI and LMFA)
Turbulent transfer and concentration statistics in a street canyon with tree planting
Sofia Fellini
Notes: Transport and mixing processes in the urban environment are characterized
168 by complex uid structures due to the interaction between the atmospheric
169 ow and the city. The presence of buildings and vegetation highly aects the
170 structure of the urban boundary layer, characterized by the generation of a
171 shear layer at the top of the canopy, wake diusion behind buildings, and form
172 drag due to the pressure dierences across the roughness elements (Roth, 2000).
173 Moreover, the ow eld in the streets is altered by the advectiveconvective uxes
174 due to the dierential solar irradiance on building walls and to the heat sources
175 related to human activities

## Slide 3
Realistic interaction between turbulent flow and urban canopy
Separation between the flow within and above the canopy
The experimental setup
Sofia Fellini (DIATI and LMFA)
Turbulent transfer and concentration statistics in a street canyon with tree planting
Sofia Fellini

## Slide 4
Scale 1:200
Large street canyon with height 10 cm, width 20 cm, length 50 cm (H/W=0.5)
Two lateral rows of trees, with space between 14 cm and space from the buildings 3 cm
Linear source at street level emitting Ethane as passive scalar
Sofia Fellini (DIATI and LMFA)
The experimental setup
Sofia Fellini (DIATI and LMFA)
Turbulent transfer and concentration statistics in a street canyon with tree planting
Sofia Fellini

## Slide 5
DRAG COEFFICIENT
Characterization of model trees
AERODYNAMIC POROSITY
Sofia Fellini (DIATI and LMFA)
Turbulent transfer and concentration statistics in a street canyon with tree planting
Sofia Fellini

## Slide 6
Mean concentration field
500
400
300
200
100
0
Flame Ionization Detector (FID)
Sofia Fellini (DIATI and LMFA)
Turbulent transfer and concentration statistics in a street canyon with tree planting
Sofia Fellini

## Slide 7
The ventilation efficiency
Sofia Fellini (DIATI and LMFA)
Turbulent transfer and concentration statistics in a street canyon with tree planting
Sofia Fellini

## Slide 8
Mean velocity field
-1
-0.5
0
0.5
1
1.5
-0.3
-0.2
-0.1
0
0.1
0.2
0.3
-0.2
-0.1
0
0.1
0.2
0.3
Sofia Fellini (DIATI and LMFA)
Turbulent transfer and concentration statistics in a street canyon with tree planting
Sofia Fellini
0
Z [mm]
Z [mm]
Z [mm]
Y [mm]
Y [mm]
Y [mm]
20
40
60
80
100
120
20
40
60
80
100
40
60
80
100
20
-300
-200
-100
-0
100
200
300
-300
-200
-100
-0
100
200
300
-300
-200
-100
-0
100
200
300
Laser
Doppler
Anemometer
(LDA)

## Slide 9
TKE and mass fluxes
0
0.1
0.2
0.3
0.4
-40
-20
0
20
40
-30
-20
0
10
20
-10
30
Z [mm]
Z [mm]
Z [mm]
Y [mm]
Y [mm]
Y [mm]
20
40
60
80
100
120
20
40
60
80
100
40
60
80
100
20
-300
-200
-100
-0
100
200
300
-300
-200
-100
-0
100
200
300
-300
-200
-100
-0
100
200
300
LDA
+
FID
Sofia Fellini (DIATI and LMFA)
Turbulent transfer and concentration statistics in a street canyon with tree planting
Sofia Fellini

## Slide 10
Sofia Fellini (DIATI and LMFA)
Turbulent transfer and concentration statistics in a street canyon with tree planting
Sofia Fellini
Work in progress
Vertical flux
at roof
Spectra at roof
Statistical analysis of concentration signal
Increase of turbulent flux at small scales with trees
Gamma distribution with constant
Turbulent mass flux becomes dominant with trees