## Slide 1: Large-scale tank experiments simulating soil aquifer treatment Assessing the attenuation potential of emerging organic compounds and nutrients during managed aquifer recharge Marcel Horovitz1,2, Edinsson Muñoz-Vega2, Teresa Leitão1, Christoph Schüth2, Stephan Schulz2 1 Laboratório Nacional de Engenharia Civil (LNEC), Hydraulics and Environment Department, Water Resources and Hydraulic Structures Unit, Avenida do Brasil 101, 1700-066 Lisbon, Portugal 2 Technical University of Darmstadt, Institute of Applied Geosciences, Hydrogeology Group, Schnittspahnstraße 9, 64287 Darmstadt, Germany

## Slide 2
OECD (2019), Pharmaceutical Residues in Freshwater: Hazards and Policy Responses
https://sswm.info/water-nutrient-cycle/reuse-and-recharge/hardwares/recharge-and-disposal/soil-aquifer-treatment (accessed: 22.04.2022)
Introduction – SAT-MAR
Soil Aquifer Treatment (SAT) is one of several techniques of Managed Aquifer Recharge (MAR) using treated wastewater effluent as feedwater to recharge groundwater resources in water scarce regions and providing intermediate storage for later use
SAT-MAR as tertiary treatment for secondary treated wastewater effluents:
  Risks due nutrients (N, P) and emerging organic compounds (e.g., pharmaceuticals)
OECD (2019), Pharmaceutical Residues in Freshwater: Hazards and Policy Responses
Alam et al. (2021,)Managed aquifer recharge implementation criteria to achieve water sustainability

## Slide 3
Edinsson Muñoz-Vega (PhD Thesis) – Role of organic matter, redox processes and biofilm formation in the transport of selected emerging organic contaminants
UNESCO (2021) – MANAGING AQUIFER RECHARGE: A Showcase for Resilience and Sustainability
Small Scale – Column Experiments
Field Scale – SAT-MAR Sites
Attempt to bridge the gap:
Sand Tank Experiments
Motivation for large-scale sand tank experiments simulating SAT-MAR
Processes due to mixing of groundwater and infiltrating treated wastewater
High resolution monitoring and sampling
Controlled conditions
Dry and wet cycles
Risk assessment
Greskowiak et al. (2017), The uncertainty of biodegradation rate constants of emerging organic compounds in soil and groundwater - A compilation of literature values for 82 substances

## Slide 4
Experimental Facility – Design of Large-Scale Sand Tanks
2.76 m
2.5 m
1.0 m
0.5 m
Three large-scale sand tanks made from HDPE (high density polyethylene)
fine sand
SAT-Basin
Unsaturated Zone
Saturated Zone
(GW flow)
Dry and wet cycles (3 days infiltration, 4 days drying)
0.5 m
Feed waters:
  Treated wastewater effluent (Lisbon treatment plant)
  Groundwater (LNEC campus)

## Slide 5
Numerical Model
Feflow Model
Ksat ~ 1.2 * 10-4 m/s
Porosity = 0.33
Dispersivity
  Longitudinal = 1 cm
  Transversal = 0.1 cm
Van Genuchten Parameter
  Alpha = 3.6 m-1
  N = 4.7
  Theta_s = 0.33
Soil moisture probes
Pressure transducer

## Slide 6
Timestep = 1.5 days
Timestep = 20 days
45 cm
25 cm
45 cm
25 cm
45 cm
25 cm
5 cm
5 cm
5 cm
Timestep = 1 day
Redox probe (18 readings) in the infiltration section (white dashed line)
Numerical Model vs. Observation of Redox Potential

## Slide 7
25 cm
40 cm
5 cm
50 cm
Timestep = 13.5 days
Timestep = 27 days
25 cm
40 cm
5 cm
50 cm
Numerical Model vs. Observation of Redox Potential
Redox probe (18 readings) near the end of the sand-tank (white dashed line)

## Slide 8
Highly equipped sand tank to study mixing processes - Ongoing
In total 90 redox sensors:
  2 vertical redox probes with 18 sensors each
  3 horizontal redox probes with 18 sensors each
Soil moisture probes in 5 depths
Electrical conductivity logger at inflow and outflow
Sampling in saturated zone:
  Micropiezometers at 3 positions and screened in 3 depths
Sampling in vadose zone:
  Suction cups at 3 depths
Suction Cup
Redox probes
Soil moisture probes
Pressure transducer
Electrical conductivity logger

## Slide 9
Samples to be analyzed for:
  Major ions
  Trace metals
  DOC
  Pharmaceuticals (carbamazepine, diclofenac, ibuprofen, naproxen, gemfibrozil, and triclosan) with wide range of physicochemical parameter and degradation potential
Dissolved organic matter characterization via fluorescence spectrometry
  Humic and fulvic like composition in groundwater
  Protein-like (readily degradable) and slightly humic-like in treated wastewater effluent
  Outflow shows mixing and might show degradation of protein-like components
+
+
+
+
+
+
Highly equipped sand tank to study mixing processes - Ongoing

## Slide 10
Mixing processes of infiltrating treated wastewater and groundwater observable in redox signal
Reaching nitrate reducing conditions
Highly equipped sand tank – Ongoing – Preliminary Results of Redox Probes

## Slide 11: Thank you for your attention
The MARSoluT ITN has received funding from the European Union’s
Horizon 2020 research and innovation programme under the
Marie Skłodowska Curie grant agreement No 814066.
Further information on MARSoluT project:
https://www.marsolut-itn.eu/
For questions: mhorovitz@lnec.pt