## Slide 1: Physicochemical parameters and stable isotope composition of water in Northern Mara Sub-Goldfield, Tanzania: Implications for groundwater-surface water interaction
Justine L. Myovela a,b,*, Godson Godfray b and Mohamedi Salimu b
a University of Pécs, Institute of Geography and Earth Sciences, Department of Geology and Meteorology, Ifjúság u. 6, Pécs, 7624, Hungary
b University of Dodoma, College of Earth Sciences and Engineering, Department of Geology, P. O. Box, 11090, Dodoma, Tanzania
*Corresponding author: justine1@gamma.ttk.pte.hu
Jung et al., 2020

## Slide 2
1.INTRODUCTION
Groundwater-surface water interaction is crucial for both physical and chemical fluxes in the hydrologic cycle.
Contamination of water resources through anthropogenic activities has been a major environmental concern (Nisi et al., 2014; UN-water, 2011)
Motivation:
70% of industrial and mine wastes in developing countries contaminate the existing water resources.
(UN-water, 2009)
Quinn et al., 2016

## Slide 3: OBJECTIVES
To conduct water quality assessment around Northern Mara Sub-goldfield (NMSF).
To determine spatial variation of δ18O and δ2H of groundwater and surface water sources.
River Mara (Photo by Justine L. Myovela)

## Slide 4
Henckel et al., 2016
2.STUDY AREA
Northern Mara Sub-gold Field (NMSF) is situated in Tarime district, Mara region, Northwest Tanzania.
This gold-rich field is within the sulfide ore system in Musoma-Mara greenstone belt, a part of Lake Victoria Fields (Henckel et al., 2016)
Google Earth image, 2020

## Slide 5: OBJECTIVES
3.METHODS
26 water samples: during rainy season (rivers, shallow & deep groundwater, dug wells and tailings pond)
HATCH meter: pH, Electrical conductivity (EC), Total Dissolved Solute (TDS) and Total hardness.
H-O Isotopes analysis-Liquid Isotope Analyzer (V-SMOW)

## Slide 6: OBJECTIVES
Key message; Most drinking water sources meet
the recommended standards (WHO & TBS)
except; 10-Shallow well east of Ingwe dam
12-Shallow well south of Tailings pond
21-Kegonga community shallow well
22-Matongo community shallow well
4.RESULTS: WATER QUALITY
Tailings ponds
Myovela et al., in prep

## Slide 7
4.RESULTS: WATER QUALITY
Affected water sources
10-Shallow well east of Ingwe dam
12-Shallow well south of Tailings pond
21-Kegonga community shallow well
22-Matongo community shallow well
Myovela et al., in prep
22
10
12
21
Shallow wells are more vulnerable to contamination than deep wells.

## Slide 8: OBJECTIVES
4.RESULTS: δ18O AND δ2H OF WATER SAMPLES
Wide isotopic variations
δ2H; -28.5 to 21.4 ‰
δ18O; -5.37 to 2.37 ‰
The slope of LMWL(δ2H = 5. 9 δ18O + 5.51; R2=0.94) is slightly lower than the slope of GMWL (δ2H = 8.2 δ18O + 11.27; R2=1)
Key message;
Majority of studied water samples have been isotopically modified.
Myovela et al., in prep

## Slide 9: OBJECTIVES
5.DISCUSSION: WATER INTERACTION
-Several shallow and groundwater sources have similar isotopic signatures indicating mixing at a certain stage in their hydrological circle.
-Complex hydrological regime
Adapted from Yang and Han, 2020
Myovela et al., in prep
Myovela et al., in prep

## Slide 10: OBJECTIVES
6. FUTURE WORK AND CONCLUSION
FUTUTE WORK
Groundwater modelling to depict the depth of contamination and other possible sources of contaminations.
CONCLUSIONS
Most drinking water sources meet the recommended standards set by WHO &TBS except few water sources such as Kegonga shallow well.
Shallow wells are more vulnerable to contamination than deep wells.
Several shallow groundwater sources have likely been recharged by more evaporated sources for example Shallow well south of Tailings Pond.

## Slide 11
THANK YOU FOR LISTENING

## Slide 12: OBJECTIVES
REFERENCES
Abu Jabal, M. S., Abustan, I., Rozaimy, M. R., & El Najar, H. (2018). The deuterium and oxygen-18 isotopic composition of the groundwater in Khan Younis City, southern Gaza Strip (Palestine). Environmental Earth Sciences, 77(4)
Henckel J, Poulsen K, Sharp T, Spora P. Lake Victoria Goldfields. Episodes 2016;39:135-154
Jung, Koh, Kim, Jeen, & Lee. (2020). Stable Isotopes of Water and Nitrate for the Identification of Groundwater Flowpaths: A Review. Water, 12(1), 138
Nisi, B., Raco, B., & Dotsika, E. (2014). Groundwater Contamination Studies by Environmental Isotopes: A review. Threats to the Quality of Groundwater Resources, 115–150.
Quinn, N.W.T,., Parrot, S., Farley, M (2016). Conceptual water budget analysis for screening agricultural and wetland water management projects.
Rozanski, K., Araguás-Araguás, L., & Gonfiantini, R. (1993). Isotopic Patterns in Modern Global Precipitation.
UN-Water Annual Report 2009.
UN-Water Annual Report 2011.
Yang, K., & Han, G. (2020). Controls over hydrogen and oxygen isotopes of surface water and groundwater in the Mun River catchment, northeast Thailand: implications for the water cycle.