## Slide 1
Lauren Biermann, Louise Schreyers, Tim van Emmerik, Thanh-Khiet Bui, Yangrong Ling, and Davida Streett
24 May 2022
Finding Riverine Plastics in Floating Plant Patches using Worldview-3 Satellite Imagery

## Slide 2
Main take-away messages
2. Satellite imagery shows plastic in rivers
3. Direct sensing need to be combined with field-based estimates
Due to spatial resolution limitation, estimates of plastic densities are still off by several orders of magnitude!
1. Plastics have distinct spectral signatures
Can be detected both in lab and field with hyperspectral/multispectral sensors
High resolution multispectral imagery, e.g.: Worldview-2 and 3

## Slide 3
Plastics have distinct spectral signatures (lab)
Count 12 patches (patch > 0.1 m2)
Linear discriminant analysis weight to separate vegetation and plastic items overlaid with central wavelengths and bandwidths of the Wordlview-3. Source: Tasseron et al., 2021
Leveraging Yellow and Red band for distinguishing vegetation and plastic items

## Slide 4
Plastics have distinct spectral signatures (field)
Count 12 patches (patch > 0.1 m2)
Source: Tasseron et al. (in review)
Same curve than in the lab, but signal is less strong
Attenuation probably due degraded state of items

## Slide 5
Satellite imagery shows plastics in hyacinths (space)
Count 12 patches (patch > 0.1 m2)
Direct detection of floating debris in the Saigon river. Source: Worldview-3 image from 3 March 2020 @2020, DigitalGlobe.
Reflectance values for Worldview-3 bands for floating debris, water and hyacinths content (n = 56)
Worldview-3 optical multispectral sensor: from Visible to Near-Infrared (400-1040 nm)
Spatial resolution of 1.24 m
Notes: Distinct spectral characteristics

## Slide 6
Satellite imagery shows plastics in accumulation zones (space)
Count 12 patches (patch > 0.1 m2)
Example of satellite imagery used to identify plastic carpet locations and monitor their dynamics in the Citarum River (Indonesia). Credits: Copernicus ESA (Sentinel-2) and Maxar.
Notes: Distinct spectral characteristics

## Slide 7
Overview of Remote Sensing techniques for plastic detection
Count 12 patches (patch > 0.1 m2)
Notes: Distinct spectral characteristics

## Slide 8
Next steps in detecting plastic items/aggregations
Scene acquisition: clouds!
Very High Resolution: cost of scenes
Can only detect large accumulations: 1.24 meter of spatial resolution
Plastic densities estimated at: 5.8 × 101 items km−2
(three orders of magnitude lower than with UAV-based estimates)
Only 1% of items are above 1 meter of size!
Validation with ground-truth data difficult to obtain
Notes: Challenges are technical but also logistical

## Slide 9
Thank you!