## Slide 1: Presentation On Reliability-Based Hybrid Metaheuristic Optimization Model for the Design of Two Loop Network Under Mechanical Uncertain Scenarios
by
Seelam Naga Poojitha1 and Vinayakam Jothiprakash2
1Research Scholar, 2Professor, Indian Institute of Technology, Bombay, Powai, Mumbai, Maharashtra, India, 400076
Correspondence E-mail: pooji.pujitha@gmail.com, vprakash@iitb.ac.in
Vienna, Austria and Online
Session HS3.8, Presentation: EGU22-12971

## Slide 2
Introduction
Objective
Methods
Methodology
Case study
Results and Discussions
Conclusions
Contents

## Slide 3
Introduction
Water supply system (WSS) is worldwide valuable public infrastructure asset used for conveying water from source to communities (Alegre and Coelho 2012)
Water distribution network (WDN) is the part of WSS that transports treated water from supply source at treatment plant to the communities (Elshaboury et al. 2020)
WDN design alone accounts for about 50 to 70% of total cost invested for the design of WSS (Zhao 2003)
Its operation, maintenance, and rehabilitation involve significant financial investments (Ezzeldin et al. 2014)
Major initial capital investment of WDNs is on the installation, inspection, and maintenance of pipes (Ghesis et al. 2016)
The study focuses on the economical design of WDNs, considering network pipes as the primary design variables

## Slide 4
Contd.,
Combinatorial optimization problem (Suribabu 2010)
          e.g. TLN
          Number of Pipes = 8
          Number of commercially available pipes = 14
          Possibilities = 148
          Enumeration - Not tractable
          Discrete Feasible solution sets (due to nonlinear relationship)
Non deterministic polynomial time hard (NP-hard) problems (Yates et al. 1984)
          Easy to verify but, difficult to solve
          The quest for the formulation of a new efficient, global convergence based optimization technique is still gaining momentum
Figure 1. Layout of TLN
Alperovits and Shamir (1977))
Nature of the WDN Design Problem

## Slide 5
Reliability of the WDN is the probability that the network is able to deliver the required demands within the minimum required pressure conditions to the communities (Su et al. 1990)
In its lifetime liable to mechanical failures and vulnerable to hydraulic uncertainties
  Mechanical failure refers to the failure of WDN components like pipes, pumps, and valves, etc.
Hydraulic failure occurs due to insufficient heads available at various demand nodes because of uncertainty in nodal demands and pipe roughness (Bao and Mays 1990)
“For the effective design of WDNs it is necessary to consider the reliability of the system”
Contd.,
Reliability of WDN

## Slide 6
Objective of the Study
Reliability-based optimal design of WDNs using metaheuristic optimization model under mechanical uncertain scenarios
Methods
A reliability-based hybrid metaheuristic optimization model is formulated
Optimization model
Hybrid optimization technique with combined features of evolutionary and swarm intelligence techniques, DE-KHA is considered
Simulation model
EPANET simulation tool Rossman (2000) that simulates the WDNs hydraulic properties, nodal pressure head and actual demand delivered at the demand nodes is considered
Reliability model
Reliability of the WDN is assessed considering the pipe failure using the minimum cut set method

## Slide 7
Contd.,
Optimization Model
Differential evolution (DE)
(Storn and Price 1995)
Operators : (1) Mutation, (2) Crossover, and (3) Selection schemes
Excellent exploration abilities – Diversified search (Das et al. 2005)
Krill herd algorithm (KHA)
(Gandomi and Alavi 2012)
Operators : (1) Foraging motion, (2) Neighbor induced motion, and (3) Physical diffusion
Excellent exploitation abilities – Intensified search
Figure 2. Krill Herd
(Source:https://images.squarespacecdn.com/content/v1/5ba0efb9266c077060b48c68/1537849392860H6IMD6H4JUC52OIHVKC6/Krill_Coronado.jpg?format=1000w)
Hybrid metaheuristic algorithm DE-KHA
(Poojitha and Jothiprakash 2022)

## Slide 8
Framework of Optimization Model
Initial random population
Improve population using DE mutation and crossover schemes by exploring with available information
Fitness evaluation
Improve population using KHA schemes by exploiting the available information
Selection scheme
Fitness evaluation
Population-based evolutionary search
Optimal solutions
Perform until the termination criterion
Selection scheme
Figure 3. Darwin’s principle of survival of fittest
Source: https://towardsdatascience.com/making-a-robot-learn-how-to-move-part-1-evolutionary-algorithms-340f239c9cd2
Contd.,

## Slide 9
Hydraulic Infeasibility
Maximum pipe closure combinations
no
Stop
Compute probability of failure of each pipe
Apply pipe closure combinations
For pipe closure combination = 1
Simulate network hydraulic properties
Record minimum cut set
Estimate reliability of WDN
Start
Calculate failure probability of minimum cut sets
Pipe closure combination + 1
yes
no
yes
Reliability Model
Approach : Minimum cut set
A minimum cut set is a component or set of system components which, when failed, causes failure of the system (Billinton and Allan 1983)
Probability of failure of pipe i is determined using Poisson probability distribution
The expected number of failures of ith pipe in an year is given as
is the expected number of failures of ith pipe in an year per unit length, (Su et al. 1987)
Reliability, Ri = 1 -
Contd.,

## Slide 10
yes
Assessment of mechanical reliability
Start
Optimization model
Simulation model
Reliability model
Capital cost of WDN
Termination criteria
Is + 1
Capital cost of WDN
Stop
yes
Is = 1
Alternate diameter set
Hydraulic properties
Penalty is not added
no
Penalty is added
no
R < Rmin
Note:
di and li are the diameter and length of ith pipe
PM is the static penalty multiplier
Is is the iteration size
R is the reliability of WDN
Rmin is the predefined minimum reliability of the WDN, which in the present case is varied from 0.6 to 0.8 with a step size of 0.1
Methodology
S.t Energy, Hydraulic, and reliability constraints

## Slide 11: Case Study
TLN is a hypothetical network first studied by Alperovits and Shamir (1977).
It is a two looped network with 8 pipes each of 1000 m length, 6 demand nodes and a single reservoir with a fixed head of 210 m (CWS, Exeter)
The minimum pressure head requirement at each demand node is 30 m.
Two-Loop Network (TLN) Benchmark Problem
Figure 4. Layout of TLN
(Alperovits and Shamir (1977))
Table 1. Details of TLN
No. of Links | No. of commercially available options | Possible options | Hazen Williams constant
8 | 14 | 148 (1.47578 ×109) | 130

## Slide 12
Results and Discussions
Results of sensitivity analysis
To calibrate the optimal (best) values for model parameters guidelines of Hofmann et al. (2004) and Gandomi and Alavi (2012) are followed
Table 2. Calibrated parameter values of DE-KHA
Mutation factor | 0.8
Crossover probability | 0.5
Foraging velocity | 0.3
Maximum induced speed | 0.08
Maximum diffusion speed factor | 0.6
Sensing distance factor | 0.9
Time step | 0.9
Number of krill (population size) | 300
Maximum iteration size | 200
Penalty Multiplier | 107

## Slide 13
Contd.,
Figure 5. Convergence plot showing the variation of the optimal cost obtained over iterations with Rmin = 0.8 and 0.9

## Slide 14
Figure 6. Convergence plot showing the variation of the optimal cost obtained over iterations with Rmin = 0.8 and 0.9
Contd.,

## Slide 15
Figure 7. Tradeoff of capital cost and mechanical reliability of TLN with Rmin varied from 0.6 to 0.9
Contd.,

## Slide 16
Figure 8. Tradeoff of capital cost and mechanical reliability with Rmin varied from 0.6 to 0.9
Contd.,

## Slide 17
Figure 9. Tradeoff of capital cost and mechanical reliability with Rmin = 0.6
Contd.,

## Slide 18
Conclusions
The computation results on successful application of the reliability-based metaheuristic optimization on TLN
Demonstrates the efficacy of the optimization model in locating the best possible design costs with less computational effort
Of 200 maximum iterations considered for a single run, irrespective of the Rmin considered, the model converged to best solutions in just 24 to 63 iterations
For the same design cost, discrete feasible diameter options are located with discrete mechanical reliability values
The feasible designs options with a wide range of mechanical reliability varying from 0.42837 to 0.94921 are proposed
The study suggests the explicit consideration of reliability and surrogate measures for robust design of WDNs by extending the hybrid model as a multi-objective framework

## Slide 19
Any Questions, comments, or Suggestions?

## Slide 20
Thank You All for your Attention!