## Slide 1
MiniPINS – Design status and the latest activities
Maria Genzer1, Maria Hieta1, Antti Kestilä1, Harri Haukka1, Ignacio Arruego2, Victor Apéstigue2, Alejandro Gonzalo Melchor2, Miguel González-Guerrero2, Javier Martínez Oter2, Álvaro de Pedraza2, Almudena García-Llases2, Gustavo Rodríguez2 Jose Antonio Manfredi3, Cristina Ortega4, Carmen Camañes4, Manuel Dominiguez-Pumar5,Servando Espejo6, Héctor Guerrero7, Matti Palin1, Jarmo Kivekäs1, Petri Koskimaa1, and Matti Talvioja8
EGU 2022
Affiliations on next page
The contract is carried out under a programme of and funded by the European Space Agency

## Slide 2: Background
MiniPINS is an ESA study led by the Finnish Meteorological Institute (FMI) to develop and prototype miniaturized surface sensor packages (SSPs) for Mars and the Moon. Phase 0 of the study ending in Mission Definition Review was completed in 2020, and phase A ending in Preliminary Requirements Review in 2021.
The other partners of the study are: Instituto Nacional de Técnica Aerospatial (INTA), Centro de Astrobiología (CAB, CSIC-INTA), Added Value Solutions (AVS), Universitat Politècnica de Catalunya (UPC), Instituto de Microelectrónica de Sevilla (IMSE), and IMDEA Nanociencia. Also Talvioja Consulting Oy participates in the work.
Mars SSP MINS is a penetrator with approx. 25 kg mass, piggy-backed by another Mars mission spacecraft to the Martian orbit and deployed from there. The design of MINS has significant heritage from FMI’s MetNet mission design *
Moon SSP LINS is a 7 kg station deployed by a lunar rover. The reference carrier mission for LINS is ESA EL3 lander.
* Harri et al. (2017), The MetNet vehicle: a lander to deploy environmental stations for local and global investigations on Mars, Geosci. Instrum. Method. Data Syst., 6, 103-124

## Slide 3: Mission overview - LINS
Preliminary LINS deployment sites in Schrödinger crater
LINS packages will be a contribution by ESA to another Lunar mission. The baseline carrier mission for LINS is European Large Logistics Lander (EL3).
Up to 4 LINS packages will be placed on the Moon surface by a rover. LINS will have an interface for the rover robotic arm.
From 7 kg total mass, 1.5 kg is reserved for the payload
Once placed, LINS will perform environmental measurements for a minimum of 2 years

## Slide 4: LINS mechanical design, status at phase B1
Outer wall structure and some of the solar panels not shown in the drawing
The structure is divided in two parts, the external frame, that holds in position the solar panels and the external payloads, and the internal frame, that contains the RHU, the electronics and some sensors that do not require direct exposition or need to be protected from the thermal environment.

## Slide 5: LINS thermal design
One of the most challenging aspects of LINS design is thermal design, as LINS needs to survive 14-day long, cold lunar nights when temperature drops down to -170°C. LINS design consists of a double structure, an internal and an external one. The external one acts as an exoskeleton for the internal and is separated from it by 8 PEEK blocks.
The lower cover of the module can completely contact the lunar regolith, since it would not provide a significant thermal path as it is isolated from the internal one. In addition, the separation between the two structures provides some space to accommodate additional thermal insulation if necessary.
LINS cannot survive Lunar nights on solar cells and batteries alone, so an RHU (3W) is needed to provide extra heating. During the day, extra heat is evacuated through the cold wall with a heat switch.
LINS Temperature field [°C] during Lunar Night (worst cold case).
LINS Temperature field [°C] during Lunar “noon” (worst hot case).

## Slide 6: Suggested LINS Payload
Panoramic camera
Adaption of the MASCOT camera from DLR.
Soil thermoprobes
3D heat flux sensor, based on the structure of a wind sensor for Mars. Provided by UPC.
Tilt accelerometer
COTS component from Analog Devices. Qualified for ExoMars 2016 mission.
Magnetometer
MOURA, developed for MetNet Precursor by INTA
Seismometer
MEMS short period seismometer from Imperial College. InSight heritage.
Dosimeter
MOSFET dosimeter from Dyndall National Institute, heritage from NANOSAT 1B mission.

## Slide 7: Mission overview - MINS
MINS is a contribution by ESA to another Mars mission, or other mission of opportunity
4 penetrators are deployed hyperbolically from Mars approach orbit to various landing sites on Mars. The landers perform fully autonomous aerodynamic braking with inflatable braking units (IBUs) and land with 60-80 m/s velocity, penetrating the soil up to 0.5 m.
From 25 kg total mass of the lander, up to 4.5 kg is reserved for the payload
Once landed, MINS will perform surface and sub-surface environmental measurements, for a minimum of 1 Martian year (2 Earth years)
Name | Location | Elevation | Crustal magnetic field | Soil penetrability
Gale Crater | 5S, 140E | -4 km | Not active | Sand and duricrust (cemented regolith), not much dust
Western Tharsis, South of Olympus Mons | 10N, 135W | -1 – 0 km | Not active | Thick covering of dust (2-6 m)
Syrtis Major | 15N, 70E | 0 – 1 km | Slightly active | Coarse sand and duricrust, little dust
Western Eridania (Crater) | 45.5S, 169.5E | 0 – 1 km | Active | Sand and duricrust, not much dust, possibly subsurface ice
South Memnonia (Bernand Crater) | 23S, 154W | 0 km | Active | Mixture of dust and sand
Preliminary landing site candidates for MINS penetrators

## Slide 8: MINS EDL system – inflatable braking units
MINS hypersonic IBU deployed
MINS in landing configuration with transonic IBU deployed
Penetration
Hypersonic IBU deployment
Transonic IBU deployment
Braking by means of transonic IBU
Science mission
on-surface operations
Landing event
Entry
Separation of hypersonic IBU
MetNet landing concept
MINS in stowed position
European Space Agency is facilitating industrial development of an European inflatable deceleration system.

## Slide 9: MINS penetrator design at phase B1
The geometry of MINS includes a thin section to improve penetrability to the soil, a medium section with 150 mm diameter to accommodate a 2U CubeSat structure inside, and a top section with a wider diameter to stop the penetration and avoid the top part to be buried inside the soil. The deployable boom is accommodated in the top section, together with some surface sensors. The boom is based on telescopic deploying concept. The system electronics, like OBC, radio and batteries are located inside the 2U Cubesat structure.
The electronics for the subsystems of MINS penetrator are developed using two approaches:
Using COTS with flight heritage and delta-qualification – mainly CubeSat systems
  For example, radio and batteries
In-house development
  For example, on-board data handling
~80 cm

## Slide 10: MINS science and payload
MINS peforms scientific measurements above, at, and below the surface of Mars:
  Context images, visual spectrometry
  Meteorological measurements
  Solar irradiance and dust optical properties
  Chemical and thermophysical properties of the soil below the surface
  Total ionizing dose on the surface
  Seismological measurements
Air temp. sensor (CAB)
Solar irradiance sensor (INTA)
Seismometer (Imperial College)
Relative humidity sensor (FMI)
Pressure sensor (FMI)
Dust sensor (Carlos III University)
Chemistry package (CAB)
Wind sensor (UPC)
Visual spectrometer (VTT, Finland)

## Slide 11
MiniPINS Prototyping activities

## Slide 12: Preliminary development of test impact facility (INTA)
An existing air-vacuum cannon was combined with a penetration-targeting structure and a three-axis 60kg wireless accelerometer to test the penetrators with different terrains and impact velocities.
Preliminary penetration tests performed with scaled-down mass dummies (~2 - 4 kg) of MINS penetrator in different configurations. Photo on the right shows the accelerometer inside the projectile.

## Slide 13: Target S-number determination
Diameter (mm) | Mass (gr) | Speed (m/s) | Target Material | Depth (cm) | S Number
55 | 1937 | 66 | Loose sand | 92 | 44
55 | 1945 | 65 | Wet sand | 78 | 38
55 | 1945 | 66 | Wood chipboard 625 Kg/m3 | 7 | 3,4
37 | 1993 | 70.2 | Plywood 429Kg/m3 | 17 | 3,7
1-section projectiles were used to determine the S-numbers of different targets.
S-number for “hard case” (3-4) was achieved.
For “soft case” the desired S-number was ~10, the target materials used in these first tests proved to be too soft. They could still be used to verify the performance of the ”stopper” of 3-section design.

## Slide 14: Deceleration tests with 3-section design
Mass (gr) | Speed (m/s) | Target Material | Penetration Depth (cm)
3985 | 60 | Expanded polysterene *) | 41,9
3989 | 56 | Dry sand | 55
4660 | 55 | Expanded polysterene | 43,5
4660 | 61 | Expanded polysterene | 40,7
4656 | 60,5 | Expanded polysterene | 43,5
*) S-number estimated between 30 and 45
Tests were performed with the 3-section 4.6 kg aluminium projectiles on “soft” soils (expanded polystyrene and dry sand). There were two main conclusions:
The repeatability of the launch process is high.
The stopper section did its job, given that in all cases the penetrator was stopped at the end of this section.
Deceleration profile measurement 10 ms for 600g => 60 m/s impact speed

## Slide 15: Flexible solar cells (IMDEA)
COTS Perovskite Solar Cells (PVC) from SAULE technologies, with efficiency as high as 25%, were tested under Martian conditions of temperature (down to -145°C) and solar irradiance. Preliminary results:
A maximum in efficiency is around -75°C
The efficiency is not decreased after 5 thermal cycles
Unrolling tests of solar cells deployment system based on Shape Memory Alloy technology

## Slide 16: Deployment test at IMDEA

## Slide 17: Thermoprobe tests (UPC)
Testing objectives: Needle-type and spherical 3D thermoprobe sensors, developed at UPC, were tested for their ability to characterize the thermophysical properties of regolith:
In buried cylinder (simulation of regolith entering MINS penetrator front chamber).
Without cylinder (simulation of LINS lunar probe).
The sensors use Fourier methods.

## Slide 18: Spherical thermoprobe
Thermoprobe tested with 9 simulants of regolith made of glass microbeads.
Thermal impedance of the sphere is measured and fitted with model – Fourier methods
Measured thermal conductivity and diffusivity:
Very good match with reference values for all regolith Samples

## Slide 19: Needle type - inside cylinder
Needle-type probe. Larger frequencies (1mHz – 1Hz).
Probe present very different thermal impedances depending on the regolith simulant.

## Slide 20: Low-temperature tests of ASICs in CMOS technology (IMSE)
Mixed-signal ASICs in CMOS technology developed by IMSE originally for INTA’s Solar Irradiance Sensor were tested in low temperatures required by LINS mission. The ASIC proved to be fully operational down to -185°C (lower limit of the test chamber) without any major degradation observed.