## Slide 1: Langmuir Probe observations during eclipses of Cassini with Saturn and the Main Rings: ring optical depths and photoelectrons
EGU 2022 – Vienna (finally!)
Georgios Xystouris, Christopher Stephen Arridge, Michiko Morooka, and Jan-Erik Wahlund
g.xystouris@lancaster.ac.uk

## Slide 2: LP and I-V curves
1
Sweeps: every ~10min (or ~30s), -32V to +32V, lasting 0.5s
Ions: linear approximation on ; Electrons:
Gradients on positive bias: multiple e- populations; ← Best parameters fitting on Maxwellians
Notes: Gradiend of the current with respect to the bias voltage
Ufloat is the potential at the distance of the LP. Ufloat is not Usc

## Slide 3: Example of eclipses in an orbit
Eclipses:
118 by Saturn
163 by the main rings
2

## Slide 4: IV curves during an eclipse
3
S/C becomes VERY negatively charged <- lack of sunlight
LP behavior changes:
drops to almost zero
almost disappears
→ We can identify when the LP is in the shadow
Notes: Sweeps in shadow are different than sweeps in sunlight.
CURRENT GOES TO ZERO IN SHADOW.
THERE IS NO U_FLOAT VISIBLE
LP SHOWS when Cassini is in Shadow -> useful to attack the photoelectrons issue

## Slide 5: Rings opacity
4
Rings:
A, B: optically thick (B: thickest)
C, D: optically thin (D: thinnest)
Able to identify structures (Encke Gap, Maxwell Gap)
In agreement with previous studies (e.g. Wahlund+ 2018, Hadid+ 2018, Colwell+ 2010)
Colombo
Gap
Maxwell
Gap
Encke
Gap
Xystouris et al. (in prep.)
Notes: Combining the IV curve changes with: LP surface photoelectron yield

## Slide 6
Thank you
“Langmuir Probe observations during eclipses of Cassini with Saturn
and the Main Rings: rings optical depths and photoelectrons”
G. Xystouris, C. S. Arridge, M. Morooka, and J-E. Wahlund
g.xystouris@lancaster.ac.uk
Notes: Eclipses: 118 by Saturn, 163 by the main rings

## Slide 7: Extras: Rings and shadowing
B-ring
D-ring
C-ring
A-ring
6
Notes: 2 groups: A-B: cast shadow -> EUV optically thick
C-D: optically thin
C-ring: more optically thick than D-ring

## Slide 8: Extras: Results
LP I-V curves change dramatically in eclipses
  A I-V curve can tell when we’re in the shadow
  Maybe we need a better way to analyse data during eclipses?
Rings appear variable EUV (sunlight) opaqueness:
  A- and B-ring optically thick; B-ring is the most optically thick
  C- and D-ring optically thin; C-ring a bit more optically thick than D-ring?
  Some rings features are visible (Maxwell Gap, Encke Gap)
  In agreement with previous studies, e.g. Wahlund+(2018), Hadid+(2018), Colwell+(2010)
Photoelectrons complicate data analysis for many missions → knowledge from this work to be used in future missions data analysis and planning
Demonstration of using a magnetospheric instrument to study planetary features
7

## Slide 9: Extra: Future work
Investigate additional parameters; e.g. secondary electrons, high energy electrons, PPOs etc.
Investigate any asymmetries
9

## Slide 10: Extras: Backup example of eclipses in an orbit
Eclipses:
118 by Saturn
163 by the main rings
8