## Slide 1
Overview of the seafloor geodetic observation conducted by the Japan Coast Guard using the GNSS-Acoustic ranging combination technique
Yuto Nakamura1, Tadashi Ishikawa1, Shun-ichi Watanabe1, Yusuke Yokota2
1: Hydrographic and Oceanographic Department, Japan Coast Guard
2: Institute of Industrial Science, University of Tokyo
EGU2022 (May 23-27, 2022)
G3.4

## Slide 2
(2)
“steady” backslip
“early” postseismic
“long-term” postseismic
Graphical abstract
Eurasian plate
(Amur plate)
Pacific plate
Philippine Sea plate
North American plate
Japan Trench
Nankai Trough
Motivation of seafloor geodetic observation
Overview of GNSS-A and JCG’s sites (SGO-A)
Observation results, geophysics revealed from recent observations
Technological advancements and future works

## Slide 3: Table of contents
Motivation of seismic/geodetic observations at Japan
Overview of GNSS-A, JCG’s sites (SGO-A) and data analysis
Observation results, geophysics revealed from recent observations
Technological advancements and future works

## Slide 4: 1. Motivation of seafloor geodetic observation
The Japanese Islands are at a tectonically active zone where four tectonic plates meet.
Megathrust earthquakes occur along the subduction zones (e.g. 2011 Tohoku-oki Earthquake, )
Eurasian plate
(Amur plate)
Pacific plate
Philippine Sea plate
North American plate
Japan Trench
Nankai Trough
Megathrust earthquakes
Tectonic plate boundaries around Japan
Japan: the tectonically active islands

## Slide 5: 1. Motivation of seafloor geodetic observation
Earthquake history of Nankai Trough, from Ishibashi (2004)
Megathrust earthquakes repeatedly occur along…
Japan Trench (e.g. 2011 Tohoku-oki Earthquake, )
Nankai Trough (Ishibashi 2004)
Numerous groups conduct seismic/geodetic observations to elucidate the mechanism of megathrust earthquakes.
Japan Coast Guard conducts seafloor geodetic observation using GNSS-A.
Seafloor geodetic observation (us)
and more…

## Slide 6: 1. Motivation of seafloor geodetic observation
Monitoring seafloor crustal deformation: why is it important?
Oceanic plate
Overriding plate
Terrestrial GNSS observation
⇒GEONET (GSI)
Fault slip
Crustal deformation near the trough axis (undersea)
⇒seafloor geodetic observation (JCG)
The source regions of megathrust earthquakes are mainly undersea.
Crustal deformation of the seafloor is important for elucidating megathrusts.
Coseismic slip of the 2011 Tohoku-oki earthquake: mainly undersea
Geodetic inversion
(Iinuma et al. 2012)
Tsunami waveform inversion
(Satake et al. 2013)

## Slide 7: 2. Overview of GNSS-A, JCG’s sites (SGO-A) and data analysis
Radio wave signals
land
GNSS satellites
GNSS site
seafloor
sea surface
×
Land: GNSS observation (GEONET)
Seafloor: cannot be observed!
Underwater: use acoustic ranging to obtain the position of a seafloor benchmark→GNSS-Acoustic ranging (GNSS-A)
Monitoring seafloor crustal deformation: GNSS-Acoustic (GNSS-A)

## Slide 8: 2. Overview of GNSS-A, JCG’s sites (SGO-A) and data analysis
Ship’s positions
are known by GNSS
transponder
Sailing observation (ship-ship-transponder trilateration)
Sail
Solve positions of each of transponder
developed by JCG & Univ. Tokyo
Round-trip travel time
solve with collection
of various slant ranges
Unknown sound
speed perturbation
JCG performs seafloor geodetic observation using the GNSS-Acoustic ranging combination technique (GNSS-A).
Onboard transducer
(Photo by JAMSTEC)
Transponder (seafloor station)
Positioning of seafloor stations by acoustic ranging
Acoustic ranging

## Slide 9: 2. Overview of GNSS-A, JCG’s sites (SGO-A) and data analysis
Terrestrial GNSS vs. Seafloor GNSS-A
10 cm
GEONET site “Omaezaki”
GNSS-A site “TOK1”
TOK1
Omaezaki
 | GNSS | GNSS-A
Number of sites in Japan | Approximately 1,300 GEONET sites (operated by GSI) | Approximately 60 sites (operated by JCG and universities)
Observation frequency | continuous | 3-4 times per year
Precision (horizontal component) | less than 1 cm (daily coordinates) | 2-3 cm (1σ)
Major error sources | Atmospheric (Ionospheric/tropospheric delay | Atmospheric delay + sound speed perturbation (mainly due to water temperature)
Example: GEONET vs. GNSS-A in the Tokai region |  | 
10 cm
~60 km
Comparison between the terrestrial GNSS network GEONET operated by the Geospatial Information Authority of Japan (GSI) and GNSS-A observation by JCG and universities is shown on the table below.

## Slide 10: 2. Overview of GNSS-A, JCG’s sites (SGO-A) and data analysis
Nankai Trough
Japan Trench
SGO-A sites
● before 2004
● set in 2011-12
● set in 2019-20
JCG currently operates 27 GNSS-A observation sites along the Japan Trench and the Nankai Trough, named the Seafloor Geodetic Observation Array (SGO-A).
Map on the right shows the distribution of the SGO-A sites.
SGO-A was reinforced after the 2011 Tohoku-oki Earthquake (orange points).
Four sites were installed in FY2019 near the trough axis of the Nankai Trough (red points).
Map of the SGO-A sites
Tokyo
Kyoto
Hiroshima
Sendai

## Slide 11: 2. Overview of GNSS-A, JCG’s sites (SGO-A) and data analysis
JCG currently uses GARPOS (GNSS-Acoustic Ranging combined Positioning Solver; Watanabe et al. 2020) in the analysis routine.
GARPOS implements empirical Bayesian inversion and simultaneously estimates transponder positions and underwater sound speed structure.
The source code of GARPOS is open to everybody working on GNSS-A seafloor geodesy! Check our Zenodo repository:
GARPOS v1.0.1 (latest version)
https://doi.org/10.5281/zenodo.6414642
Observation equation
Antenna-transducer offset (relative position)
Sound speed perturbation model
Transponders’ positions
Estimated parameters
Observed travel time
GNSS antenna position
Attitude of the sea surface platform
Observables
Onboard transducer position
Correction coefficient (sound speed variation)
Two-way travel time
transmission
reception
Sound speed
Depth
Reference (calculated) travel time
Reference sound speed profile
Observation equation implemented in GARPOS
Attitude

## Slide 12: 2. Overview of GNSS-A, JCG’s sites (SGO-A) and data analysis
Sound speed
Depth
Two-way travel time
transmission
reception
Attitude
JCG’s analysis routine using GARPOS
Raw observation data files converted to GARPOS data format.
Single epoch analysis is performed using GARPOS to obtain the transponder array geometry of the latest observation epoch.
The mean transponder array geometry is computed from the single epoch analysis results of all epochs.
Assuming that the transponder array geometry is rigid, all observation epochs are reanalyzed by constraining the data with the mean array geometry computed in Step 3.
Finally, the time series of the site is created by computing the array centroid of each epoch, using the results from Step 4.
Step 5
Step 1
Step 2
Step 3
Step 4
Schematic diagram of JCG’s analysis routine
Raw data
GARPOS data
Single epoch analysis
Calculate mean array geometry
Time series
Analysis with array geometry constraint
epoch 1
epoch 2
epoch 3
epoch n
…
epoch 1
epoch 2
epoch 3
epoch n
…

## Slide 13: 3. Observation results, geophysics revealed from recent observations
Horizontal velocity of last 4 years
(w.r.t. Eurasian plate)
Dark arrows: velocity of the SGO-A sites
Light arrows: velocity of GSI’s GEONET

## Slide 14: 3. Observation results, geophysics revealed from recent observations
Latest observation results along the Japan Trench
(KAMN-CHOS)
Japan Trench
CHOS
FUKU
MYGW
MYGI
KAMS
KAMN
Tokyo
Sendai

## Slide 15: 3. Observation results, geophysics revealed from recent observations
Japan Trench
BOSN
SAGA
Latest observation results along the Japan Trench
(BOSN, SAGA)
Tokyo
Sendai

## Slide 16: 3. Observation results, geophysics revealed from recent observations
Latest observation results along the Nankai Trough
(TOK1-KUM2)
ZENW
TOK1
TOK2
TOK3
KUM1
KUM2
Hiroshima
Kobe
Fukuoka

## Slide 17: 3. Observation results, geophysics revealed from recent observations
Latest observation results along the Nankai Trough
(KUM3-MRT3)
MRT3
SIOW
SIO2
MRT1
KUM4
KUM3
MRT2
Hiroshima
Kobe
Fukuoka

## Slide 18: 3. Observation results, geophysics revealed from recent observations
Latest observation results along the Nankai Trough
(KUM3-MRT3)
TOS1
HYG1
HYG2
ASZ1
TOS2
ASZ2
Hiroshima
Kobe
Fukuoka

## Slide 19: 3. Observation results, geophysics revealed from recent observations
Recent study on geophysics of the subduction zones around Japan using SGO-A
Decadal postseismic movement after the 2011 Tohoku-oki Earthquake (Watanabe et al. 2021)
Watanabe et al. 2021

## Slide 20: 3. Observation results, geophysics revealed from recent observations
Afterslip in areas adjacent to the coseismic slip (i.e. KAMN, FUKU)
  Diminished in 1-3 years (-2014)
Persistent subsidence at FUKU
  Possibly due to viscoelastic relaxation after coseismic displacement at offshore of FUKU?
Movement of the coseismic slip area after 2017: can be explained as a sum of viscoelastic relaxation and backslip
Watanabe et al. (2021)

## Slide 21: 3. Observation results, geophysics revealed from recent observations
Watanabe et al. 2021
Before 2014: afterslip is dominant at the north and south ends of the coseismic slip region (i.e. KAMN and FUKU).
After 2014: velocity is stable, but is faster than the velocity before 2011.
  Viscoelastic relaxation is still present at the coseismic slip region.
  Subsidence of FUKU can be explained by viscoelastic relaxation in the slip region offshore.

## Slide 22: 4. Technological advancements and future works
Observation frequency of the SGO-A sites: improving, yet far from continuous observation
Pole system (before 2009)
Hull-mounted system (2009-)
Multiple acoustic ranging (2016-)
Future ???
Observation frequency: currently 3-4 times per year per site
To further improve frequency:
need of a new sea surface platform?
Buoy?
ASV (e.g. Wave Glider)?
UAV (Unmanned aerial vehicle)?
Ishikawa et al. (2020)

## Slide 23: 4. Technological advancements and future works
Event detection capability of SGO-A
Numerical and statistical experiments were performed to evaluate the event detection capability
It is necessary to improve observation frequency and spatial coverage of SGO-A to detect smaller events (especially far offshore).
(Yokota et al. 2021)

## Slide 24: 4. Technological advancements and future works
Analysis strategy: from SGOBS to GARPOS
SGOBS (Fujita et al. 2006)
Alternative estimation of transponder positions and sound speed structure using linearized inversion
(Watanabe et al. 2020)
Empirical Bayesian inversion
Simultaneous estimation of transponder positions and sound speed structure
GARPOS-MCMC
Full Bayesian inversion using Markov Chain Monte Carlo (MCMC)
For details, see Watanabe et al. in this session!
GARPOS (2021-)
SGOBS (-2021)
Future ???
Fujita et al. (2006)
Watanabe et al. (2020)

## Slide 25: 4. Technological advancements and future works
# Site_name = CHOS
# Campaign = 1204.meiyo_m4
# Date(UTC) = 2012-04-19
# Ref.Frame = ITRF2008
# Latitude0 = 35.50277778
# Longitude0 = 141.66944444
# Height0 = 24.00
# Stations = M01 M02 M03 M04 M11 M12 M13 M14
# M01_dPos = -36.5030 698.5700 -1509.5790
# M02_dPos = 750.0060 -9.6570 -1548.1650
# M03_dPos = 9.6750 -781.3210 -1556.1690
# M04_dPos = -768.0610 -32.3080 -1519.3960
# M11_dPos = 75.2230 802.1480 -1497.9700
# M12_dPos = 854.5610 113.3070 -1539.5900
# M13_dPos = 116.8820 -666.7590 -1545.8500
# M14_dPos = -666.0480 68.5790 -1517.2000
# ATDoffset = 1.9452 -0.7653 21.3339
,SET,LN,MT,TT,flag,ST,ant_e0,ant_n0,ant_u0,head0,pitch0,roll0,RT,ant_e1,ant_n1,ant_u1,head1,pitch1,roll1
0,S01,L01,M01,2.271449,False,12998.546235,-8.76681,1474.63035,13.59756,186.4,-0.76,0.71,13001.87919,-8.50997,1465.94866,13.39895,186.19,1.95,-1.04
1,S01,L01,M02,3.027084,False,13008.54628,-8.62977,1450.56564,12.7152,188.86,-1.35,0.93,13012.63487,-9.15161,1440.50533,13.80715,189.16,-0.25,0.48
2,S01,L01,M03,3.593219,False,13028.546345,-11.55922,1401.97245,13.50447,191.2,2.0,-0.53,13033.20107,-12.29072,1391.65533,12.53032,191.93,-0.4,-0.86
3,S01,L01,M04,2.954364,False,13038.546375,-13.60719,1378.3708,13.4282,189.78,-0.5,-0.76,13042.562245,-14.65926,1368.03363,12.89624,189.59,1.44,0.93
4,S01,L01,M11,2.138648,False,13048.546455,-15.38928,1354.52261,13.03522,187.99,-2.41,1.43,13051.74661,-14.90793,1345.65016,13.46705,187.15,1.01,-1.35
5,S01,L01,M12,2.875131,False,13058.5464,-15.54531,1329.28916,12.57873,186.09,-1.22,0.2,13062.48304,-14.64234,1319.03164,12.79195,186.08,-1.47,-0.97
6,S01,L01,M13,3.360925,False,13068.5465,-15.8706,1303.541,12.93603,184.7,1.51,1.66,13072.96893,-14.26268,1293.26341,12.65954,185.87,-2.32,0.77
7,S01,L01,M14,2.740823,False,13078.546545,-13.77302,1277.97544,13.20333,183.7,1.21,-2.37,13082.348875,-14.39044,1269.76292,12.37441,183.87,1.02,1.79
8,S01,L01,M01,2.152039,False,13088.54653,-13.83453,1254.04902,13.82523,181.4,-0.75,4.7,13091.760075,-12.29386,1245.41211,13.31,180.52,2.56,-0.54
...
One can solve GNSS-A only with this file
(supporting information such as sound speed profile may be needed, but not essential)
Not only for GARPOS: a general format for GNSS-A
Campaign information
Site information & approx. parameters
Data for each acoustic signal
Time
Travel time
Ship position (transmit/return)
Ship attitude (transmit/return)
Construction of GNSS-A data format: a GNSS-A “RINEX” format
GNSS-A data + configuration file (.ini)
Positions of the seafloor transponders

## Slide 26: 4. Technological advancements and future works
Evaluating error sources of GNSS-A: for details, see Yokota et al. in this session!
Nakamura et al. (2021)
D
R
Survey line
L
Transponder array
Effects of observation scheme (transponder array size, survey line radius)
R
L
Geometries of the transponder array and survey line affect the positioning accuracy of the transponders.
Current configuration of JCG’s observation was found to be appropriate (Nakamura et al. 2021).
reference profile
actual structure
residual structure
Γ in GARPOS
internal wave in a pycnocline
warm
cold
seafloor stations
vessel
projection
Evaluating effects of oceanographic disturbances
Interpretation of sound speed structure parameters obtained by

## Slide 27: Summary
JCG conducts GNSS-A seafloor geodetic observation.
Seafloor Geodetic Observation Array (SGO-A)
Analysis: GARPOS
Nankai Trough
Japan Trench
SGO-A sites
● before 2004
● set in 2011-12
● set in 2019-20
Recent work in geophysics: decadal postseismic movement after the Tohoku Earthquake
Technological advancements
Observation frequency and coverage
Analysis strategy
Error analysis
For details, check Watanabe-san and Yokota-san’s presentations (both in this session)!