## Slide 1
Violet Kanyiginya, PhD student- RMCA, VUB, MUST
Dr. Olivier Dewitte, promoter, RMCA
Prof. Matthieu Kervyn, promoter, VUB
Dr. Ronald Twongyirwe, promoter, MUST
Understanding natural hazards in a changing landscape: A citizen science approach in Kigezi highlands, southwestern Uganda

## Slide 2: Region characteristics
Tropical mountainous region
Steep topography
High rainfall 990-1540 mm
Alternating dry & wet seasons
Deep weathering
High population density
High human-induced land use changes

## Slide 3
Among the most exposed regions to natural hazards in the country
Limited studies in the region
Detailed inventories is key for understanding hazard interactions

## Slide 4: Objectives
Building a comprehensive inventory of natural hazards, evaluate their spatial-temporal distribution and interactions
Investigate multi-decadal landscape dynamics in relation to landslides and flood hazards
Determine flash flood frequency and magnitude in selected watersheds

## Slide 5
15 Geo-observers
8 River watchers
104 senior citizens
Methodology
1954 aerial photographs,
catchment characterization
Discharge measurement, rain gauges
Reports, literature & archives, satellite images, field surveys
Comprehensive inventory
Monitoring daily stream water levels
Tracing multi-decadal landscape change
Participatory citizen scientists

## Slide 6: The data collection & validation processes
Data collected: Location, date and time of occurrence, description of hazard, impacts, pictures

## Slide 7
Tracing multi-decadal landscape change
Interviews & FGDs with the senior (70-98 years) in 8 study watersheds
Historical timelines constructed and used during the interviews
Participatory mapping was applied to highlight the LULC changes

## Slide 8: Natural hazards recorded and their distribution
Chart: 
| Landslides | Floods | Hailstorm | Windstorm | Pests & diseases | Lightning
 | 142 | 69 | 15 | 20 | 17 | 3
266 hazard occurrences in in 2 years

## Slide 9: Reliability and value added by geo-observers data
Chart: Source of inventory
| Geo-observers | Field survey | Archives & literature
Number of records in 2years | 266 | 177 | 10
Natural hazards recorded in 2years from different sources
Proximity to the affected area & real-time reporting
Inclusive reporting (small and large events)
The data is georeferenced and detailed
Reliable in hazard vulnerability assessment

## Slide 10: Natural hazard distribution and interactions
Rainfall is the main trigger; >90% occurrences in the peak rainy season
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Number of events | 19 | 18 | 15 | 8 | 20 | 6 | 0 | 5 | 10 | 37 | 28 | 7
Rainfall/mm | 9 | 13 | 14 | 18 | 9 | 6 | 2 | 5 | 10 | 19 | 15 | 10
Number of events recorded in 2020 versus rainfall
35 hazard interactions characterized
40% primary directly triggered other hazards
60% hazards/processes increased the probability of secondary hazards occurring
Storm
Floods
Triggers
(Flash) floods
Landslides
Triggers
Triggers
Road undercuts, vegetation removal
Landslides
(Flash) floods
Increase probability
E.g.1
E.g.2
Data collection affected by COVID-19

## Slide 11: The landscape change
October 1954
July 2019
Deforestation (e.g. natural tree species to eucalyptus)
Increased cultivation of hillslopes
Drainage of wetlands
Road construction
Management practices abandoned (terraces & fallowing)
Population increase

## Slide 12: Reconstructing multi-decadal landscape change
October 1954
August 2021
Wetland conversion

## Slide 13: Conclusion
Population growth has played a significant role in accelerating land use/cover changes & possibly influenced the patterns of natural hazards
Value added on data collected by citizen-led approaches in understanding natural hazards interactions
Raised community’s awareness on prevailing natural hazards in the region
Could be considered in developing early warning systems for Disaster Risk Reduction
Violet.Kanyiginya@vub.be