## Slide 1: Laboratory simulation of gas hydrate formation at ice surfaces in Earth atmosphere Brian Durham, Christian Pfrang, Ali Hassanpouryouzband Session AS3.16 - Atmospheric surface science and ice nucleating particles EGU2022

## Slide 2: Gas capture at a growing ice surface
The property of ice to `cage’ otherwise mobile gas molecules has significance in the evolving hydrogen economy.
In the carbon economy, CO2 is a hydrate-former, and its property as a radiation absorber means it can be quantified continuously and non-destructively in the gas phase.
The relevance of CO2 is that rainwater and snow are 40 x supersaturated relative to the Henry equilibrium, and the frost that forms on your windscreen can release between16 and 64 times the Henry equilibrium content (EGU 2020). This also means that the pH of fresh rainwater typically rises when shaken with successive changes of ambient air.
Pure CO2 hydrate will hold 1mol CO2 per 6mol H2O. This proportion declines with lower partial pressure of the molecule according to a curve generated by University of Lille. This appears to confirm that cage occupancy is a scalable non-stoichiometric relationship, (Chazallon and Pirim (2018) `Selectivity and CO2 capture efficiency in CO2 -N2 clathrate hydrates investigated by in-situ Raman spectroscopy', Figs 4A and 4B).
Windscreen frost
analysed by degassing
Chazallon and
Pirim (2018)
Figs 4A and 4B

## Slide 3: Gas capture at a growing ice surface
Our principle is to measure depletion of CO2 from an airstream by formation of `frost’, and to match that value to the release of the molecule in melting the condensate
The current apparatus uses:
  1 m3 Tedlar gas sample bag, ambient air filtered 1µ;
  Pre-cooler and inter-cooler heat-exchangers (bath at 0.1°C), delivering a known mol fraction of CO2 /air, of which CO2 and water vapour content are monitored by NDIR, flow monitored by MFC),
  Frost-chamber (bath at 0.1°C for instrument calibration, cooled to -5°C for frost-making), outflow CO2 monitored by NDIR, flow monitored by MFC).
Procedure:
  Calibrate instruments for 1 hour with both chillers at 0.1°C;
  Reduce downstream chiller to -5°C , grow frost for 3 hours;
  Melt condensate by lifting the frost chamber out of its chiller bath, allowing the same air-stream to sublimate/melt the frost and any caged gas;
  Calibrate for final hour;
Frost-making May 2022
Schematic of frost-making flow path,
June 2022

## Slide 4: Release of CO2 captured at a growing ice surface
Test run 28 June 2022 for illustration;
Gas mixture 0.5 L per minute flow for 3 hours, frost chamber at -5°C over :
Following lifting of frost chamber from waterbath at 22:00, the downstream CO2 rises with release from condensate. Downstream H2O proved unstable in all runs, trace omitted.
Thanks to Daniel Wilson and Ian Smillie of Licor UK for loan of demonstrator analysers LI840A and LI850.
Campbell Science LoggerNet 4.1 on-screen monitoring
Green = CO2 D/S;
Red = CO2 U/S;
Black = temperature (°C);
Blue = water vapour U/S

## Slide 5: Gas capture at a growing ice surface Interim conclusion and next steps
CO2 release at beginning of melt cycle provisionally supports:
  Lille results;
  Degassing of windscreen frost;
  CO2 supersaturation in atmospheric water.
Next steps:
  Repeat frost-making from lower and higher µmol fractions of CO2 to extend Lille curve;
  Frost-making at a range of freezing temperatures (Hassanpouryouzband et al 2019 `Geological CO2 capture and storage ..,’);
  Direct degassing of the melt phase, by bubbling 1 mol of CO2 -free dry air through frost chamber for 20 minutes to achieve quantitative analysis of the melt;
  As above, with/without SDS (sodium dodecyl sulphate) as hydrate `promoter.’
Hardware upgrades include CO2/water vapour analysers, and gas chromatograph at the outlet to quantify N2 and O2 hydrates at atmospheric pressures.