## Slide 1: CO2 INJECTION FOR GEOTHERMAL POWER GENERATION AND STORAGE IN HYDROTHERMAL RESERVOIRS IN AL WAJH BASIN, SAUDI ARABIA
Bora Yalcin, Justin Ezekiel, P. Martin Mai

## Slide 2
(Mohriak, 2014)
CO2-based geothermal energy mining
Red Sea region has high heat flux (60-100 mW/m2) and favorable hydrothermal system.
Al Wajh is a rift basin with thick syn-rift turbidites capped by anhydrite seal.
AWSO-1 well ,seismic section and satellite gravity map available for geo-model input
Location of Al Wajh Basin
Model Area
AREA OF INTEREST & MOTIVATION
Motivation
A
A’
A
A’

## Slide 3
Umluj
Burqan
Yanbu
AlWajh
Basement
Structural model/grid
MPS facies model
GEOMODEL
AWSO-1
Syn-rift submarine paleo analog
Yalcin et al., in preparation
Leppard, 2006
30 km
115 km
We used VBM technique for structural model.
We used the channel dimensions from present bathymetry data as main input for multipoint simulation
We derived sand/silt/shale probability cubes based on published statistics. Then, in addition to the well data, we conditioned the distribution density of the channels to those probability cubes

## Slide 4
Porosity distribution
Permeability distribution
Temperature model
PETROPHYSICAL PROPERTY MODEL
Sector Model
Yalcin et al., in preparation
AWSO-1
12 km
6 km
We assigned representative porosity and permeability distributions for turbidite facies associated rock types.
For the channel sand: We applied pore-size (and hence the permeability) re-distribution to honor grain size changes based on proximity to the sediment source.
We selected a representative –smaller- area as sector model for simulation purposes

## Slide 5
CO2 Relative Permeability
FLUID PROPERTY MODEL
CO2 Viscosity
Yalcin et al., in preparation
(after NIST)
(after Spycher et.al., 2003)
(Van Genuchten parameter: m = 0.77)
CO2 Solubility
We explicitly modeled both H2O and CO2 viscosity, solubility for a desired range of temperature and pressure
We then also assign relative permeability curves with Van Genuchten parameter of 0.77

## Slide 6
CO2 Injection - Production scheme
SIMULATION SCHEME
Yalcin et al., in preparation
Well pattern with open boundary condition
1600 m
INJ
INJ
INJ
INJ
PROD
(Harry Campell)
Open boundary (heat and pressure) condition for the simulation model
We focused on the upper 400 meters of syn-rift sedimentary rocks for the simulation
We designed the well pattern such that we can achieve 95% of CO2 saturation on the production well.
7 years of injection and 33 years of production in total 40 years of simulation.
Specs of simulation

## Slide 7
FLUID FLOW SIMULATION
CO2 Plume in time & space
Yalcin et al., in preparation
Seal
Top 400 m
Total energy in pre-salt sediments in Al-Wajh basin
13.6 % of the energy in place is recovered
**Yearly electricity production of USA was 15 ExaJ as of 2021
Ref: (https://www.eia.gov/)

## Slide 8: PRELIMINARY RESULTS AND OUTLOOK
With this work we established the GRV (gross rock volume), rock type distribution and total energy potential for syn-rift sedimentary rocks in Al Wajh
For a 40 years of Injection production scenario from upper 400 meters of syn-rift sedimentary rocks:
  With the current well pattern design we recover 13.6% of the thermal energy in place with CO2 plume
  Energy production starts on the order of Peta Joules (E+15) per year
Currently we work on the uncertainty quantification of the reservoir simulation
With this study we will assess the heat mining potential of the Al Wajh basin via CCUS method