## Slide 1: Revealing unexpected sources and quantities of groundwater discharge into major river systems during drought conditions
Julia Zill, Christian Siebert, Tino Rödiger, Markus Weitere, Ulf Mallast
M.Sc. Julia Zill (PhD student)
Helmholtz Centre for Environmental Research
Dep. Catchment Hydrology & Dep. River Ecology

## Slide 2: Revealing unexpected sources and quantities of groundwater discharge into major river systems during drought conditions
Julia Zill, Christian Siebert, Tino Rödiger, Markus Weitere, Ulf Mallast
M.Sc. Julia Zill (PhD student)
Helmholtz Centre for Environmental Research
Dep. Catchment Hydrology & Dep. River Ecology

## Slide 3: Challenges of diffuse nutrient loads
Groundwater discharge is the major diffuse source of nutrients (N, P) 1, 2, 3
Oversaturation of nutrients leads to eutrophication 4, 5
Eutrophication jeopardizes ecosystem stability and biodiversity 6, 7, 8
Efficient eutrophication management needs knowledge of river-aquifer systems
Rockström et al., 2009

## Slide 4: Elbe River as research area
Cretaceous marl- and sandstone as bedrock
Unconsolidated glacio-fluvial quarternary sediments
Highly eutrophic river, particular under drought conditions 10

## Slide 5: Multi-methodological approach
Groundwater discharge
Localisation & Steadiness
Quantification & Probability
Hydraulic gradients
Flux balance
Geochemical modeling (PhreeqC)
Darcy approach

## Slide 6: A: hydraulic gradient
effluent conditions  river gain groundwater
influent conditions  river lose groudwater
highly dynamic conditions  seasonal fluctuations

## Slide 7: B: flux balance
 Total gw volume: 33 m³/s = 28 %
Volumetric flow for each segment was calculated by subtraction
Segment A,B,I show major gw discharge

## Slide 8: C: Inverse geochemical modeling
 Total gw volume: 39 m³/s = 30 %
chemical composition of the river segments end as an integral of all inflows
Segments A, B, C, I show major gw discharge

## Slide 9: D: Darcy approach
 Total gw volume: 8 m³/s = 7%
hydraulic gradient
river bank area
hydraulic conductivity

## Slide 10: Combined results
A-C: major gw flow
D-H: moderate to low flow
I: drainage ditches overlay the gw signal
 Total gw volume: 7 – 30 %

## Slide 11: Combined results
Location and quantification of groundwater discharge
Impact may increase under drought conditions
Providing essential information for a sustainable river management
Multi-methodological approach is necessary for understanding large scale systems
Blueprint for other river basins

## Slide 12
1: Sharpley, A.N., Chapra, S.C., Wedepohl, R., Sims, J.T., Daniel, T.C., Reddy, K.R.: Managing Agricultural Phosphorus for Protection of Surface Waters: Issues and Options, J Environ Qual, 23, 437-451, https://doi.org/10.2134/jeq1994.00472425002300030006x, 1994.
2: Donohue, I., Styles, D., Coxon, C., Irvine, K.: Importance of spatial and temporal patterns for assessment of risk of diffuse nutrient emissions to surface waters, J Hydrol, 304, 183-192, https://doi.org/10.1016/j.jhydrol.2004.10.003, 2005.
3: UBA: Federal Environmental Agency, Nitrogen and phosphorus loads from point and diffuse sources to surface waters in Germany, https://www.umweltbundesamt.de/sites/default/files/medien/384/bilder/dateien/2_abb_n-p-eintraege_2020-09- 17.pdf, last access: 02. November .2021, 2020.
4: Bachmann, R.: The Role of Agricultural Sediments and Chemicals in Eutrophication. J Water Pollut Con F, 52, 2425-2600,1980.
5: Dodds, W.K.: Eutrophication and trophic state in rivers and streams, Limnol Oceanogr, 51, 671-680, https://doi.org/10.4319/lo.2006.51.1_part_2.0671, 2006.
6: Mallin, M.A., Johnson, V.L., Ensign, S.H., MacPherson, T.A.: Factors contributing to hypoxia in rivers, lakes, and streams, Limnol Oceanogr, 51, 690-701, https://doi.org/10.4319/lo.2006.51.1_part_2.0690, 2006.
7: Dodds, W.K., Bouska, W.W., Eitzmann, J.L., Pilger, T.J., Pitts, K.L., Riley, A.J., Schloesser, J.T., Thornbrugh, D.J.: Eutrophication of U.S. Freshwaters: Analysis of Potential Economic Damages, Kansas State University, Manhattan, Kansas, Environ. Sci. Technol., 43, 12–19, https://doi.org/10.1021/es801217q, 2009.
8: Donald, D.B., Bogard, M.J., Finlay, K., Bunting, L., Leavitt, P.R.: Phytoplankton- Specific Response to Enrichment of Phosphorus-Rich Surface Waters with Ammonium, Nitrate, and Urea, PLOS ONE, 81, e53277. https://doi.org/10.1371/journal.pone.0053277, 2013.
9: Rockström, J., Steffen, W., Noone, K. … Foley, J.A. (2009): Planetary boundaries: Exploring the safe operating space for humanity, Nature 461, 472-475.
10: Hardenbicker, P., Weitere, M., Ritz, S., Schöll, F., Fischer, H.: Longitudinal Plankton Dynamics in the Rivers Rhine and Elbe, River Res Applic, 32, 1264– 1278, https://doi.org/10.1002/rra.2977, 2016.