## Slide 1: Tracing N2O formation in full-scale wastewater treatment with natural abundance isotopes
Team Empa: Joachim Mohn, Kerstin Zeyer
Team Eawag: Wenzel Gruber, Eberhard Morgenroth, Adriano Joss
Team University of Basel: Paul Magyar, Moritz F. Lehmann
Team ETH: Luzia von Känel, Daniel Braun
Funded by FOEN, SNSF, cantons: Bern, Basel-Landschaft, Thurgau, Zürich, companies: TBF+Partner AG Consulting Engineers, Holinger AG, Hunziker Betatech AG, Alpha Wassertechnik AG, arabern WWTP , REAL Luzern WWTP, Cham WWTP (GVRZ), ERZ Zürich, Giubiasco WWTP, Entsorgung St. Gallen and Uster WWTP.

## Slide 2: Relevance of N2O emissions from wastewater treatment
Introduction:
Nitrogen removal in WWTP: Microbial conversion of N-input (NH4+, R-NH2) to N2
Problem: Co-emissions of N2O; emission factor
IPCC emission factors based on few campaigns and not treatment specific.
Research questions:
Provide N2O emission estimates for treatment processes (relevant for CH)?
Identify microbial processes and parameters relevant for temporal variations?
Develop strategies for emission reduction?

## Slide 3: Specific N2O emission factors for treatment processes
Techniques Sampling via multiple floating flux chambers and central analytics
W. Gruber et al. (2020), Science of the Total Environ., https://doi.org/10.25678/0003WD
W. Gruber et al. (2021), Water Research X, https://doi.org/10.1016/j.wroa.2021.100122
Campaigns Campaigns at 10 different WWTP in Switzerland
From EF (N2O) to Swiss emissions Nutrient removal categories:
Carbon removal: 0-1 – 8%
Nitrification only: 1.8%
Denitrification: 0.9%
x N-load per category
= 410 – 1690 t N2O-N/yr-1
≈1% Swiss GHG emissions
What are responsible microbial processes?

## Slide 4: Isotope study: St. Gallen - Hofen WWTP
W. Gruber et al. (2022), Water Research X, https://doi.org/10.1016/j.wroa.2022.100130

## Slide 5: Temporal patterns and driving parameters
W. Gruber et al. (2022), Water Research X, https://doi.org/10.1016/j.wroa.2022.100130
Average emissions rather low, EF (N2O): 0.2%
Highest emissions in “cold season” controlling EF (N2O) – all lanes fully aerated!
Emissions correlated with NO2- / NO3- in effluent (and anti-correlated with N-removal efficiency)

## Slide 6: Isotope campaigns
W. Gruber et al. (2022), Water Research X, https://doi.org/10.1016/j.wroa.2022.100130
Isotope analysis of N species
NH4+: δ15N by hypobromite method
NO2-: δ15N, δ18O by azide method
NO3-: δ15N, δ18O by denitrifier method
δ18O of water
high temperature carbon reduction (TC/EA) and IRMS analysis
N2O isotopomer analysis Bag sampling and TREX-QCLAS analysis
SP=δ15Nα-δ15Nβ, δ15N, δ18O

## Slide 7: Microbial process attribution by isotopes (exemplary results)
W. Gruber et al. (2022), Water Research X, https://doi.org/10.1016/j.wroa.2022.100130
Reactive N-species
(NO2-)
δ18O(NO2-) - δ18O(H2O) ≈ 13‰ Complete oxygen exchange of nitrite with water
δ18O(H2O) good proxy for δ18O(NO2-)
For anoxic conditions (aeration off) δ18O(NO2-) increased due to enhanced consumption
N2O isotopomers
Aerated conditions: low SP values indicate nD or hD as main N2O production pathway, no contribution of Ni
Anoxic conditions: increasing SP values indicate partial N2O reduction
nitrifier denitrification
Ni
nD
hD
nitrification
denitrification

## Slide 8: Conclusions / Reduction strategies / Future plans
N2O from WWTP relevant GHG source (≈ 1% Swiss GHG emissions)
Highest emissions mostly occur in cold season, when NO2- accumulates
Isotopes indicate emissions mainly by (heterotrophic) denitrification
Reduction strategies
Maximize N2O reduction by optimizing reject water dosage (to diurnal variation of organic substrate) avoiding aeration of zone 1 (which reduces N2O reduction / increases emissions)
Future
On-line isotope analyses for qualitative N2O pathway identification
To develop targeted N2O mitigation strategies for individual WWTPs
Thank you for listening!
If you are interested check publications of Wenzel Gruber (Eawag)