## Slide 1
Stability analysis of check dam impacted by intermittent surges
Daochuan Liu（Ldaochuan@163.com）
26 May，2022
Notes: 1
Every one. I’m Daochuan Liu. My report is “Stability analysis of check dam impacted by intermittent surges”.

## Slide 2
PART 01 Introduction
PART 02 Fluctuation and decaying of surges movement
PART 03 Stability of check dam impacted by intermittent surges
CONTENTS
PART 04 Cases analysis
PART 04 Discussion and Conclusion
Notes: This report contents part 01~04.

## Slide 3
彭州至汶川高速方案研究
成都经济区环线高速公路彭州连接线工可
  Part 01
  Introduction
  CONTENTS
Notes: Prat one is introduction.

## Slide 4
Wenchuan-Yingxiu Disaster chain
Yu-zi river Disaster chain
Debris flows in Mingjiang river valley
Active geological structure
Frequent earthquakes
Great difference of elevation
Abundant rainfall
  Part 01
Notes: As we all know, because of active geological structure, Frequent earthquakes, Great difference of elevation and Abundant rainfall, a large number of natural disasters have occurred in western China. Such as Wenchuan-Yingxiu disaster chain, Debris flows in Ming-jiang river valley, Yu-zi river disaster chain.

## Slide 5
Expressway, Railway, Pipeline
Linear engineering
Check dam, silt dam, drainage channel
Prevention engineering
Multi-story building, Steel building
Building engineering
  Part 01
Notes: According to the field investigation, debris flow has great damage to linear engineering, prevention engineering and build engineering in the form of impact. Actually, viscose debris flows always move in the manner of intermittent surges and show obvious fluctuation. The impact of single surge has on the check dam was the only factor to be taken into consideration in the traditional design of debris flow control engineering, whereas stability variation of the check dam impacted by intermittent surges was always neglected.

## Slide 6
彭州至汶川高速方案研究
成都经济区环线高速公路彭州连接线工可
  Part 02
  Fluctuation and decaying of surges movement
※ Observation and data collection
  CONTENTS
※ Fluctuation and decaying characteristics
Notes: So this report initially discusses fluctuation and decaying characteristics of intermittent surges based on the material of the Jiangjia Gully (JJG).

## Slide 7
Area of 48.7 km2 ,channel length of 13.9 km
v was measured by two cross section
H was measured by ultrasonic sensors
Q, F, L can be estimated by v and H
Observation and data collection
  Part 02
Notes: Firstly, observation and data collection could be described. The JJG is on the right bank of the Xiaojiang River, with area of 48.7km2 and channel length of 13.9 km. Each year, about ten debris flows are observed in the last 60 years, and each event consists of tens to hundreds of surges. Real-time monitoring of debris flow in JJG is carried out every rainy season, which contains velocity, depth, discharge and so on.

## Slide 8
  Part 02
Fluctuation and decaying characteristics
Ligule form
Arrow form
Palm form
Chart: Surge number N
1st surge
2nd surge
Notes: These pictures shows the movement process of intermittent surges in the channel. The head is accompanied by strong turbulence while the body and tail are dominated by laminar flow. The head of different surges also shows different forms, such as ligule form, arrow form, and palm form.

## Slide 9
Fluctuation and decaying characteristics
Fluctuation with the surge process
Finally decays in a power law
α of v and H are 0.05~0.25 and 0.1~0.4
Nonlinear dynamic of surge series
Chart: (a)
 | 0.64442 | 0.64145 | 0.63853 | 0.63566 | 0.63284 | 0.63007 | 0.62734 | 0.62466 | 0.62202 | 0.61943 | 0.61688 | 0.61436 | 0.61189 | 0.60945 | 0.60705 | 0.60469 | 0.60236 | 0.60007 | 0.59781 | 0.59558 | 0.59339 | 0.59122 | 0.58909 | 0.58698 | 0.58491 | 0.58286 | 0.58084 | 0.57885 | 0.57688 | 0.57494 | 0.57302 | 0.57113 | 0.56926 | 0.56741 | 0.56559 | 0.56379 | 0.56201 | 0.56026 | 0.55852 | 0.55681 | 0.55511 | 0.55344 | 0.55178 | 0.55015 | 0.54853 | 0.54693 | 0.54535 | 0.54378 | 0.54224 | 0.5407 | 0.53919 | 0.53769 | 0.53621 | 0.53475 | 0.5333 | 0.53186 | 0.53044 | 0.52903 | 0.52764 | 0.52627
 | 0.59944 | 0.59771 | 0.59599 | 0.5943 | 0.59262 | 0.59096 | 0.58932 | 0.5877 | 0.58609 | 0.5845 | 0.58293 | 0.58137 | 0.57983 | 0.57831 | 0.5768 | 0.5753 | 0.57382 | 0.57236 | 0.57091 | 0.56947 | 0.56805 | 0.56664 | 0.56524 | 0.56386 | 0.56249 | 0.56113 | 0.55979 | 0.55846 | 0.55714 | 0.55583 | 0.55453 | 0.55325 | 0.55197 | 0.55071 | 0.54946 | 0.54822 | 0.54699 | 0.54577 | 0.54457 | 0.54337 | 0.54218 | 0.541 | 0.53984 | 0.53868 | 0.53753 | 0.53639 | 0.53526 | 0.53414 | 0.53303 | 0.53192 | 0.53083 | 0.52974
 | 1.1135 | 1.1113 | 1.1093 | 1.1145 | 1.1125 | 1.107 | 1.1052 | 1.1034 | 1.0917 | 1.082 | 1.0887 | 1.0841 | 1.0797 | 1.0785 | 1.0682 | 1.0597 | 1.0515 | 1.0478 | 1.0443 | 1.0352 | 1.025 | 1.0247 | 1.0189 | 1.016 | 1.0079 | 1.0039 | 0.99615 | 0.98861 | 0.98125 | 0.97407 | 0.96707 | 0.96024
Chart: (b)
 | 5.3577 | 5.3569 | 5.3585 | 5.3642 | 5.3684 | 5.3678 | 5.3637 | 5.3576 | 5.3521 | 5.3482 | 5.3426 | 5.3422 | 5.3288 | 5.3283 | 5.3263 | 5.3164 | 5.3093 | 5.3081 | 5.3078 | 5.3047 | 5.3016 | 5.2995 | 5.2956 | 5.2835 | 5.2708 | 5.2641 | 5.2572 | 5.251 | 5.2455 | 5.2405 | 5.2277 | 5.2152 | 5.2028 | 5.1905 | 5.1763 | 5.1623 | 5.1484 | 5.1347 | 5.1149 | 5.0953 | 5.0759 | 5.0568 | 5.038 | 5.0193 | 5.0009 | 4.9827 | 4.9648
 | 7.0952 | 7.0865 | 7.0746 | 7.0873 | 7.0888 | 7.084 | 7.0806 | 7.0905 | 7.0818 | 7.0649 | 7.0553 | 7.0451 | 6.996 | 6.97 | 6.9727 | 6.9508 | 6.9284 | 6.9112 | 6.8697 | 6.8415 | 6.8115 | 6.7958 | 6.7809 | 6.7399 | 6.6918 | 6.6947 | 6.663 | 6.6575 | 6.6236 | 6.6084 | 6.5794 | 6.5578 | 6.5473 | 6.5063 | 6.4698 | 6.43
X ~H, v, ρ, Q, etc.
α ~ Decaying coefficient
Notes: From a macro perspective, debris flow event can be regarded as a surge series . X is the parameters observed in real time, such as depth (H) velocity (v), flow density (ρ), flow discharge (Q), etc.
As we can see from these two pictures, it can be clearly seen that the velocity and depth fluctuate with the surge process and their mean curve < X > finally decays in a power law form. According to the results, the decaying coefficient α of the flow velocity and depth series are respectively 0.05~0.25 and 0.1~0.4, indicating that the intermittent surges present nonlinear dynamic behavior.

## Slide 10
彭州至汶川高速方案研究
成都经济区环线高速公路彭州连接线工可
  Part 03
  Stability of check dam impacted by surges
※ Empty‑storage reservoir condition
  CONTENTS
※ Half‑storage reservoir condition
Notes: From the above analysis, we can see the difference between single surge and intermittent surges, also shows different impact process of debris flow.
Then, the stability of the check dam under the impact of intermittent surges were discussed with empty and half storage reservoir conditions.

## Slide 11
Chart: surge number n
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34
890802 | 16.188 | 7.737 | 7.0231 | 8.5351 | 5.5381 | 3.717 | 4.0423 | 3.4094 | 2.1449 | 2.9308 | 2.4988 | 2.2571 | 1.682 | 1.381 | 1.5396 | 1.1252 | 1.0044 | 1.0641 | 1.0233 | 0.89229 | 0.68104 | 0.70125 | 0.64237 | 0.6255 | 0.59696 | 0.46838 | 0.53382 | 0.46956 | 0.47909 | 0.4289 | 0.43012 | 0.40803 | 0.36287 | 0.3584
890803 | 16.0162 | 9.5975 | 8.8045 | 8.6276 | 6.5875 | 5.1374 | 4.3265 | 3.0738 | 3.0437 | 2.2734 | 1.9792 | 1.6892 | 1.3635 | 1.257 | 1.1337 | 1.0323 | 0.91939 | 0.82473 | 0.74065 | 0.6622 | 0.62066 | 0.57978 | 0.54413 | 0.51883 | 0.49867 | 0.46925 | 0.44175 | 0.42816 | 0.41412
970715 | 3.4705 | 2.4955 | 2.1546 | 2.402 | 2.4528 | 2.316 | 2.0035 | 0.93437 | 2.2804 | 1.1735 | 1.4065 | 1.262 | 1.2372 | 1.1626 | 1.1296 | 1.0313 | 0.85774 | 0.72676 | 0.71175 | 0.68083 | 0.63294 | 0.54074 | 0.50649 | 0.42144 | 0.44996 | 0.42138 | 0.37457 | 0.38319 | 0.3224
Chart: surge number n
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34
890802 | 246.8592 | 56.6604 | 44.4899 | 46.5859 | 27.1807 | 13.9814 | 15.8055 | 11.9926 | 6.1576 | 10.9236 | 9.3846 | 8.5231 | 5.1035 | 3.7554 | 5.6758 | 2.903 | 2.602 | 3.4043 | 3.3913 | 2.5756 | 1.4727 | 1.7558 | 1.5551 | 1.6202 | 1.5306 | 0.8719 | 1.4379 | 1.003 | 1.2375 | 0.91259 | 1.0099 | 0.90123 | 0.66386 | 0.74923
890803 | 329.3859 | 70.4759 | 38.5548 | 36.8196 | 26.4111 | 19.9792 | 17.4461 | 10.1346 | 13.6811 | 7.6691 | 7.0798 | 5.8567 | 4.019 | 4.1936 | 3.8436 | 3.4312 | 2.8282 | 2.3512 | 2.0359 | 1.6762 | 1.73 | 1.5791 | 1.3821 | 1.3755 | 1.2918 | 1.0872 | 1.0258 | 1.0239 | 0.95767
970715 | 72.8413 | 18.3261 | 9.9546 | 9.7963 | 9.4016 | 8.1077 | 6.4437 | 1.9226 | 7.8389 | 2.443 | 4.0044 | 3.4432 | 3.4403 | 3.1992 | 3.1678 | 2.783 | 1.9783 | 1.5172 | 1.5629 | 1.4872 | 1.3708 | 1.0058 | 0.9603 | 0.68115 | 0.98157 | 0.83991 | 0.67501 | 0.83513 | 0.501
  Part 03
Considering run up in formula
3~5th was rapid decay area
Empty‑storage reservoir condition
Kc=1
Ky=1
Rapid decay area
Rapid decay area
Hci = Hi + Hp
Notes: Under the condition of empty-storage reservoir, when the intermittent surges impact on the check dam, the loads on the check dam are the self-weight of dam body, static pressure, side pressure and the impact force of surges. Especially, the value of the impact force in this report has considered the run-up phenomenon of surges. The result showed that Kc and Ky both decrease with the evolution of the surges under the condition of the empty-storage reservoir, and the decaying rate of the former 3~5 surges were the fastest.

## Slide 12
  Part 03
Half‑storage reservoir condition
Considering run up in formula
3~5th was rapid decay area
Envelope relationship between depth and stability coefficient
Hci = Hi + Hp
Notes: Compared with empty condition, the biggest difference is that the half-storage reservoir has a large amount of deposition before the check dam. So these two formula should consider the deposition pressure. As we can see the pictures, Kc and Ky both decreased with the evolution of surges, which was very similar to the case of the empty condition. In addition, results showed the relationship between surge depth and Kc and Ky. It was obvious that there was an envelope relationship between depth and stability, thus directly explaining the infuence of depth on dam stability.

## Slide 13
彭州至汶川高速方案研究
成都经济区环线高速公路彭州连接线工可
  Part 04
  Dissussion and Conclusion
※ Comparison and discussion
  CONTENTS
※ Conclusion

## Slide 14
Chart: surge number n
| 1 | 2 | 3 | 4 | 5
Jiang et al. 2019 | 1.4 | 1.38 | 1.32 | 1.27 | 1.18
Sun et al. 2018 | 4.165 | 4.0124 | 3.8053 | 3.573 | 3.3357 | 3.1058 | 2.8902 | 2.6918 | 2.5116 | 2.3488 | 2.2024 | 2.0709 | 1.9528 | 1.8466 | 1.751 | 1.6646 | 1.5865 | 1.5156 | 1.4512 | 1.3925 | 1.3388 | 1.2896 | 1.2444 | 1.2028
890802 | 4.2973 | 2.9256 | 2.5678 | 2.5296 | 2.0408 | 1.6613 | 1.6012 | 1.4262 | 1.1092 | 1.2045 | 1.0834 | 1.0082 | 0.86398 | 0.76596 | 0.78198 | 0.66359 | 0.61014 | 0.61704 | 0.59809 | 0.55115 | 0.46821 | 0.47 | 0.44207 | 0.43077 | 0.4168 | 0.35721 | 0.38264
890803 | 4.1718 | 3.1863 | 2.7866 | 2.395 | 2.0294 | 1.7259 | 1.5165 | 1.2733 | 1.1864 | 1.0315 | 0.93148 | 0.84193 | 0.74366 | 0.69249 | 0.64414 | 0.60506 | 0.5622 | 0.52451 | 0.48729 | 0.45285 | 0.42845 | 0.40814 | 0.39185
970715 | 2.2041 | 1.6855 | 1.4483 | 1.4359 | 1.3662 | 1.2662 | 1.127 | 0.69246 | 1.0633 | 0.74924 | 0.78241 | 0.72796 | 0.71006 | 0.67796 | 0.6594 | 0.62072 | 0.55556 | 0.49758 | 0.48448 | 0.4677 | 0.44272 | 0.39947 | 0.37876 | 0.3336
Chart: surge number n
| 1 | 2 | 3 | 4 | 5
Jiang et al. 2019 | 7 | 2.5 | 2 | 0.8 | 0.6
Sun et al. 2018 | 12.2897 | 11.1763 | 10.2287 | 9.3933 | 8.644 | 7.9672 | 7.3545 | 6.7999 | 6.2984 | 5.8453 | 5.436 | 5.0664 | 4.7324 | 4.4302 | 4.1564 | 3.908 | 3.6822 | 3.4765 | 3.2887 | 3.1169 | 2.9594 | 2.8147 | 2.6814 | 2.5583
890802 | 20.3919 | 12.2905 | 10.9841 | 11.8827 | 8.8915 | 6.2052 | 7.0549 | 6.2227 | 4.0261 | 6.8309 | 6.6216 | 6.6708 | 4.5779 | 3.7479 | 6.5674 | 3.3967 | 3.3709 | 5.438 | 6.1547 | 4.5456 | 2.317 | 3.4156 | 3.2149 | 4.0198 | 4.1058 | 1.7202 | 5.9378
890803 | 20.6784 | 13.46 | 10.8163 | 10.6515 | 9.6094 | 8.6137 | 8.4725 | 6.3673 | 8.9598 | 6.1661 | 6.6188 | 6.339 | 4.8715 | 6.2977 | 6.8072 | 6.8796 | 5.9636 | 5.221 | 5.0366 | 4.3042 | 6.5226 | 6.4418 | 5.3033
970715 | 7.8773 | 5.3426 | 4.145 | 4.368 | 4.4332 | 4.1997 | 3.7007 | 1.5266 | 5.3537 | 2.1485 | 3.6483 | 3.3323 | 3.5425 | 3.4981 | 3.7052 | 3.4234 | 2.4835 | 1.9888 | 2.2483 | 2.3097 | 2.2976 | 1.6788 | 1.8054 | 1.2624
  Part 04
Jang et al. (2019) have not given the trend of the whole process of Kc and Ky
Sun et al. (2018a) assumed that the discharge and depth in each surge was equal and only showed the smooth decay process of Kc and Ky
Results differently found out the influence of variation parameters on the stability change process
Comparison and discussion
Sun et al. 2018
Jiang et al. 2019
Sun et al. 2018
Jiang et al. 2019
Notes: We compared our results with Sun et al. (2018a) and Jang et al. (2019), which showed the similar decay rule of the Kc and Ky when intermittent surges impact on the check dam. However, Jang et al. (2019) have not given the trend of the whole process of Kc and Ky because of a few simulation data. Sun et al. (2018a) assumed that the discharge and depth in each surge was equal and only showed the smooth decay process of Kc and Ky (Fig. 11), whose results diferently found out the infuence of variation parameters on the stability change process.

## Slide 15
  Part 04
Conclusion
Intermittent surges showed strong fluctuation characteristics in the moving process. The decay coefficients of velocity and depth were 0.05 ~ 0.25 and 0.1 ~ 0.4, respectively. This was different from the random series, meaning that the intermittent surges show strong nonlinear behavior.
Regardless of the working conditions, the anti-slip stability coefficient Kc and anti-overturning stability coefficient Ky both decreased with the variation of surges, and the decaying rate of the former 3~5 surges were the fastest. Moreover, the stability coefficient decreased with the increase of deposition height.
There is an envelope relationship between depth and stability coefficient, which makes the change of depth restrict the development of dam stability coefficient, thus indicating that the stability coefficient of anti-slip and anti-overturning are very sensitive to the change of the flow depth of the surges.
Notes: Based on the research, There are three conclusions. Firstly, secondly, finally.

## Slide 16
Thanks For Your Attention！