## Slide 1
Qinzheng Li1,2, Johannes Böhm1, Linguo Yuan2, Robert Weber1
Development of a global model for zenith wet delays based on the random forest approach
1Department of Geodesy and Geoinformation, Vienna University of Technology (TU Wien), Austria
2Faculty of Geosciences and Environmental Engineering, Southwest Jiaotong University, China
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria

## Slide 2
Introduction
1/9
High correlation between residual delay and other parameters of interest such as station height and receiver clock bias
Incorrect modeling of tropospheric (wet) delay
affects precision and accuracy of position solution
causes mis-interpretation of geophysical signals such as crustal deformation, terrestrial water storage variations
Tropospheric delay is a major error source in the analysis of space geodetic observations
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria
Several positioning and navigation tasks such as real-time applications do not have the benefit of post-processing analyses, necessitating the availability of accurate a-priori estimates for ZWD.
Performance of tropospheric delay modeling is significantly limited due to the high dynamics of the wet portion in the neutral atmosphere

## Slide 3
Introduction
Ray-tracing through NWMs
Require the knowledge of vertical profiles of temperature and humidity
Saastamoinen (1972) model
Global empirical troposphere models such as GPT3
2/9
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria
Unable to capture daily and complex variations of meteorological parameters
Unable to account for spatial and temporal variations in the relationship
RF-based ZWD model
Meteorological data are available
Without meteorological data
How can we improve ZWD prediction accuracy if meteorological data are available at some stations?

## Slide 4
Dataset and Methodology
Radiosonde Measurements
Meteorological variables at discrete isobaric levels (usually twice per day)
Zenith wet delay (ZWD) are determined by the numerical integration of nonhydrostatic refractivity from the site's height to top sounding profiles
Validation: Sounding profiles for the year 2020
3/9
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria
Modeling: 10 years (2010-2019) of radiosonde data at 586 sites

## Slide 5
ZWD modeling based on the RF regression
Functional formulation (RF-B):
Functional formulation (RF-A):
Functional formulation (RF-D):
Functional formulation (RF-C):
Dataset and Methodology
4/9
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria

## Slide 6
Optional number of trees for a random forest system
10-fold cross validation
Dataset and Methodology
RMS of ZWD differences between modeled and 'observed' values
Ensemble learning can help the RF-based ZWD model to achieve better generalization ability
ZWD modeling accuracy tends to be stable when the number of trees is larger than 20
5/9
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria

## Slide 7
Overall performance of the RF-based ZWD models
Results
Model | Bias [cm] | STD [cm] | RMS [cm] | R
GPT3 | -0.48 | 4.16 | 4.19 | 0.92
RF-A | -0.13 | 4.14 | 4.14 | 0.92
RF-B | -0.12 | 4.16 | 4.16 | 0.92
RF-C | 0.03 | 3.09 | 3.09 | 0.95
RF-D | 0.04 | 2.94 | 2.94 | 0.96
RF-A achieves a bias of -0.1 cm and overall RMS error of 4.1 cm, which is comparable to GPT3
ZWD modeling accuracy cannot be improved by the introduction of a-priori information from the GPT3 model
ZWD prediction accuracy is significantly improved by taking into account surface meteorological parameters in the functional formulation , especially for es
6/9
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria

## Slide 8
Results
RF-based ZWD models mitigate negative biases in the regions with monsoon climate and tropical rainforest climate types, in particular with the introduction of surface meteorological information
7/9
Spatial features of model accuracy
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria

## Slide 9
Spatial features of model accuracy
Results
ZWD prediction acccuracy for RF-C and RF-D is clearly improved across the globe by considering the surface meteorological parameters in the modeling
Complex variations of the moisture in the lower atmosphere for the regions with monsoon climate type
8/9
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria
Mean values and seasonal components in PW time series were removed
Notes: the predicted ZWD accuracy can be further improved across the globe by considering surface meteorological variables especially in regions with monsoon climate type

## Slide 10
The RF-based ZWD model with meteorological parameterization (RF-D) can achieve an overall accuracy of 2.9 cm and a bias close to zero
ZWD modeling accuracy is significantly improved by the introduction of surface water vapor pressure into functional formulation in comparsion with the surface temperature
The RF-based ZWD models clearly mitigate negative biases in the regions with monsoon climate and tropical rainforest climate type
Compared with the GPT3, ZWD modeling accuracy can be improved across the globe by considering surface meteorological parameters, especially in the regions with monsoon climate type
Summary
9/9
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria

## Slide 11
Thank you!
Department of Geodesy and Geoinformation
Vienna University of Technology
Wiedner Hauptstraße 8
1040 Wien, Austria
Faculty of Geosciences and Environmental Engineering
Southwest Jiaotong University
Xi'an Road 999
Chengdu 611756, China
e-mail: qinzheng.li@geo.tuwien.ac.at
Qinzheng Li
The subroutine of GZWD-RF model can be freely accessed from the VMF Data Server
https://vmf.geo.tuwien.ac.at/codes/gzwd_rf/
Session G1.3 - Data Science and Machine Learning in Geodesy
EGU 2022 - European Geosciences Union General Assembly
May 23-27, 2022, Wien, Austria