## Slide 1: Integrated Multiscale Urban Flood Modeling with Drainage Pipe System
L. Dasallas, H. An and S. Lee
Chungnam National University, Korea
KWater Research Institute, Korea
Korea Environment Institute

## Slide 2: Outline
Research background
Supplementing research gaps
Methodology
Model input data
Urban flood event
Results and discussion
Summary and conclusion

## Slide 3: Why is FLOOD MODELING important?
Flood susceptibility
Flood preparation and mitigation
4
Susceptibility to rainfall events

## Slide 4
Watershed
~1,000,000,000 m2
Inundation
<50,000,000 m2
Sewer pipe cell grid
<100 m2
FLOOD MODELING TECHNIQUES
Spatial Extent
Dimensionality
Mathematical complexity
Kinematic
Inertial
Diffusive
Coupled
5
Dynamic

## Slide 5: Urban flood modeling
Inundation modeling | Urban flood modeling
2D overland flow | More complex dynamics (building, artificial barriers)
Soil type based infiltration | More impervious surfaces, more runoff
 | Integration of surface and sewer pipe system
Generalized DEM | Requires higher resolution DEM
Scale (~50km2) | Scale (<100m2)
 | More densely populated areas
6

## Slide 6: RESEARCH GAPS
Limited availability of adequate resolution elevation data
Lack of systematized drainage network data
Scarce researches on flood modeling/mitigation
Issues for developing countries:
Separate computations of large scale runoff, urban domain-scale inundation and sewer pipe interaction
Long simulation time for high-resolution data
Incompatibility and complexity in integration
Flood modeling:
7

## Slide 7
Validation: 2009 Rainfall event
SEWER PIPE MODELING
DTM
DSM
Road network
Urban sub-catchment modified DEM
Watershed DEM
Rainfall data
MULTI-SCALE FLOOD MODELING
Urban flood extent and depth
Manhole
Sewer pipe
Storm drain
Drainage network
Model application: 2020 Rainfall event
Urban flood analysis
Research conclusion
Rainfall-runoff and inundation
Surface and subsurface interaction
Methodology outline
11

## Slide 8
Constructing synthetic sewer network using GIS
Sewer pipe data (293)
ID Length Shape Slope Manning coefficient Diameter Upstream manhole Downstream manhole
Manhole data (333)
ID Location in x and y-coordinates Bottom elevation Shape diameter
Drainbox data (1866)
ID Area Face perimeter Bottom elevation Depth Location in x and y-coordinates Smaller width of storm drain cover Tube diameter between drainbox and pipe Connecting pipe
pipe
manhole
Storm drain
23

## Slide 9
Chart: Date
| 44146 | 44146.25 | 44146.5 | 44146.75 | 44147 | 44147.25
Tanay | 17 | 6 | 44 | 176 | 136 | 12
Science Garden | 1 | 4 | 17 | 26 | 110 | 62
NAIA | 2 | 6 | 15 | 24 | 99 | 37
Manila | 31 | 1 | 0 | 15 | 86 | 31
Urban flood events
Vamco 2020
26

## Slide 10: Results and Discussions

## Slide 11: SYNTHETIC SEWER SYSTEM
Stream channel
Synthetic sewer system:
1st order
Synthetic sewer system:
2nd order
39

## Slide 12: SIMULATION RESULTS: FLOOD DEPTH (M)
40

## Slide 13: SIMULATION RESULTS: FLOOD DEPTH (M)
41

## Slide 14: Flood depth comparison: Case 1 and Case 2
A
B
C
D
Case 1: No sewer
Case 2: Sewer
42

## Slide 15: Sewer pipe flow
Predominant flow is observed within the principal pipe
Weakened/backflows are observed in:
  Chokepoint pipe junctions
  Pipes with lesser steep slope
  Upstream connecting pipe is perpendicular to the receiving pipe
Pipe flow Q (m3/s)
44

## Slide 16
5. Comparison of sewer and no-sewer simulation
Case 1: No sewer flood simulation
Case 2: 2nd order sewer-integrated flood simulation
Change in water level (Tumana Station)
Tumana station
Observed increase in simulated water level and flood extent on surrounding flood plain with integration of sewer flow
26

## Slide 17: Flood validation 2020 Case event
45
 | District |  | Street | Maximum height | Peak | Flood time | Image
1 | Bench | Tumana | Pipino, Mais | tuhod sa 2nd floor |  |  | 
2 |  | Tanong | Manggahan st | dibdib |  |  | Image 1
3 | Paula | Tanong | Providence village, Anne st. | 20 ft | 10-11am |  | Image 2
4 |  | Malanday | Malaya st | 2nd floor | 6am |  | 
5 |  | Tumana | Dona Petra | 2nd floor |  |  | Image 3
6 |  | Conception Uno | Shoe avenue | gutter deep | 10:30 AM |  | 
7 |  | Conception Uno | Libis | balikat |  |  | 
8 |  | San roque | Midtown subd, dragon st | dibdib |  |  | 
9 |  | Malanday | Purok 4 | bewang second floor |  |  | 
10 |  | Malanday | Bouganvilla | bubong |  |  | Image 4
11 |  | Tumana | Bagong Farmers 1 | step 1 from 2nd floor |  |  | 
12 | Robert | Dela Pena | Flores st | leeg | noon |  | Image 7
13 |  |  | Providence, Austin St | bewang second floor |  |  | 
14 |  |  | Providence | bewang second floor |  |  | 
15 |  | Calumpang | Roxas st | bewang | noon |  | 
16 | Gema | Sto nino | sto nino highschool, agriculture st | bewang |  |  | 
17 | Airam | San roque | Munding ave, ignacio st, dela paz highway | dibdib |  |  | 
18 |  | Sto. Nino | Pla pla st. | 1 step to 2nd floor |  |  | 
19 |  | Tanong | Providence | 5m | 4am |  | 
20 | Emelita | TAnong | Tuazonville, Road 3 and road 4 | tuhod |  |  | 
21 | Ultimo | Tanong | Lopez jaena | lampas tuhod |  |  | 
22 | Luciano | San roque | New Marikina subd, flamingo, eagle, paralle, bacolod st. | dibdib |  |  | 
23 | Luciano |  | lark st | 5ft | 12nn |  | 
24 | Judea | Parang | Kaolin st. Calcite st | 2 ft |  |  | 
25 | Shiela | Malanday | Purok 7, Dahlia st | 2nd floor |  |  | 
26 |  | Barangka |  | lubog ang 1st floor | 7am |  | Image 5
27 | Johnardie | Tumana | singkamas | lampas 2nd floor | 10-11am |  | 
28 | Janina | Conception Uno | Libis, jp rizal | dibdib. Lampas tao | 10-11am | subside 3-4pm | Image 6
29 | Elsa | Tumana | Ampalaya | 2nd floor |  |  | 
30 | Janice | San Roque | eagle st, new marikina | 4ft |  |  | 

## Slide 18: Flood validation 2020 Case event
>2.0m flood depth
~1.0m flood depth
~0.5m flood depth
46

## Slide 19: Sewer pipe model: Analysis summary
Model can simulate recession of flood in surfaces connected to the sewer pipes
Increase in river extent is observed when applying sewer simulation
Surcharge is expected for bottleneck pipes, slope with smaller values and when upstream pipe is perpendicular to the receiving pipe
Accuracy of flood is sensitive to small changes in DEM
51

## Slide 20: Limitations/recommendations for future studies
River widening/desilting
Construction of:
  River levees
  Outlets with gateways
  Pump stations
Increasing pipe diameter for bottle neck areas
Recommendation for well-designed sewer system
Recommendation in reducing flood vulnerability of the study domain
Applicable for short-term urban flood events
Lack of information for detailed river cross section area
Information on upstream dam and levee
Detailed survey of sewer network
Higher order synthetic system simulation
52

## Slide 21: Thank you for listening.
Contact:
Lea Dasallas, PhD
Chungnam National University, Korea
lea.dasallas@o.cnu.ac.kr