## Slide 1
Dynamic and equilibrium surface tension of Rhamnolipid:
Effect of real-time temperature
Thuc Nguyen and Gilboa Arye
(nguyan@post.bgu.ac.il, aryeg@bgu.ac.il)
French Associates Institute for Agriculture and Biotechnology for Drylands, Jacob Blaustein Institutes for Desert Research,
Ben Gurion University of the Negev, Israel
Figure 1. Chemical structures of mono and di-rhamnolipid
(Wittgens et al., 2017)
Figure 2. Pendant drop method for surface tension measurement
Control chamber:
T (°C) = constant
H (%) = constant
RLP solution
Air
Figure 3. Surface tension as a function of time (γt)
With high biodegradability, bio-surfactants are considered as an eco-friendly alternative to synthetic surfactants. In conjunction with the changing soil temperature under effects of climate change, knowledge about temperature-dependent surface activities of bio-surfactants is essential. In this study, dynamic and equilibrium surface tension of Rhamnolipid (RLP) was investigated as functions of concentration and temperature.

## Slide 2
Equilibrium surface tension as a function of temperature
Figure 4. Equilibrium surface tension (γeq) as a function of concentration.
γeq decreased due to adsorption of surfactant at water/air interface.
As adsorption reached saturation, γeq remained unchanged.
Figure 5. Critical micelle concentration (CMC) as a function of temperature
Figure 6. Equilibrium surface tension as a function of temperature
γeq at pre-CMC decreased more significantly with increasing temperature than γeq at post-CMC, most likely because micelles are more stable with heat than monomers.
2
CMC
With increasing temperature, the reduction in hydration of hydrophilic groups favors micellization  decreased CMC.
With further increased temperature, the breakdown of the structured water surrounding disfavors micellization  increased CMC

## Slide 3
Dynamic surface tension under effects of temperature
Figure 7. Surface tension of 30 ppm and 400 ppm RLP as a function of time (γt )
Figure 8. dγ/dt-0.5 as a function of concentration
dγ/dt-0.5 decreased with increasing concentration
 DL increased with increasing concentration.
dγ/dt-0.5 vs ln(C) created two linear regressions with two distinctive slopes, representing pre-CMC and post-CMC. Temperature affected the slopes at pre-CMC more than at post-CMC.
 Temperature affected diffusion at pre-CMC more than at post-CMC.
Conclusions:
Equilibrium surface tension decreased with increasing temperature.
The diffusion of surfactant molecules increased with increasing temperature.
At both equilibrium and dynamic surface tension, the pre-CMC concentrations were affected more significantly than the post-CMC concentrations.
3
=
∼
Asymptotic solution of Ward and Tordai equation
The diffusion coefficient at long term (DL) was estimated from the slope dγ/dt-0.5 by fitting γt (t-0.5 ) to the asymptotic equation.
DL is inversely proportional to dγ/dt-0.5 .