## Slide 1
Investigating the interaction between snowmelt runoff and road in the activation of hillslope instabilities affecting a landslide-prone mountain basin through a multi-modeling approach
Luca Mauri1, Sara Cucchiaro2, Stefano Grigolato1, Giancarlo Dalla Fontana1, Paolo Tarolli1
1Department of Land, Environment, Agriculture and Forestry, University of Padova, Legnaro (PD), Italy
2Department of Agricultural, Food, Environmental and Animal Sciences, University of Udine, Udine (UD), Italy
EGU22-4691

## Slide 2
Snowmelt runoff is responsible for the activation of land degradation processes in mountain landscapes
Roads presence in steep slopes mountain areas is also linked with landslides occurrence
Accurate investigation of the interaction between snowmelt runoff and roads in the occurrence of hillslope failures is still obscure
Snowmelt, roads and landslides in mountain landscapes
Mauri et al., 2022. Evaluating the interaction between snowmelt runoff and road in the occurrence of hillslope instabilities affecting a landslide-prone mountain basin: a multi-modeling approach. [under review in Journal of Hydrology]

## Slide 3
Scope: to assess the relationship between snowmelt runoff, road presence and terrain instabilities affecting a landslide-prone steep slope mountain meadow (northern Italy)
Research purpose, study area, material and methods (1/2)
Mauri et al., 2022. Evaluating the interaction between snowmelt runoff and road in the occurrence of hillslope instabilities affecting a landslide-prone mountain basin: a multi-modeling approach. [under review in Journal of Hydrology]

## Slide 4
Research purpose, study area, material and methods (2/2)
Mauri et al., 2022. Evaluating the interaction between snowmelt runoff and road in the occurrence of hillslope instabilities affecting a landslide-prone mountain basin: a multi-modeling approach. [under review in Journal of Hydrology]
Snowmelt Runoff Model - SRM
Road Erosion Steady-State model - RESS
SImulated Water Erosion model - SIMWE
(Martinec and Rango, 2008)
(Montgomery and Dietrich, 1994; Borga et al., 2005)
(Mitasova et al., 2003)
Role of the road ?

## Slide 5
Multi-modelling results and statistics (1/3)
Snowmelt Runoff Model -SRM-
Mauri et al., 2022. Evaluating the interaction between snowmelt runoff and road in the occurrence of hillslope instabilities affecting a landslide-prone mountain basin: a multi-modeling approach. [under review in Journal of Hydrology]
Road Erosion Steady-State model -RESS-

## Slide 6
Multi-modelling results and statistics (2/3)
SIMulated Water Erosion model -SIMWE-
Mauri et al., 2022. Evaluating the interaction between snowmelt runoff and road in the occurrence of hillslope instabilities affecting a landslide-prone mountain basin: a multi-modeling approach. [under review in Journal of Hydrology]
Receiver Operating Characteristic (ROC) analysis
Cohen’s kappa-index
Area Under the ROC Curve (AUC)
[Instability susceptibility maps validation]
(AUC)=0.92 (Sr), 0.94 (Rr)
[predicted vs observed instabilities agreement]
k= 0.58 (Sr), 0.55 (Rr)
(Cohen, 1960)
Guzzetti et al., 2006

## Slide 7
Multi-modelling results and statistics (3/3)
Mauri et al., 2022. Evaluating the interaction between snowmelt runoff and road in the occurrence of hillslope instabilities affecting a landslide-prone mountain basin: a multi-modeling approach. [under review in Journal of Hydrology]
YesRoad vs NoRoad cross section of SIMWE-derived water depth across the landslide area

## Slide 8
Conclusions
Results attested the key role played by the road in altering snowmelt runoff pathways
Results also proved the combined contribution of snowmelt runoff and road to the foreseen activation of a shallow landslide
A challenging predictive, multi-modeling approach is presented and validated
Efficient tool for prevent and mitigate the occurrence of similar land degradation processes over time
Mauri et al., 2022. Evaluating the interaction between snowmelt runoff and road in the occurrence of hillslope instabilities affecting a landslide-prone mountain basin: a multi-modeling approach. [under review in Journal of Hydrology]

## Slide 9: Thank you!
luca.mauri.2@phd.unipd.it

## Slide 10
ALS-survey parameters | Information / Value
Period of the survey | April-December 2018
Survey conditions | Snow-free conditions, minimal leaves presence
LIDAR system | Optech ALTM Gemini
Number of flights | 46
Average flight altitude (a.g.l.) | 850 m
Flying speed | 75 knots
Scan angle | 32°
Laser frequency | 100 kHz
Average point density | 5 pt/m2
Input | Unit of measurement
Temperature (T) | °C
Precipitation (P) | mm/h
Snow Covered Area (SCA) | %
Temperature Lapse Rate (γ) | °Cm-1
Critical Temperature (TCRIT) | °C
Degree-day factor (An) | cm°C-1d-1
Rainfall Contributing Area (RCA) | (-)
Recession coefficient (k) | (-)
Runoff coefficient snow (Cs) | (-)
Runoff coefficient rain (Cr) | (-)
Time lag (L) | (h)
Overview of ALS surveys parameters and characteristics
Snowmelt Runoff Model (SRM) inputs
Input | Value | Unit of measurement
Max snowmelt runoff (Srmax) | 11.3 (May 2018) | mmh-1
Saturated soil conductibility (k) | 10-3 (G) 0.0 (Rd, Rk) | ms-1
Excess rate (May 2018) | 0.0 (G) 11.3 (Rd, Rk) | mmh-1
Manning (n) | 0.045 (G) 0.016 (Rd) 0.099 (Rk) | (-)
SIMulated Water Erosion (SIMWE) inputs. G stands for grassland, Rd stands for road and Rk stands for rocky areas located on the top of the watershed
Mauri et al., 2022. Evaluating the interaction between snowmelt runoff and road in the occurrence of hillslope instabilities affecting a landslide-prone mountain basin: a multi-modeling approach. [under review in Journal of Hydrology]

## Slide 11
Input | Value | Unit of measurement
DEM without road | / | (-)
Road points | / | (-)
Drainage systems location | / | (-)
Soil depth (z) | 0.5 | m
Internal friction angle (ϕ) | 35.0 | Decimal degrees
Soil density (ρs) | 1800 | kg·m-3
Soil transmissivity (T) | 0.3·10-3 | m2·s-1
Soil cohesion (Cohs) | 0.1 | kg·m-1·s-2
Root cohesion (Cohr) | 0.0 | kg·m-1·s-2
Vegetation surcharge (W) | 0.0 | kg·m-1·s-2
Road width | 4.0 | m
Relative road cut depth (rrc) | 0.5 | (-)
Max rainfall runoff (Rrmax) | 62.8 (May 2018) | mm·h-1
Max snowmelt runoff (Srmax) | 11.3 (May 2018) | mm·h-1
Rainfall intensity increment step | 1.0 | mm·h-1
Water density (ρw) | 1000 | kg·m-3
Flow direction algorithm | D-inf | (-)
Road Erosion Steady-State (RESS) inputs necessary for soil stability investigations
Model | Symbol / Abbreviation | Description
Snowmelt Runoff Model (SRM) | Sr | Snowmelt runoff
 | Rr | Rainfall runoff
 | SRr | Combined Sr and Rr
 | T | Temperature
 | P | Precipitation
 | SCA | Snow Covered Area
 | γ | Temperature Lapse Rate
 | Tcrit | Critical temperature
 | An | Degree-day factor
 | RCA | Rainfall Contributing Area
 | K | Recession coefficient
 | Cs | Runoff coefficient snow
 | Cr | Runoff coefficient rain
 | L | Time lag
Road Erosion Steady-State model (RESS) | z | Soil thickness
 | ϕ | Internal friction angle
 | ρs | Soil density
 | ρw | Water density
 | Tr | Soil transmissivity
 | Cohs | Soil cohesion
 | Cohr | Root cohesion
 | W | Vegetation surcharge
 | rrc | Relative road cut depth
 | CritSr | Critical Sr
 | CritRr | Critical Rr
 | CritSRr | Critical SRr
 | RISr | Relative Impact index from Sr
 | RIRr | Relative Impact index from Rr
 | RISRr | Relative Impact index from SRr
SIMulated Water Erosion model (SIMWE) | k | Saturated soil conductibility
 | n | Manning’s n
Symbols and abbreviations used in models application
Mauri et al., 2022. Evaluating the interaction between snowmelt runoff and road in the occurrence of hillslope instabilities affecting a landslide-prone mountain basin: a multi-modeling approach. [under review in Journal of Hydrology]