## Slide 1
Precision of Galileo satellite orbits obtained from simulated VLBI observations
Wolf H.1, Böhm J.1, Nothnagel A.1, Hugentobler U.2, Schartner M.3
1TU Wien, Department of Geodesy and Geoinformation
2TU München, Institute for Astronomical and Physical Geodesy
3ETH Zürich, Department of Civil, Environmental and Geomatic Engineering
EGU 2022

## Slide 2
Overview
Comparing evaluation of satellite observations for estimating orbit arcs by analysis …
26.05.2022
EGU 2022
… beforehand
Dilution of Precision (DOP) factors as indicator for sensitivity of satellite observations
... of simulations
precision of estimated orbit arc assessed based on Monte Carlo simulations

## Slide 3
Evaluation of satellite observations
Dilution of Precision (DOP) factors indicate sensitivity of observation towards (in our application) different parameters
DOP factors for sensitivity towards satellite position in the NTW-frame such as
  normal component → normal DOP (NDOP)
  tangential component → tangential DOP (TDOP)
  cross-track component → cross-track DOP (WDOP)
represent formal error in respective component per VLBI measurement error in → unitless
the smaller the value of the respective DOP the higher the sensitivity of the observation to the corresponding parameter
→ DOP factors as optimization criterion for scheduling of satellite observations
26.05.2022
EGU 2022

## Slide 4
Precision of Galileo satellite orbits
26.05.2022
EGU 2022
schedules
simulations
analysis
1000 simulations with 50 [ps] white noise for satellite scans
creating schedules including quasar and satellite observations
estimation of offset from a-priori orbit (sp3) for the individual components of satellite position as piecewise linear offsets
precision of adjusted arc in terms of repeatability

## Slide 5
VieSched++ is used to create schedules including satellite and quasar observations
  satellite scans with 5 seconds duration
  30 seconds break in between for calibration, slewing, …
  e.g. 24 hour session including satellite observations for 40 minutes from 4:00 to 4:40
    4:00:00 – 4:00:05
    4:00:35 – 4:00:40
    …
    4:39:40 – 4:39:45
    → in total 69 satellite scans
  remaining part of schedule is filled with quasar observations
    more than 100 scheduled sources for each schedule
Scheduling of satellite and quasar obs.
26.05.2022
EGU 2022

## Slide 6
Adjustment of Galileo satellite orbits
26.05.2022
EGU 2022
Vienna VLBI and Satellite Software (VieVS) for simulating and analysing the schedules
  1000 simulations
    white noise of 50 [ps] for satellite observations
  estimation of offset from a-priori orbit (sp3) for the individual components of satellite position
  estimation settings
    source coordinates
    station coordinates
    troposphere
    clock
    EOP
    satellite position
      as continuous piecewise linear offsets
      estimation interval: 10 min precision of adjusted arc in terms of repeatability
      relative constraints for each component: 10 cm

## Slide 7
Scenario I: GSAT0208
26.05.2022
06.02.2022 00:00 – 00:00
9 station network
Obs. period A: 08:10 – 08:50
  KOKEE12M
  MACGO12M
  NYALE13S
  WESTFORD
  WETTZ13S
  RAEGYEB
Obs. period B: 21:50 – 22:30
  HART15M
  ISHIOKA
  NYALE13S
  RAEGYEB
  WETTZ13S
EGU 2022

## Slide 8
Scenario I: GSAT0208
Obs. period A: 08:10 – 08:50
  #stations: 6
  ØNDOP: 18.8
  ØTDOP: 1.3
  ØWDOP: 2.3
26.05.2022
06.02.2022 00:00 – 00:00
9 station network
Obs. period B: 21:50 – 22:30
  #stations: 5
  ØNDOP: 62.2
  ØTDOP: 1.4
  ØWDOP: 1.8
EGU 2022

## Slide 9
Scenario I: GSAT0208
26.05.2022
Obs. period A: 08:10 – 08:50
  #stations: 6
  ØNDOP: 18.8
  ØTDOP: 1.3
  ØWDOP: 2.3
Obs. period B: 21:50 – 22:30
  #stations: 5
  ØNDOP: 62.2
  ØTDOP: 1.4
  ØWDOP: 1.8
EGU 2022

## Slide 10
Scenario I: GSAT0208
26.05.2022
Obs. period A: 08:10 – 08:50
  #stations: 6
  ØNDOP: 18.8
  ØTDOP: 1.3
  ØWDOP: 2.3
Obs. period B: 21:50 – 22:30
  #stations: 5
  ØNDOP: 62.2
  ØTDOP: 1.4
  ØWDOP: 1.8
EGU 2022

## Slide 11
Scenario II: GSAT0206
06.02.2022 00:00 – 00:00
9 station network
Obs. period A: 00:50 – 01:40
  ISHIOKA
  KOKEE12M
  MACGO12M
  NYALE13S
  WESTFORD
Obs. period B: 12:10 – 13:00
  MACGO12M
  NYALE13S
  RAEGYEB
  WESTFORD
  WETTZ13S
EGU 2022
26.05.2022

## Slide 12
Scenario II: GSAT0206
Obs. period A: 00:50 – 01:40
  #stations: 5
  ØNDOP: 46.5
  ØTDOP: 1.6
  ØWDOP: 1.8
06.02.2022 00:00 – 00:00
9 station network
Obs. period B: 12:10 – 13:00
  #stations: 5
  ØNDOP: 40.7
  ØTDOP: 2.0
  ØWDOP: 2.3
26.05.2022
EGU 2022

## Slide 13
Scenario II: GSAT0206
Obs. period A: 00:50 – 01:40
  #stations: 5
  ØNDOP: 46.5
  ØTDOP: 1.6
  ØWDOP: 1.8
Obs. period B: 12:10 – 13:00
  #stations: 5
  ØNDOP: 40.7
  ØTDOP: 2.0
  ØWDOP: 2.3
26.05.2022
EGU 2022

## Slide 14
Scenario II: GSAT0206
Obs. period A: 00:50 – 01:40
  #stations: 5
  ØNDOP: 46.5
  ØTDOP: 1.6
  ØWDOP: 1.8
Obs. period B: 12:10 – 13:00
  #stations: 5
  ØNDOP: 40.7
  ØTDOP: 2.0
  ØWDOP: 2.3
EGU 2022
26.05.2022

## Slide 15
Conclusion
26.05.2022
EGU 2022
precision of the adjusted arc is dependent on observation geometry
DOP factors and results of analysis based on Monte Carlo simulations concur
DOP factors could be used as optimization criterion during the scheduling process
observations rather insensitive to satellite normal component → contraints advisable

## Slide 16
References
26.05.2022
EGU 2022
Wolf H. (2021): Satellite Scheduling with VieSched++, Master Thesis, Technical University of Vienna.
Hellerschmied A. (2018): Satellite Observations with VLBI, Doctoral Thesis, Technical University of Vienna.
Klioner S. (1991): General Relativistic Model of VLBI Observables, Proceedings of the AGU Chapman Conference on Geodetic VLBI: Monitoring Global Change, Washington D.C., April 22-26. 1991.
VieSched++: https://github.com/TUW-VieVS/VieSchedpp/