## Slide 1: Prediction of hourly runoff in the Savitri River basin in India: Use of a local approximation approach
Authors: Namitha Elza Saji, V Jothiprakash, Bellie Sivakumar,
Indian Institute of Technology Bombay
HS3.1

## Slide 2: Nonlinear Local Approximation method of Prediction
Time series of hydro-meteorologic variables are the main input for hydrologic prediction
Hydro-meteorologic time series have both deterministic and stochastic component
Available hydrologic prediction concepts either considers deterministic or stochastic nature of time series
Chaos theory considers both deterministic and stochastic nature of a series
Nonlinear local approximation method of prediction (NLAP) method is for forecasting the future values of a variable using the concepts of chaos theory.
Figure 1: Time series plot for daily runoff (Source: Islam and Sivakumar 1999)
Notes: Once the phase-space is correctly reconstructed in a dimension m for a single or multivariate series, the dynamics of a system can be represented in terms of an m-dimensional mapping function, ƒT (Sivakumar 2003). The mapping function can be written in the following form:
Yj+T = fT(Yj)
where Yj and Yj+T are vectors describing the state of the system at current state and future state respectively.
An appropriate expression for fT is to be found to predict the future using either global or local approximation techniques. The global approach considers the entire phase space of the attractor whereas the local approximation approach only considers nearby states to make prediction. The local approximation method is commonly used in studies for identification of chaos.
In the local approximation approach entire phase space is subdivided into many local neighbourhoods and an approximation function is found for each neighbourhood. To predict a variable X j+T at a future state using past observations and an m-dimensional vector Yj at current state, k nearest neighbours of Yj are found based on the minimum values of ║Yj -Yj′║, where j′ < j.
An optimum value of k is determined by a trial and error procedure (Dhanya and Kumar 2011). The single variable prediction and the multi-variable prediction approach slightly differs in the manner it is considering neighbours. In single variable case, the variable to be predicted is included in the reconstructed vector and the prediction is obtained by averaging the k number of nearest neighbours of the variable.

## Slide 3: Nonlinear Local Approximation method of Prediction
Phase space reconstructed in dimension ‘m’
(Last vector is Yj)
Identifying k number of nearest neighbour of Yj as Yj’ , j’ <j
Find vector Yj’+1
Finding Xj’+1 = mth element of Yj’+1
= mean(Xj’+1)
Y1 = (X1, X2)
Y2 = (X2, X3)
Y3 = (X3, X4)
Y4 = (X4, X5)
Y5 = (X5, X6)
Y6 = (X6, X7)
Y7 = (X7, X8)
Y8 = (X8, X9)
Y9 = (X9, X10)
Suppose Y5 and Y3 are the two nearest neighbours of Y9
Yj’ = Y5 & Y3
Yj’+1 = Y6 & Y4
Y6 = (X6, X7)
Y4 = (X4, X5)
Xj’+1 = X7 & X5
X11 = mean (X7 & X5 )
Example: For dimension 2
Prediction accuracy depends on embedding dimension (m) and number of nearest neighbours (k) considered

## Slide 4: Study area – Savitri River Basin
One of the west flowing river basins in India
Basin has a total area of 2262.42 km2
Lies within the global coordinates of 18⁰20 N to 17⁰50 N and 73⁰07 E to 73⁰41 E.
Originates in the Mahabaleshwar plateau and flows down for a length of 95.1 km to join the Arabian Sea at Bankot Creek.
Hourly runoff series for the monsoon season from four stream gauges for a common period 2000-2010 is used
Figure 2: Location of Savitri river basin

## Slide 5: Methodology
Phase space reconstruction using hourly runoff from 2000 to 2009
Predicted hourly runoff during 2010 using local approximation
Identified complexity (dimension) by False Nearest Neighbour (FNN) approach
Prediction accuracy checked by:
Correlation coefficient (CC)
Nash –Sutcliffe efficiency (NSE)
Normalized root mean square error (NRMSE)

## Slide 6: Results
Kangule station
a)
b)
c)
Figure 3: a) Time series of hourly runoff at Kangule station, b) Phase reconstructed for hourly runoff series at Kangule station, c) FNNplot for hourly runoff series at Kangule station
Optimum embedding dimension =9

## Slide 7
Local approximation prediction accuracy
Figure 4: Local approximation prediction accuracy at Kangule station shown by a) CC, b) NSE, c) NRMSE
CC = Correlation coefficient, NSE = Nash-Sutcliffe efficiency, NRMSE = Normalized root mean square error
a)
b)
c)
Optimum number of neighbours = 4
m=9 & k=4
Figure 5: Scatter plot for predicted and observed hourly runoff at Kangule station

## Slide 8
Station | Optimum Embedding dimension | Optimum Number of neighbours | CC | NSE | NRMSE
Kangule | 9 | 4 | 0.996 | 0.992 | 0.011
Bhave | 13 | 3 | 0.980 | 0.961 | 0.014
Birwadi | 6 | 22 | 0.998 | 0.995 | 0.010
Kokkare | 9 | 23 | 0.996 | 0.993 | 0.011
CC = Correlation coefficient, NSE = Nash-Sutcliffe efficiency, NRMSE = Normalized root mean square error
Conclusions
Prediction accuracy achieved is comparable with more complicated techniques
One time step ahead prediction accuracy is good

## Slide 9: References
Dhanya, C.T., & Kumar, N. D., (2011), “Predictive uncertainty of chaotic daily streamflow using ensemble wavelet networks approach”, Water Resources Research, Vol. 47, W06507, doi:10.1029/2010WR010173.
Fathima, T.A., & Jothiprakash, V., (2014), “Behavioural analysis of a time series– A chaotic approach”, Sa¯dhana¯Vol. 39, Part 3, 659–676, Indian Academy of Sciences.
Farmer DJ, Sidorowich JJ (1987) Predicting chaotic time series. Phys Rev Lett 59:845–848
Gharde K. D., Kothari M. (2015) Application of ANN and Fuzzy Logic Algorithms for Streamflow Modelling of Savitri Catchment, Journal of Earth System Sciences 124, N0.5, pp. 933-943
Islam, M. N., & Sivakumar, B., (2002), “Characterization and prediction of runoff dynamics: a nonlinear dynamical view”, Advances in Water Resources,25, 179–190.
Kennel, M.,B., Brown, R., & Abarbanel, H., D., I., (1992), “ Determining embedding dimension for phase-space reconstruction using a geometrical construction”, PHYSICAL REVIEW A, VOLUME 45, NUMBER 6.
Sivakumar, B., (2003), “Forecasting monthly streamflow dynamics in the western United States: a nonlinear dynamical approach”,Environmental Modelling & Software,18 (2003) 721–728.
Sivakumar, B., (2017), “Chaos in hydrology: bridging determinism and stochasticity”, Springer, Dordrecht
Sivakumar, B., Berndtsson, R., & Persson, M., (2001), “Monthly runoff prediction using phase space reconstruction”, Hydrological Sciences Journal, 46:3, 377-387, DOI: 10.1080/02626660109492833.
Srivalli, Ch. N. S., Jothiprakash, V., & Sivakumar, B., “Complexity of streamflows in the west-flowing rivers of India”, Stochastic Environmental Research and Risk Assessment (2019) 33:837–853, https://doi.org/10.1007/s00477-019-01665-3.
Vignesh, R., Jothiprakash, V., & Sivakumar, B., (2015), “Streamflow variability and classification using false nearest neighbour method”, Journal of Hydrology ,531 706–715.

## Slide 10: Thank you

## Slide 11: Phase space reconstruction
Represents the state of a system
The coordinates represents variables of the system
Gives an idea about how that system evolves over time
The arrangement of points in the phase space result in attractor
A well-defined attractor is a representation of presence of chaos in the system
Figure : Phase space diagram for daily runoff (Source: Islam and Sivakumar 1999)

## Slide 12: SINGLE VARIATE PHASE SPACE RECONSTRUCTION
According to Takens’s embedding theorm for dimension 2
N=10, Assuming  =1, d=2 ,t =1
Zj= (Xj, Xj+, Xj+2, …, Xj+(d-1))
j → 1, 2, …, N-(d-1)/t
= 1,2,..9,10-(2-1)1
= 1,2,3…9
Zj= (Xj, Xj+1)
Z1 = (X1, X2)
Z2 = (X2, X3)
Z3 = (X3, X4)
Z4 = (X4, X5)
Z5 = (X5, X6)
Z6 = (X6, X7)
Z7 = (X7, X8)
Z8 = (X8, X9)
Z9 = (X9, X10)

## Slide 13: FNN METHOD
D1,2 = = Euclidian distance between Z1 & Z2 and so on
For d=2, τ=1
Z1 = (X1, X2)
Z2 = (X2, X3)
Z3 = (X3, X4)
Z4 = (X4, X5)
Z5 = (X5, X6)
Z6 = (X6, X7)
Z7 = (X7, X8)
Z8 = (X8, X9)
Z9 = (X9, X10)
For Z1
D1,2
D1,3
D1,4
D1,5
D1,6
D1,7
D1,8
D1,9
For Z2 to Z8
…
….
….
….
….
….
….
….
For Z9
D9,1
D9,2
D9,3
D9,4
D9,5
D9,6
D9,7
D9,8
Neighbours for d=2
Z1, Z4
Z2, Z6
Z3, Z5
Z4, Z8
Z5, Z9
Z6, Z2
Z7, Z1
Z8, Z7
Z9, Z3
The FNN algorithm for dimension d=2
Check distance and loneliness criteria (Kennel et al 1992)
If both criterions are satisfied, it is a false neighbour.
Count total number of false neighbours
False Neighbours for d=2
Z1, Z4
Z2, Z6
Z3, Z5
Z4, Z8
Z5, Z9
Z6, Z2
Z7, Z1
Z8, Z7
Z9, Z3
FNN plots of time series under behavioural study. (Source:Fathima & Jothiprakash 2014)