## Slide 1: A depth averaged Material Point Method for the simulation of snow slab avalanche Release
Louis Guillet1, Bertil Trottet1, Lars Blatny1, Denis Steffen1, Johan Gaume1,2
EGU 2022
1Snow and Avalanche Simulation Laboratory (SLAB), Swiss Federal Institute of Technology (EPFL), Lausanne, Switzerland
2WSL Institute for Snow and Avalanche Research SLF, CH-7260 Davos, Switzerland
Notes: Alternative title: New insights into the initiation and propagation of snow avalanches.

## Slide 2: Reminder of Bertil’s presentation
Anti crack to supershear transition within few meters
No bending in the slab and no collapse during supercritical regime
+ 3D simulations have heavy numerical cost
Motivation for a depth-averaged model
Anti-crack
Super-shear

## Slide 3: Depth-Averaged MPM
Shallow water hypothesis + plane stress
Columns instead of particles (Abe and Konagi, 2016)
Elastic-purely brittle weak layer seen as an external force
Shear
Displacement
Cohesion
1
Shear cohesive force
Weak Layer dammaged : Residual friction
Weak Layer Modelling
Depth-averaged equations

## Slide 4: DAMPM PST Simulation with
Down-slope
Up-slope
Purely elastic slab
Elastic-purely brittle WL
Critical length
Numerical « sawing »
Crack propagation
: cohesive weak layer
: dammaged weak layer
Parameters :
Crack propagation in super shear mode

## Slide 5: Comparision with 3D model and analytical solutions
Position x
Crack velocity
Convergence to same results as with the 3D MPM (Trottet et al. 2022)
Critical length comparison
Quantitative validation for PST simulations

## Slide 6: Large scale simualtion with elastic slab 50 x 50 m
Up-slope
Down-slope
Crack velocity
Position
: Up-slope crack velocity
: Cross-slope crack velocity
Crack propagation on different directions
Same results as in 3D Simulations (Trottet et al. 2022)

## Slide 7: Large scale simulation
Qualitative comparison with real avalanches
Foto : Jürg Schweizer, Isabelle Sabater, montagnes-magazine.com
Plastic model for the slab : Cohesive Modified Cam Clay
Good qualitative comparison on the avalanche shape !

## Slide 8: Simulation on more complexe terrain
Up slope
down slope
Up slope
down slope
Crack initiation

## Slide 9: Simulation on more complexe terrain
Up slope
down slope
Up slope
down slope
Fast computation of release zone on more complex terrain

## Slide 10: Conclusion
Fast model for avalanche release simulation
Quantitative validation with 3D simulations and analytical solutions
Qualitative comparison with large scale and complex terrain simulations
Need to match the depth-averaged yield surface to the 3D yield surface in order to mimic staunch wall
Quantitative comparison on complex cases
Discussion and future work

## Slide 11: References
K. Abe and K. Konagi. Numerical simulation for runout process of debris flow using depth-averaged material point method. Soils and Foundations, 56, 2016.
L. Benedetti, J. Gaume, and J.-T. Fischer. A mechanically-based model of snow slab and weaklayer fracture in the propagation saw test. International Journal of Solids and Structures,158:1–20, 2019. ISSN 0020-7683. doi: https://doi.org/10.1016/j.ijsolstr.2017.12.033. URL https://www.sciencedirect.com/science/article/pii/S0020768317305358.
M. Christen, P. Bartelt, J. Kowalski, and L. Stoffel. Calculation of dense snow avalanches in three-dimensional terrain with the numerical simulation program RAMMS. 04 2010.
E. A. de Souza Neto, D. Peric, and D. R. J. Owen. Computational Methods for Plasticity. Springer, 2008. ISBN 978-1-4020-6577-4. A. de Vaucorbeil, V. P. Nguyen, S. Sinaie, and J. Y. Wu. Chapter two - material point method after 25 years: Theory, implementation, and applications. volume 53 of Advances in Applied Mechanics, pages 185–398. Elsevier, 2020.
J. Gaume, G. Chambon, N. Eckert, and M. Naaim. Influence of weak-layer heterogeneity on snow slab avalanche release: application to the evaluation of avalanche release depths. Journal of Glaciology, 59(215):423–437, 2013. doi: 10.3189/2013JoG12J161.
J. Gaume, T. Gast, J. Terran, A. Van Herwinjen, and C. Jiang. Dynamic anticrack propagation in snow. Nature Communication, 9(3047), 2018.
C. Jiang, C. Schroeder, J. Teran, A. Stomakhin, and A. Selle. The material point method for simulating continuum materials. In ACM SIGGRAPH 2016 Courses, SIGGRAPH ’16, New York, NY, USA, 2016. Association for Computing Machinery.
Z. Kazmi and K. Konagai. Field mesurment and numerical simulation of debris flows from dolomites slopes destabilized during the 2005 kashmie eartquake, pakistan. Journal of earth-quake Engineering, 18:364–388, 2014.
A. Puzrin. Constitutive Modelling in Geomechanics. International series of monographs on physics. Springer, 2012. ISBN 978-3-642-27395-7.
G. Richard. Depth-averaged equations for compressible shallow-water flows and tsunami. preprint at https://hal.inrae.fr/hal-02959509, 2020.
A. Stomakhin, C. Schroeder, L. Chai, J. Teran, and A. Selle. A material point method for snow simulation. ACM Trans. Graph., 32(4), July 2013. ISSN 0730-0301. doi: 10.1145/2461912. 2461948. URL https://doi.org/10.1145/2461912.2461948.
B. Trottet, R. Simenhois, G. Bobillier, A. van Herwijnen, C. Jiang, and J. Gaume. From sub-rayleigh to intersonic crack propagation in snow slab avalanche release. In EGU General Assembly 2021, online, 19–30 Apr 2021, EGU21-8253, 2021.
W. Wu and M. Pastor. Point based numerical methods in geomechanics. ALERT Doctoral School, 56:127, 2020.
X. Zhang, Z. Chen, and Y. Liu. The Material Point Method, A Continuum-Based Particle Mathod for Extreme Loading Cases. Academic Press, 2017. ISBN 987-0-12-407716-4.

## Slide 12
PST Simulation plastic slab Cohesive Modified Cam Clay
Parameters
Down slope
Up slope
Grpah crack length comparison
Tensile length
Higher tensile length
Good match with the analytical tensile length

## Slide 13: Depth-Averaged MPM
Tapez une équation ici.
Shallow water hypothesis + plane stress
Columns instead of particles (Abe and Konagi, 2016)
Elastic-purely brittle weak layer seen as an external force
Shear
Displacement
Cohesion
1
Shear cohesive force
Weak Layer dammaged : Residual friction
Weak Layer Modelling
Depth-averaged equations

## Slide 14
DAMPM: A depth-averaged MPM
weak layer failure
slab failure
intact
shear failure
intact
tensile failure
© Guillet et al. (SLAB)

## Slide 15
DAMPM: A depth-averaged MPM
model
reality